## Slide 1: GAS procedure in TGai
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jaehyung Song | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7898 | jaehyung.song@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Date: 2012-03-03
Authors:

## Slide 2: Abstract
This document proposes optimized GAS/ANQP procedure by eliminating unnecessary GAS/ANQP query.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: Background
The contribution 12/0053, which was presented in January meeting, proposed GAS/ANQP configuration change counter inclusion in Beacon/Probe Response, but an AP should update GAS/ANQP information via periodic or event driven backbone communication with the server
GAS/ANQP information is rarely changed, so periodic transmission of GAS/ANQP configuration change counter in Beacon increases unnecessary air resource overhead

## Slide 5: Proposal’s summary
STA caches GAS/ANQP configuration change counter.
When the STA associates to the AP, STA transmits the association request message with GAS/ANQP configuration change counter to the preferred AP.
After receiving GAS/ANQP configuration change counter, the AP can indicate whether GAS/ANQP query information of the STA has been changed. If the configuration change counter mismatches between STA and AP, the STA should update GAS/ANQP query information included in the association response message. Otherwise (i.e., GAS configuration change counter is matched), the STA skips the GAS/ANQP procedure.

## Slide 6: Example of proposal (i.e., GAS procedure skip)
STA caches GAS/ANQP configuration change counter.
When the STA associates to the AP, STA transmits the association request message with GAS/ANQP configuration change counter to the AP.
(Configuration Change Counter is matched)  AP sends the association response message with status code ‘SUCCESS’ to the STA and then, STA skips the GAS/ANQP procedure.
(Configuration Change Counter is mismatched)  AP defers the association and sends the association response message with updated GAS/ANQP information IE.

## Slide 7: Proposed IE
Configuration change counter IE is included in association request message:
GAS/ANQP information IE can be included in association response message:

## Slide 8: Conclusion
Text for the specification framework document was proposed in contribution 11-12-0254-00-00ai.