## Slide 1: Prioritized Active Scanning in TGai
Name | Affiliations | Address | Phone | email
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Date: 2012-05-04
Authors:

## Slide 2: Abstract
This document proposes enhancement of active scanning by reducing the Probe Response transmission of AP.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Background (1/2)
Three kinds of active scanning are defined in the current IEEE802.11 standard
  Broadcasted Probe Request
    Containing Wildcard SSID, Wildcard BSSID in Probe Request
    All APs received Probe Request should respond with Probe Response
  Unicasted Probe Request
    Containing SSID, BSSID in Probe Request
    AP which has the same SSID/BSSID in Probe Request should respond with Probe Response
  Multicasted Probe Request
    Containing SSID List, Wildcard BSSID in Probe Request
    APs of which SSID is one of the SSID List in Probe Request should respond with Probe Response
Each method has the following Cons.
  Broadcasted Probe Request
    Probe Response Flooding: Too many Probe Responses may be sent
  Unicasted/Multicasted Probe Request
    If there is no APs with desired SSID(s) around STA, delay of active scanning can be increased
Therefore, the mechanism to discover the AP with desired SSID needs to be defined without increasing delay of active scanning and Probe Response flooding

## Slide 5: Background (2/2)
Active Scanning Procedure
  Wait until the ProbeDelay time has expired or a PHYRxStart.indication primitive has been received.
  Perform the Basic Access procedure.
  Send a probe request to the broadcast destination address, with the SSID and BSSID from the MLME-SCAN.request primitive. When the SSID List is present in the MLME-SCAN.request primitive, send one or more probe request frames, each with an SSID indicated in the SSID List and the BSSID from the MLME-SCAN.request primitive.
  Set to 0 and start a ProbeTimer.
  If PHY-CCA.indication (busy) primitive has not been detected before the ProbeTimer reaches MinChannelTime, then set NAV to 0 and scan the next channel, else when ProbeTimer reaches MaxChannelTime, process all received probe responses.
  Set NAV to 0 and scan the next channel.
According to the current active scanning procedure, scanning STA has to monitor the channel for at least MinChannelTime. If any signal is detected in the channel, STA has to monitor the channel till MaxChannelTime has expired.

## Slide 6: Proposal
For active scanning, two steps of procedure after sending Probe Request (including desired SSID(s) & indication of two step scanning enabled) can be defined
  STA Perspective
    First Step
      STA monitors the channel to receive Probe Response from AP(s) with desired SSID(s) during the specific time interval (e.g., FirstMinChannelTime)
      If STA receives Probe Response from the AP(s) with desired SSID, STA may perform the following up procedure such as authentication and association with the AP before MaxChannelTIme has been reached
    Second Step
      If STA has not received Probe Response from AP(s) with desired SSID(s) within the specific time interval (e.g., FirstMinChannelTime), it monitors the channel to receive Probe Response for non-desired SSID (i.e., wildcard SSID) from all APs near by the STA during the specific time interval (e.g., SecondMinChannelTime)
      If STA has not received any Probe Response within the certain time interval (e.g., FirstMinChannelTime + SecondMinChannelTime), STA scans the next channel. Otherwise, STA monitors the channel until the ProbeTimer reaches MaxChannelTime, and processes received Probe Responses

## Slide 7: Proposal (Continued)
For active scanning, two steps of procedure after sending Probe Request (including desired SSID(s) & indication of two step scanning enabled) can be defined
  AP Perspective
    If AP with desired SSID of STA receives the above Probe Request, it responds with Probe Response within the specific time interval (e.g., FirstMinChannelTIme)
    If AP without desired SSID of STA receives the above Probe Request, it waits for the specific time interval (e.g., FirstMinChannelTIme) and send Probe Response.
    If AP without desired SSID of STA hears Probe Response sent by the AP with the desired SSID of the STA, it may cancel its transmission of pending Probe Response.

## Slide 8: Proposal (Continued)
Example
  If AP without desired SSID of STA receives the above Probe Request, it waits for the specific time duration (e.g., FirstMinChannelTIme) and sends Probe Response.
Figure1 . Probe response

## Slide 9: Comparison between the existing procedure and the proposed method
Operational assumption for the existing procedure
  Single channel operation
    STA sends the Probe Request including desired SSID(s).
    When the STA has not received Probe Response from AP(s) with desired SSID(s) within the specific time interval (i.e., MinChannelTime), STA sends the Probe Request including Wildcard SSID again after MinChannelTime.
  Multichannel operation
    STA sends the Probe Request with desired SSIDs list.
    If the STA has not received Probe Response from AP(s) with desired SSID(s) within the specific time interval (i.e., MinChannelTime), STA scans the next channel(s). If the STA has scanned all channels and has not received any Probe Response from AP(s) with desired SSID(s), STA sends the Probe Request with Wildcard SSID again.
  That is, in case STA has not received Probe Response from AP(s) with the desired SSID after sending the Probe Request with the specific SSID(s), STA may send the Probe Request with Wildcard SSID again.

## Slide 10: Comparison between existing procedure and the proposed method
Operational assumption for the proposed method
  Single channel operation
    STA sends the Probe Request with desired SSID(s) and the parameter of the specific time interval (i.e., FirstMinChannelTime).
    If the STA has not received Probe Response from AP(s) with desired SSID(s) within the specific time interval (i.e., FirstMinChannelTime), STA monitors the Probe Response sent from the AP with non-desired SSID for the second specific time interval (i.e., SecondMinChannelTime).
  Multichannel operation
    STA sends the Probe Request with desired SSID(s) and the parameter of the specific time interval (i.e., FirstMinChannelTime).
    When the STA has not received Probe Response from AP(s) with desired SSID(s) within the specific time interval (i.e., FirstMinChannelTime), STA monitors the Probe Response sent from the AP with non-desired SSID for the second specific time interval (i.e., SecondMinChannelTime). If the STA has not received any Probe Response within the certain time interval (i.e., FirstMinChannelTime + SecondMinChannelTime), STA scans the next channel(s).
  In proposal, STA just monitors the channel to receive the Probe Response from AP(s) with desired SSID during the FirstMinChannelTime and from AP(s) with non-desired SSID during the SecondMinChannelTime after sending a Probe Request

## Slide 11: Comparison between the existing procedure and the proposal
 | Existing procedure | Proposal
Case 1) There are only AP with desired SSID near by the STA. | Single Probe Request transmission is enough. No additional delay is required. | Proposal is equivalent to the existing procedure in the latency & the overhead for active scanning.
Case 2) There are only AP (s) for non-desired SSID near by the STA. | Two Probe Request transmissions are required for the channel scanning. Delay of active scanning is also increased (i.e., ProbeDelay for second Probe Request transmission). | Single Probe Request transmission is enough. Proposal provides less latency & overhead than the existing procedure.
Case 3) There is no AP near by the STA. | Two Probe Request transmissions are required for the channel scanning. Delay of active scanning is also increased (i.e., ProbeDelay for second Probe Request transmission). | Single Probe Request transmission is enough. Proposal provides less latency & overhead than the existing procedure
Case 4) There are AP(s) with desired SSID and AP for non-desired SSID near by the STA. | Single Probe Request transmission is enough. No additional delay is required. | In the latency perspective, proposal is equivalent to the existing procedure. If cancellation of pending probe response transmission from AP(s) with non-desired SSID is supported, proposal is also equivalent to the existing procedure in the overhead.

## Slide 12: Conclusion
Proposed step wise active scanning allows STA to discover the AP with desired SSID without increasing delay of active scanning and Probe Response flooding.

## Slide 13: Motion 1
Move to add the following text to the end of the clause 6 of the specification framework document:
802.11ai shall support the prioritized active scanning to reduce the latency of active scanning as well as the overhead of Probe Response.
Moved :
Seconded:
Yes: No: Abstain:

## Slide 14: Motion 2
Move to add the following text to the end of the clause 6 of the specification framework document:
Prioritized active scanning allows the STA to select the AP with desired SSID with higher priority over the AP with non-desired SSID.
Moved :
Seconded:
Yes: No: Abstain:

## Slide 15: Motion 3
Move to add the following text to the end of the clause 6 of the specification framework document:
After receiving a Probe Request, the AP with non-desired SSID may delay its transmission of Probe Response by the certain time interval as indicated in the received Probe Request.
Moved :
Seconded:
Yes: No: Abstain: