## Slide 1: Step-wise Active Scanning in TGai
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jaehyung Song | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7898 | jaehyung.song@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Date: 2012-03-03
Authors:

## Slide 2: Abstract
This document proposes enhancement of active scanning by reducing the probe response transmission of AP.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Background (1/2)
Three kinds of active scanning are defined in the current IEEE802.11 standard
  Broadcasted Probe Request
    Containing Wildcard SSID, Wildcard BSSID in Probe Request
    All APs received Probe Request should respond with Probe Response
  Unicasted Probe Request
    Containing SSID, BSSID in Probe Request
    AP which has the same SSID/BSSID in Probe Request should respond with Probe Response
  Multicasted Probe Request
    Containing SSID List, Wildcard BSSID in Probe Request
    APs of which SSID is one of the SSID List in Probe Request should respond with Probe Response
Each method has the following Cons.
  Broadcasted Probe Request
    Probe Response Flooding: Too many Probe Responses may be sent
  Unicasted/Multicasted Probe Request
    If there is no APs with desired SSID(s) around STA, delay of active scanning can be increased
Therefore, the mechanism to discover the AP with desired SSID needs to be defined without increasing delay of active scanning and Probe Response flooding

## Slide 5: Background (2/2)
Active Scanning Procedure
  Wait until the ProbeDelay time has expired or a PHYRxStart.indication primitive has been received.
  Perform the Basic Access procedure.
  Send a probe request to the broadcast destination address, with the SSID and BSSID from the MLME-SCAN.request primitive. When the SSID List is present in the MLME-SCAN.request primitive, send one or more probe request frames, each with an SSID indicated in the SSID List and the BSSID from the MLME-SCAN.request primitive.
  Set to 0 and start a ProbeTimer.
  If PHY-CCA.indication (busy) primitive has not been detected before the ProbeTimer reaches MinChannelTime, then set NAV to 0 and scan the next channel, else when ProbeTimer reaches MaxChannelTime, process all received probe responses.
  Set NAV to 0 and scan the next channel.
According to the current active scanning procedure, scanning STA has to monitor the channel for at least MinChannelTime. If any signal is detected in the channel, STA has to monitor the channel till MaxChannelTime has expired.

## Slide 6: Proposal
For active scanning, two steps of procedure after sending Probe Request (including desired SSID(s) & indication of two step scanning enabled) can be defined
  STA Perspective
    First Step
      STA monitors the channel to receive Probe Response from AP(s) with desired SSID(s) for the specific time duration (e.g., FirstMinChannelTime)
      If STA receives Probe Response from the AP(s) with desired SSID, STA may perform the following up procedure such as authentication and association with the AP before MaxChannelTIme has been reached
    Second Step
      If STA has not received Probe Response from AP(s) with desired SSID(s) for the specific time duration(e.g., FirstMinChannelTime), it monitors the channel to receive Probe Response for non-desired SSID (i.e., wildcard SSID) from all APs near by the STA for the specific time duration (e.g., SecondMinChannelTime)
      If STA has not receive any Probe Response for the certain time duration (e.g., FirstMinChannelTime + SecondMinChannelTime), STA scans the next channel. Otherwise, STA monitors the channel to process for the MaxChannelTime and process received Probe Responses

## Slide 7: Proposal (Continued)
For active scanning, two steps of procedure after sending Probe Request (including desired SSID(s) & indication of two step scanning enabled) can be defined
  AP Perspective
    If AP with desired SSID of STA receives the above Probe Request, it responds with Probe Response within the specific time duration (e.g., FirstMinChannelTIme)
    If AP without desired SSID of STA receives the above Probe Request, it wait for the specific time duration (e.g., FirstMinChannelTIme) and send Probe Response before MaxChannelTime has been reached.
    If AP without desired SSID of STA hears Probe Response from AP with desired SSID of STA, it may cancel its transmission of pending Probe Response.

## Slide 8: Proposal (Continued)
Example
  If AP without desired SSID of STA receives the above Probe Request, it wait for the specific time duration (e.g., FirstMinChannelTIme) and send Probe Response before MaxChannelTime has been reached.
Figure1 . Probe response

## Slide 9: Conclusion
Proposed step wise active scanning allows STA to discover the AP with desired SSID without increasing delay of active scanning and Probe Response flooding.
Text for the specification framework document was proposed in contribution 11-12-0256-00-00ai.