## Slide 1: Reducing Probe Responses for faster AP discovery
Authors:
March 2012
Name | Affiliations | Address | Phone | email
Jaehyung Song | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7898 | jaehyung.song@lge.com
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | Kiseon.ryu@lge.com

## Slide 2: Abstract
The submission proposes a general framework to improve the AP discovery for fast initial link set up.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4: Motivation
A number of proposals suggests methods to reduce the number of probe responses
  Most of the proposals focus on filtering mechanisms based on the network identity that the AP of interest belongs to
  While conflicting methods require a careful examination by the TG, most of the methods can be integrated in a structure manner
  However, there are possibly more filtering items that need to be included, considering user’s preference
  Two other filtering mechanisms are introduced in this perspective

## Slide 5: Probe Response Filtering
Proposals until today
  Filtering criteria proposed until today can be categorized as following:
  These filtering items can be coordinated so that they can be applied in a selective manner

## Slide 6: But, something is missing
A user applies his/her preference in AP selection, not only the identity of AP or Network
  Such as the cost of the network usage and the strength of the signal
Thus, we need another category to incorporate this user behavior

## Slide 7: Considering the user (or station) behavior
Considering the user (or station) behavior, an additional filtering item to filter out unnecessary probe responses is proposed:
  A charging information – A user can select APs, which provide free-of-charge network access, to respond to the probe request.
    Charging preference IE is included in probe request, when the STA discovers desired AP.
  Another filtering item is proposed: RSSI based filtering – A STA can select APs, which provide a signal strength above the threshold that STA specifies, to respond to the probe request.
    Signal strength (e.g., RSSI) threshold can be included in probe request, when the STA discovers desired AP.

## Slide 8: Conclusion
  Various proposals for filtering of probe response can be integrated in a structure manner.
Additional filtering item can be used to filter out unnecessary probe responses.
  Charging preference information
  Signal strength of STA

## Slide 9: Motion
Move to add the following text to the clause 5 of the specification framework document:
The 802.11ai shall support for a method to avoid transmission of undesired probe response frames, in a selective manner.
Moved : Kiseon Ryu
Seconded: Lee Armstrong
Yes: 17 No: 6 Abstain: 15
Motion failed