## Slide 1: Spec Framework Proposal: Selection of the AP for Scanning
Date: 2012-03-02
March 2012

## Slide 2: Abstract
Scanning time is one of the major cause of the delay in initial Link Setup
In active scanning, a STA transmits Probe Request frame in Broadcast, usually using wildcard SSID to find APs
It can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
This proposal reduces the overhead of active scanning by providing precise selection mechanism of the AP s to respond with Probe Response
Approach:
  Add Exclusion List to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response
    Substring of the SSIDs or Mesh IDs can be used in the List to indicate the APs or STAs to be excluded
March 2012
Jae Seung Lee, ETRI

## Slide 3: Background
This contribution is based on the following documents that have been presented at the last January 2012 IEEE 802.11 meeting
  11-12/0059r1 Selection of the AP for Scanning
  11-12/0060r0 Text for Selection of the AP for Scanning
This contribution proposes text for TGai Specification Framework Document regarding scanning enhancement for fast network discovery
Proposed Spec Framework text is included in the Straw Poll/Motion section at the end of this contribution
Jae Seung Lee, ETRI
March 2012

## Slide 4: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
March 2012
Jae Seung Lee, ETRI

## Slide 5: Selection of the AP to Scan – Background (1/3)
To discover the AP to associate, a STA transmits Probe Request in Broadcast with wildcard SSID
APs transmit Probe Response  too many probe responses
AP 1
AP 2
AP 3
AP 4
AP n
STA
Probe Request on channel x (broadcast)
Probe Response
flooding
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
March 2012
Jae Seung Lee, ETRI

## Slide 6: Selection of the AP to Scan – Background (2/3)
In many cases, STA has prior knowledge on which APs it does not want to receive Probe Response from
  It is not necessary for a STA to receive Probe Response from APs deployed by specific Service Providers if the user does not subscribe to the Service Providers
    Usually, specific substring is included in the SSID of such APs deployed by a specific Service Provider
    There are many users who do not have any WiFi Subscription for paid WiFi services provided by Service Providers
March 2012
Jae Seung Lee, ETRI

## Slide 7: Selection of the AP to Scan – Background (3/3)
  Usually, it is not necessary for a STA to receive Probe Response from the APs whose SSID include “_nomap”
    Google has announced a way for WiFi router owners to stop Google from including them in the company’s location database – by adding “_nomap” at the end of the SSID
    It is highly probable that AP whose SSID contains substring “_nomap” is not a public AP
 It will be beneficial if we can exclude such APs with specific known substrings from responding Probe Request
Slide 7
March 2012
Jae Seung Lee, ETRI

## Slide 8: Selection of the AP to Scan - Approach
Exclusion List is added to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response frame
Substring can be used in the List to indicate SSIDs or Mesh IDs
  helps to reduce the size of the Exclusion List
  Not necessary to include individual IDs in the Exclusion List
  Efficiently filter the APs with IDs with known substring
Exclusion List with substring capability can provide precise
selection of the AP to transmit Probe Response frame
March 2012
Jae Seung Lee, ETRI

## Slide 9: Selection of the AP to Scan – Example (1/3)
Example 1-1: Using existing active scanning method
. The user does not know the SSID. He does not have any WiFi subscription,
so he does not want to get response from APs deployed by Service Providers such as KT or SKT
SKT0002
SKT0003
Xx_nomap
Aa_nomap
SKT0006
KT0002
KT0003
KT0004
KT0005
Bb_nomap
KT0003
KT0004
KT0005
SKT_xy
SKT_zz
Hyatt_1
VeriLAN
Hyatt_2
Hyatt_2
STA
Probe Request
(wildcard SSID)
Too many Probe Response frames !!
(Probe Responses from many APs are not helpful
for association)
.
.
.
March 2012
Home_nomap
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
Private AP
Private AP
Private AP
Private AP
Jae Seung Lee, ETRI

## Slide 10: Selection of the AP to Scan – Example (2/3)
Example 1-2: Selection of the AP to respond using Exclusion List with substring
. The user does not know the SSID. He does not have any WiFi subscription,
so he does not want to get response from APs deployed by Service Providers such as KT or SKT
include Exclusion list containing substring KT and _nomap into the Probe Request
 Do not need to list all the SSIDs to be filtered. Do not need to know full SSID to be filtered
KT0002
KT0003
KT0004
KT0005
Bb_nomap
KT0003
KT0004
KT0005
SKT_xy
SKT_zz
Hyatt_1
VeriLAN
Hyatt_2
Hyatt_2
STA
Probe Request
(Exclusion List with SSID substring)
Reduced Probe Responses
x
x
x
x
x
x
x
x
x
x
SKT0002
SKT0003
Aa_nomap
SKT0006
Home_nomap
x
x
x
x
x
x
March 2012
Xx_nomap
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
Private AP
Private AP
Private AP
Private AP
Jae Seung Lee, ETRI

## Slide 11: Selection of the AP to Scan – Example (3/3)
Example 2: Exclusion List with substring – using substring type information
The user does not subscribe to KT but SKT
SKT0002
SKT0003
SKT0004
SKT0005
SKT0006
SKT0001
KT0002
KT0003
KT0004
KT0005
KT0003
KT0004
KT0005
VeriLAN
Hyatt_2
Hyatt_2
STA
SKT000x
SKT000z
SKT000y
Probe Request
(ExclusionList with substring)
Add substring KT and indicate
“starts with” in the substring type information
(SKT is not filtered in this example)
x
x
x
x
x
x
x
March 2012
No subscription
No subscription
No subscription
No subscription
No subscription
No subscription
Aa_nomap
Home_nomap
x
Private AP
Private AP
x
Jae Seung Lee, ETRI

## Slide 12: Exclusion List with substring capability
Added to the Probe Request frames to precisely limit the scope of STAs to respond
Specifies the set of STAs that should not transmit a response to a Probe Request frame
  If APs are selected by BSSID, SSID, SSID List, HESSID, or Mesh ID and if some of the selected APs are indicated by the lists in the Exclusion List, then they should not transmit a response to the Probe Request frame
  Substring can be used in the Exclusion List to indicate SSIDs or Mesh IDs
March 2012
Jae Seung Lee, ETRI

## Slide 13: Exclusion List element
May Include SSID List element, BSSID List element, MESHID List element, and HESSID List element
Optionally included in the Probe Request frame
Substrings can be used in SSID elements or MESHID elements
  - Interpretation of the strings are indicated in the SubstringInfo field
Octets: 1 1 1 variable
Element ID | Length | SubstringInfo | SSID List | BSSID List | MESHID List | HESSID List
March 2012
Jae Seung Lee, ETRI

## Slide 14: SubstringInfo field format
Included in Exclusion List element
Make it possible to indicate SSID or Mesh ID by their substrings
Several substring type can be indicated (starts with, ends with,…)
SubstringInfo field indicates whether the the strings contained in the SSID or Mesh ID elements included in the Exclusion List are substrings of the actual SSID or Mesh ID that indicates the STAs that should not respond with the Probe Request frame.
The Substring Supported subfield:
  Set to 1 if the STA supports the indication of substring of SSID or Mesh ID
  Set to 0 if the STA does not support the indication of substring and if it is set to 0, the value of Substring Type is reserved.
Substring Supported | Substring Type | Reserved
bits: 1 3 4
March 2012
Jae Seung Lee, ETRI

## Slide 15: Substring Type subfield
The Substring Type field indicates the type of substring used in the SSID or Mesh ID elements.
Value | Meaning
0 | Strings used in the SSID or Mesh ID elements in the Exclusion List are the actual SSIDs or Mesh IDs (not substring)
1 | The actual SSIDs or Mesh IDs of the intended STAs are the SSIDs or Mesh IDs that start with, or end with, or contain the substrings specified in the SSID or Mesh ID elements in the Exclusion List.
2 | The actual SSIDs or Mesh IDs of the intended STAs are the SSIDs or Mesh IDs that start with the substrings specified in the SSID or Mesh ID elements in the Exclusion List.
3 | The actual SSIDs or Mesh IDs of the intended STAs are the SSIDs or Mesh IDs that end with the substrings specified in the SSID or Mesh ID elements in the Exclusion List.
4-7 | Reserved
March 2012
Jae Seung Lee, ETRI

## Slide 16: Conclusion
Scanning time is one of the major cause of the delay in initial Link Setup
Legacy active scanning can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
In this proposal:
  Exclusion List is added to the Probe Request frames to precisely limit the scope of APs or STAs that should transmit probe response frame
  Use of substring in the Exclusion List to indicate SSIDs or Mesh IDs
    helps to reduce the size of the Exclusion List
    Not necessary to include individual IDs in the Exclusion List
    Provides flexible substring matching
   helps to reduce the unnecessary exchange of Probe Request frame thus increasing the efficiency of the active scanning
March 2012
Jae Seung Lee, ETRI

## Slide 17
Straw Poll 1
Should the spec framework document be updated with the following text for Fast Network Discovery:
  STA may include Exclusion List in the Probe Request frame that indicates the APs or STAs that should not transmit probe responses.
Yes
No
Abstain

## Slide 18
Jae Seung Lee, ETRI
Slide 18
Straw Poll 2
Should the spec framework document be updated with the following text for Fast Network Discovery:
  Substrings of SSIDs or Mesh IDs can be used in the Exclusion List to indicate the APs or STAs that should not transmit probe responses.
Yes
No
Abstain

## Slide 19
References
11-12/0059r1 Selection of the AP for Scanning
11-12/0060r0 Text for Selection of the AP for Scanning