## Slide 1: Spec Framework Proposal: Probe Response frame transmission interval
Date: 2012-03-02
March 2012

## Slide 2: Abstract
Scanning time is one of the major cause of the delay in initial Link Setup
  In active scanning, STA sends a probe request to the broadcast destination address, and receives the Probe Response during MaxChannelTime
  But the responding STAs may send the response frame after the MaxChannelTime and it can cause Probe Response flooding
This proposal focuses on solving such problem of active scanning
Approach:
  Include ProbeResponse deadline interval in the Probe Request frame
  The responding STA shall not transmit or retransmit Probe Response frame to the transmitter after the time limit specified in the ProbeResponse deadline interval
Jae Seung Lee, ETRI
March 2012

## Slide 3: Background
This contribution is based on the following documents that have been presented at the last January 2012 IEEE 802.11 meeting
  11-12/0061r1 Probe Response frame transmission interval
  11-12/0062r1 Text for Probe Response frame transmission interval
This contribution proposes text for TGai Specification Framework Document regarding scanning enhancement for fast network discovery
Proposed Spec Framework text is included in the Straw Poll/Motion section at the end of this contribution
Jae Seung Lee, ETRI
March 2012

## Slide 4: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Jae Seung Lee, ETRI
March 2012

## Slide 5: Probe Response flooding – Problem (1/2)
STA sends a probe request to the broadcast destination address, and receives the Probe Response during MaxChannelTime
  If the MaxChannelTime has elapsed, then the STA scans the next channel, so the STA cannot receive the Probe Response in the previous channel after the MaxChannelTime
  The responding STAs may send the response frame after the MaxChannelTime, and since it cannot be received by the requesting STA and cannot be acknowledged, the STA keep sending the Probe response
It will cause Probe Response frame flooding and severely increase the network traffic and reduce the initial link setup time
Jae Seung Lee, ETRI
March 2012

## Slide 6: Probe Response flooding – Problem (2/2)
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
Probe Request on channel X
Probe Response
AP 1-4
AP 1-5
AP 1-6
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Retransmit Probe Response
MaxChannelTime
STA cannot receive
Probe Response
after MaxChannelTime
Unnecessary
Probe Response
Unnecessary
Retransmission
Probe Response
flooding
Retransmit Probe Response
Retransmit Probe Response
Retransmit Probe Response
Retransmit Probe Response
Retransmit Probe Response
Jae Seung Lee, ETRI
March 2012

## Slide 7: Timeout Interval in Probe Request
Solution to the Flooding Problem:
ProbeResponse deadline interval determined by the transmitter of the Probe Request is included in the Probe Request frame
  The Responding STA shall not transmit or retransmit Probe Response frame to the transmitter after the time limit specified in the ProbeResponse deadline interval, since the transmitter does not listen to the Probe Response frame any more after the deadline interval
Jae Seung Lee, ETRI
March 2012

## Slide 8: ProbeResponse deadline interval (1/2)
Use existing Timeout Interval element (TIE)
  The TIE specifies time intervals and timeouts in current 802.11 Specification
  The Timeout Interval Value field contains an unsigned 32-bit integer
Define one additional Type for ProbeResponse deadline interval
Timeout Interval Type | Meaning | Units
0 | Reserved | 
1 | Reassociation deadline interval | Time units (TUs)
2 | Key lifetime interval | Seconds
3 | Association Comeback time | Time units (TUs)
4 | Time-to-Start | Time units (TUs)
5 | ProbeResponse deadline interval | Time units (TUs)
6-255 | Reserved | 
Jae Seung Lee, ETRI
Element ID | Length | Timeout Interval Type | Timeout Interval Value
Octets: 1 1 1 4
March 2012

## Slide 9: ProbeResponse deadline interval (2/2)
  Listening duration of the Probe Response determined by the transmitter of the Probe Request considering its MinChannelTime and MaxChannelTime value
    The transmitter receives Probe Response during the interval
  The responder shall check the ProbeResponse deadline interval in the Probe Request frame
  The responder of the Probe Request frame shall not transmit or retransmit the Probe Response frame if the time specified in the ProbeResponse deadline interval has been elapsed since it has received the Probe Request frame
Jae Seung Lee, ETRI
March 2012

## Slide 10: Timeout Interval in Probe Request
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
Probe Request on channel X
Probe Response
AP 1-4
AP 1-5
AP 1-6
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response
Probe Response frame is not
Transmitted after
Timeout interval (reflecting MaxchannelTime of the
Requesting AP)
has elapsed
MaxChannelTime
Transmit
Probe
Response
No flooding !!
Jae Seung Lee, ETRI
ProbeResponse
Timeout Interval
March 2012

## Slide 11: Conclusion
Slide 11
Probe Response after the MaxChannelTime can cause Probe Response flooding
In this proposal:
  ProbeResponse deadline interval which is the listening duration of the Probe Response is included in the Probe Request frame
  The responding STA does not transmit or retransmit Probe Response frame to the transmitter after the ProbeResponse deadline interval
  Used existing Timeout Interval element – No need to define new IE
  No additional frame is sent by the requesting STA to stop the responder to keep transmitting the Probe Response frame
Jae Seung Lee, ETRI
March 2012

## Slide 12: Straw Poll 1
Should the spec framework document be updated with the following text for Fast Network Discovery:
  ProbeResponse deadline interval which is the listening duration of the Probe Response shall be included in the Probe Request frame
  The Responding STA shall not transmit or retransmit Probe Response frame to the transmitter after the time limit specified in the ProbeResponse deadline interval
Yes
No
Abstain
Jae Seung Lee, ETRI
March 2012

## Slide 13: Straw Poll 2
Slide 13
Should the spec framework document be updated with the following text for Fast Network Discovery:
  ProbeResponse deadline interval shall be defined as a TIE (Timeout Interval Element)
Yes
No
Abstain
Jae Seung Lee, ETRI
March 2012

## Slide 14
References
11-12/0061r1 Probe Response frame transmission interval
11-12/0062r1 Text for Probe Response frame transmission interval
Jae Seung Lee, ETRI
March 2012