## Slide 1: Spec Framework Proposal: Selective transmission of the Probe Response
Date: 2012-03-02

## Slide 2: Abstract
In active scanning, Probe Response can cause unnecessary packet exchange which increases the network traffic and causes link setup delay
We propose the selective transmission of the Probe Response frame to reduce the unnecessary Probe Response frame
Approach:
  Filter the Probe Request by the responding AP based on Preferences and/or Capabilities of the STA that has sent the Probe Request frame
    can reduce the traffic caused by Probe Response frames
    helps the selection of appropriate STAs to be associated
Jae Seung Lee, ETRI

## Slide 3: Background
This contribution is based on the following documents that have been presented at the last January 2012 IEEE 802.11 meeting
  11-12/0063r1 Selective transmission of the Probe Response
  11-12/0064r0 Text for Selective transmission of the Probe Response
This contribution proposes text for TGai Specification Framework Document regarding scanning enhancement for fast network discovery
Proposed Spec Framework text is included in the Straw Poll/Motion section at the end of this contribution
Jae Seung Lee, ETRI
March 2012

## Slide 4: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Jae Seung Lee, ETRI

## Slide 5: Selective Probe Response - Background
To discover an AP to associate, a STA transmits Probe Request in Broadcast with wildcard SSID
It can cause too many probe responses: Need to reduce the unnecessary Probe responses
APs respond to the Probe Request even if the requesting STA cannot or will not associate with the APs
  Due to the lack of the capability of the STA, or
  The STA wants or does not want to use certain features
  AP cannot accept the STA for association because of its operating condition
   Sending Probe Response to such STAs is not necessary
Jae Seung Lee, ETRI

## Slide 6: Active Scanning - Problem
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
AP 3-1
AP 3-2
AP 3-3
AP 3-…
AP 3-n
AP 5-1
AP 5-2
AP 5-3
AP 5-…
AP 5-n
Probe Request on channel 1 (broadcast, wildcard SSID)
Channel 1
Channel 2
(idle)
Probe Request on channel 3 (broadcast, wildcard SSID)
Probe Request on channel 5 (broadcast, wildcard SSID)
Probe Request on channel 2 (broadcast, wildcard SSID)
Probe Request on channel 4 (broadcast, wildcard SSID)
Probe Request on channel n (broadcast, wildcard SSID)
Channel 3
Channel 5
Channel 4
(idle)
Channel n
Probe Response
.
.
.
Probe Response
.
.
.
Probe Response
.
.
.
Sequential
Scanning
of all
Channels
Jae Seung Lee, ETRI
APs respond to the Probe Request
although the STA cannot associate with
some of the APs

## Slide 7: Selective Transmission – Approach (1/2)
Filtering Information including preferences and/or capabilities of the STA is included in the Probe Request frame
The Responding APs or STAs can check the preferences and/or capabilities of the STA that transmitted the Probe Request
  Capability information such as security capability including RSN capability is included in the Probe Request frame
  Preference information such as request for security processing, or request for no security processing or request for association with HT, VHT, or non-HT STA is included in the Probe Request frame
Jae Seung Lee, ETRI

## Slide 8: Selective Transmission – Approach (2/2)
  If the preferences of the STA is not acceptable by the
  responding APs or STAs, or
  (2) If the capabilities of the STAs that transmit the Probe Request frame is not acceptable by the APs or STAs that
  receive the Probe Request frame, or
  (3) The responding APs or STAs cannot accept the STA because of its current condition (e.g., high Load)
  The responding APs or STAs do not transmit Probe Response frame
  reduces unnecessary Probe Response
  helps selection of AP to associate
AP Channel Report element received in the probe responses during the active scanning can be used to help the selection of the next channel to be scanned
Jae Seung Lee, ETRI

## Slide 9: Preference and/or Capability based Filtering
FilterInfo element is added to the Probe Request frame
FilterInfo IE contains optional capability elements including security capabilities of the Requesting STAs
  AP can check the security capabilities of the Requesting STAs
FilterInfo IE contains Filtering Preference element including preferences of the STAs to the responding AP
  Includes request of Security processing or request to associate HT, VHT, or non-HT STA, etc
No Probe Response to the STA if the preferences and/or capabilities of the requesting STA are not acceptable by the responding AP or STA
If the responding AP cannot accept the new STA because of its own operating condition, such as high load, it does not transmit Probe Responses
Jae Seung Lee, ETRI
Slide 9

## Slide 10: Benefits of the Filtering
Reduces the Probe Response traffic
  Filter the Probe Request because the requesting STA cannot be associated with the responding AP or STA
    No reason to transmit Probe Response frame to such STAs
Prevent the association of the STAs that cannot be accepted by the responding AP in advance, during probing
    If the STA cannot be associated with the responding AP, Probe Response is not received  association with the AP is prohibited
Helps the association process by enabling the STA to choose the appropriate APs that can be associated with the STA
Jae Seung Lee, ETRI

## Slide 11: Selective Probe Response – Example (1/2)
Jae Seung Lee, ETRI
Example: Using existing active scanning method
The requesting STA is a VHT STA and only wants to associate with a VHT AP
The STA requires management frame protection
STA
Probe Request
(Broadcast)
Receives Probe Responses
although the STA cannot,
or will not associate with the APs
.
.
.
STA41
(non-HT, no security)
STA11
(HT, No Security)
STA 28
(non-HT,
no security)
STA05
(VHT, Security,
MFPC=1,MFPR=1)
STA09
(VHT, No Security)
STA07
(HT, Security,
MFPC=1,MFPR=1)
STA40
(VHT, Security,
MFPC=0, MFPR=0)
STA29
(VHT, Security,
MFPC=1,MFPR=1)
STA03
(VHT, no security)
High Load!
STA39
(VHT, Security,
MFPC=1,MFPR=1)

## Slide 12: Selective Probe Response – Example (2/2)
Jae Seung Lee, ETRI
Example: Using FilterInfo in Probe Request
The requesting STA is a VHT STA and only wants to associate with a VHT AP
The STA requires management frame protection
STA41
(non-HT, no security)
STA
Probe Request (Broadcast)
Reduced Probe Responses!
STA11
(HT, No Security)
STA 28
(non-HT,
no security)
STA05
(VHT, Security,
MFPC=1,MFPR=1)
STA09
(VHT, No Security)
STA07
(HT, Security,
MFPC=1,MFPR=1)
STA40
(VHT, Security,
MFPC=0, MFPR=0)
STA29
(VHT, Security,
MFPC=1,MFPR=1)
STA03
(VHT, no security)
High Load!
x
x
x
x
x
x
x
x
O
O
Require VHT, Require Security,
MFPC=1, MFPR=1
(in the FilterInfo)
STA39
(VHT, Security,
MFPC=1,MFPR=1)

## Slide 13: FilterInfo element
Specifies options required for Probe Request filtering by the responder of the probe request based on the preferences and/or capabilities of the requesting STAs
Added to the Probe Request frame
Element ID | Length | AP Preference | STA security capability element (or fields) | Other TBD capability/preferences elements
Octets: 1 1 2 variable variable
Jae Seung Lee, ETRI
Slide 13

## Slide 14: AP Preference Field
Bits: 1 1 1 1 1 11
Require Security | Require No Security | Require HT | Require VHT | Require non-HT | Reserved
Specifies the preferences of the STAs that transmit Probe Request frame
    STA’s preferences for security processing, or no security processing or request for association with HT, VHT, or non-HT STA are included
    Other TBD subfields can be added in the future
Jae Seung Lee, ETRI

## Slide 15: STA security capability element
STA security capability element specifies the security capabilities of the STAs that transmit Probe Request frame
    Present if Require Security bit is set in the AP Preference field
    One option is to use RSN IE
    Modified or optimized RSN IE can be considered to be used as the STA Security capability element
Jae Seung Lee, ETRI

## Slide 16: FilterInfo element - Example
Example 1:
Example 2:
    Use RSN Capabilities field defined in RSN IE
    6 octets or more (considering future extension)
Jae Seung Lee, ETRI
Element ID | Length | AP Preference | RSN IE | Other TBD capability/preferences elements
Octets: 1 1 2 variable variable
Element ID | Length | AP Preference | RSN Capabilities | Other TBD capability/preferences elements
Octets: 1 1 2 2 variable

## Slide 17: Selective Scanning
AP Channel Report element is included in Probe Response Frame
  AP Channel Report element contains a list of channels in an operating class where a STA is likely to find an AP, excluding the AP transmitting the AP Channel Report (From 802.11 Revmb)
It can help to perform selective channel scanning
If AP Channel Report element is included in the received probe responses, then a channel in the ChannelList that is also included in the AP Channel Report element that is not scanned yet may be selected as the next channel to be scanned
  The AP Channel Report element included in the most recently received probe response should be used
Jae Seung Lee, ETRI

## Slide 18: Selective Probe Response & Selective Scan
AP 1-1
AP 1-2
AP 1-3
AP 1-…
AP 1-n
STA
AP 3-1
AP 3-2
AP 3-3
AP 3-…
AP 3-n
AP 5-1
AP 5-2
AP 5-3
AP 5-…
AP 5-n
Probe Request on channel 1
Channel 1
Probe Request on channel 3
Probe Request on channel
Channel 6
Channel 11
Probe Response
Probe Response
Probe Response
Probe Response
No response
Check the Preference and Capability of the
requesting STA in the Probe Response
Selective Scanning
Of the Channel
Jae Seung Lee, ETRI

## Slide 19: Conclusion
In active scanning, Probe Response can cause unnecessary packet exchange
We proposed the selective transmission of the Probe Response frame to reduce the unnecessary Probe Response frame
In this proposal:
  Filter the Probe Request using preferences and/or capabilities of the STA that has sent the Probe Request frame
  Selective transmission of the probe response helps to reduce the traffic caused by Probe Response frames, and also helps to select appropriate STAs to be associated with
  Selective Scanning of the channels based on the channel information can reduce the scanning time
Jae Seung Lee, ETRI

## Slide 20
Straw Poll 1
Should the spec framework document be updated with the following text for Fast Network Discovery:
  Non-AP STA may include its preferences and/or capabilities information in the Probe Request frame. If the preferences and/or capabilities of the STA are not acceptable by the responding STA, then the responding STA may not transmit Probe Response.
Yes 18
No 1
Abstain 13
Jae Seung Lee, ETRI

## Slide 21
Slide 21
Slide 21
Straw Poll 2
Should the spec framework document be updated with the following text for Fast Network Discovery:
  If the non-AP STA that has sent the Probe Request is not acceptable by the responding STA because of the responding STA’s current operating condition, then the responding STA may not transmit Probe Response.
Yes 10
No 4
Abstain 17
Jae Seung Lee, ETRI

## Slide 22
Slide 22
Slide 22
Straw Poll 3
Should the spec framework document be updated with the following text for Fast Network Discovery:
  Non-AP STA may include its security processing requirements and/or security capability in the Probe Request frame for Probe Request filtering.
Yes 4
No 0
Abstain 17
Jae Seung Lee, ETRI

## Slide 23
Slide 23
Straw Poll 4
Should the spec framework document be updated with the following text for Fast Network Discovery:
  Non-AP STA may include its required AP’s capabilities in the Probe Request frame for Probe Request filtering.
Yes 4
No 0
Abstain 19
Jae Seung Lee, ETRI

## Slide 24
Slide 24
Slide 24
Straw Poll 5
Should the spec framework document be updated with the following text for Fast Network Discovery:
  AP Channel Report element included in the most recently received Probe Response may be used to select the next channel to be scanned
Yes 9
No 0
Abstain 19
Jae Seung Lee, ETRI

## Slide 25
References
11-12/0063r1 Selective transmission of the Probe Response
11-12/0064r0 Text for Selective transmission of the Probe Response
Jae Seung Lee, ETRI