## Slide 1: SFD Text for Public Key Cryptography
Date: 2012-03-03
Authors:
Name | Affiliations | Address | Phone | email
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com

## Slide 2: Abstract
This proposal includes the text intended for inclusion into Section 3 (Security Framework).

## Slide 3: Proposed SFD Text
The TGai amendment defines the following schemes separately: STA (user) authentication (by AP), AP authentication (by STA) and key generation/management.
The TGai amendment defines ECDH-based key agreement as one of the key generation/management methods.
The TGai amendment defines methods using IETF X.509 Certificate as one of the AP authentication.
The TGai amendment defines methods using IETF X.509 Certificate as one of the STA authentication.

## Slide 4: Terminology
ECDH: Elliptic Curve Diffie-Hellman
IETF X.509 Certificate: Public Key Certificate and its Revocation List defined by RFC5280

## Slide 5: Intention of Text 1
Users and network designers currently use various authentication schemes such as Shared Secret through Public Key Certificate. TGai should make effort to satisfy their requirements.

## Slide 6: Intention of Text 2
ECDH have now become a reasonable option as a key generation algorithm. “NSA Suite B Cryptography” also specify use of ECDH as the key exchange algorithm.

## Slide 7: Intention of Text 3
IETF X.509 Certificate-based authentication for web servers is widely deployed. This is also used for Web-based authentication of wireless LAN networks. And also, IETF X.509 Certificate-based authentication is used by EAP-TTLS and EAP-PEAP. This text leads TGai amendment to support the equivalent level of security as such Web-based authentication technology when STA starts to communicate to new AP.

## Slide 8: Intention of Text 4
IETF X.509 Certificate-based user authentication is used by combination of EAP-TLS and IEEE802.1X. This text leads TGai amendment to support the equivalent level of security as EAP-TLS.

## Slide 9: Straw poll 1
Do you support to include the following text in SFD.
“The TGai amendment defines the following schemes separately: STA (user) authentication (by AP), AP authentication (by STA) and key generation/management.”
Yes: No: Abstain:

## Slide 10: Straw poll 2
Do you support to include the following text in SFD.
“The TGai amendment defines ECDH-based key agreement as one of the key generation/management methods.”
Yes: No: Abstain:

## Slide 11: Straw poll 3
Do you support to include the following text in SFD.
“The TGai amendment defines methods using IETF X.509 Certificate as one of the AP authentication.”
Yes: No: Abstain:

## Slide 12: Straw poll 4
Do you support to include the following text in SFD.
“The TGai amendment defines methods using IETF X.509 Certificate as one of the STA authentication.”
Yes: No: Abstain:

## Slide 13: Backup