## Slide 1: SFD Text for Upper Layers
Date: 2012-05-04
Authors:
Name | Affiliations | Address | Phone | email
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@gmail4.trans-nt.com

## Slide 2: Abstract
DCN: IEEE11-12/0273r7
Title: SFD Text for Higher Layers
Authors and Companies:
Hiroki Nakano (Trans New Technology, Inc.)
Scope: Upper layer
Motivation: page 3 (abstract)
Background information: page 4-18
Motion: page 19-22 including four motions

## Slide 3: Motivation
An IP(v4) address are normally assigned by DHCP(v4) and the specification of DHCP is stable. DHCP includes definition of state transition and have lots of extensions derived from lots of past discussions. Non-AP STA should be still a DHCP client.
The discussions of IPv6 address assignment are still going on actively in IETF and its specification is being changed. We should provide a framework for them.
In addition, TGai should not deny the other protocols because we are the link layer.

## Slide 4: Background Information
Common abbreviation:
DHCP: Dynamic Host Configuration Protocol, which is defined by RFC2131 and the other supplemental RFCs.

## Slide 5: The past Straw poll 1
Do you support to add the following text to the clause 4 of SFD:
“The TGai amendment defines a method of IP(v4) address assignment which works as a transport of DHCP.”
Yes: 5 No: 3 Don’t care: 17 (Mar 15 AM1)

## Slide 6: The past Straw poll 2
Do you support to add the following text to the clause 4 of SFD:
“The TGai amendment defines a generalized method for upper layer transport encapsulation during FILS to enable higher layer services.”
Yes: 7 No: 1 Don’t care: 22 (Mar 15 AM1)

## Slide 7: Proposed Amendment 1
Clause to amend: Section 3
Add to the last of Section 3:
3.3 Encapsulation Framework for HLCF
The TGai amendment defines a generalized method for upper layer transport encapsulation during FILS to enable higher layer services.

## Slide 8: Motivation of Proposed Amendment 1
This sentence intends TGai to support IPv4, IPv6 and other upper layer protocols.
Transparency as a link layer is important in order to support various upper layer protocols.

## Slide 9: Proposed Amendment 2
Clause to amend: Section 5
Add to the last:
5.2 IPv4 support
The TGai amendment defines a method of IP(v4) address assignment which works as a transport of DHCP.

## Slide 10: Proposed Amendment 2 (Supplement)
Clause to amend: Section 2
Add to appropriate line:
DHCP: Dynamic Host Configuration Protocol, which is defined by RFC2131 and the other supplemental RFCs.

## Slide 11: Motivation of Proposed Amendment 2
This sentence intends TGai to provide standard implementation technique of IP(v4) address assignment by DHCP. Our PAR says TGai is required to support “IP address assignment” as an example.
The specification of DHCP is quite stable and widely deployed, therefore it is eligible to be referred by TGai.
The following slides show that a function as a transport is sufficient to achieve the goal of TGai.

## Slide 12: Prerequisite
DHCP with RCO have ability to complete an IP address assignment with a round-trip exchange of frames.
  DHCP: Dynamic Host Configuration Protocol (RFC2131)
  RCO: Rapid Commit Option define (RFC4039)

## Slide 13: Sequence Example by DHCP with RCO
Non-AP STA
AP
DHCP server
DHCP Client Software
Processing for security
DHCP Discover w/ RCO
DHCP Ack
AS
At this point, Non-AP STA has been authenticated.

## Slide 14: Comments & Answers
Frames get bigger. It’s the problem.
  TGai intends to reduce exchanges of packets, not reduce information itself. Therefore, it is natural that less exchanges leads to bigger packets. A round trip of 1000-byte-long frames is obviously preferable to 10 round trips of 100-byte-length packets.
  TGai can provide special “compression” encodings for specific upper layer protocols, such as DHCP. For instance, most of DHCP packets have about 200-byte-long consecutive zeros and a generic data compression technique or a special encoding for DHCP can compress DHCP packets without changing information.

## Slide 15: Comments & Answers
What packets should be forwarded or not? Does it affect security?
  Basically, piggybacked frames of upper layers should be forwarded after authentication is finished. Essentially, non-AP STA can throw any kind of packets for upper layers after authentication.
  If you want a further optimization such as a premature start of IP address assignment processing before completion of authentication, you must consider security mechanism such as packet filtering. However, this is out of our scope, although TGai does not prevent such techniques.

## Slide 16: Comments & Answers
The specific name of a protocol, e.g. “DHCP”, is not suitable for SFD!
  DHCP is obviously the most deployed protocol in protocols for IP address assignment function on the 802 network.

## Slide 17: Proposed Amendment 3
Clause to amend: Section 5
Add to the last:
5.3 IPv6 support
The TGai amendment does not define any detail of IPv6 address assignment and does encourage IPv6 to use a generalized method for upper layer transport encapsulation defined by the TGai amendment.

## Slide 18: Motivation of Proposed Amendment 3
The discussions of IPv6 address assignment are still going on actively in IETF and its specification is being changed. We should provide a framework for them.

## Slide 19: Motion 1
Move to add the following text to the Section 3 of SFD:
“3.3 Encapsulation Framework for HLCF
The TGai amendment defines a generalized method for upper layer transport encapsulation during FILS to enable higher layer services.”
Moved:
Seconded:
Yes: No: Abstain:

## Slide 20: Motion 2
Move to add the following text to the Section 5 of SFD:
“5.2 IPv4 support
The TGai amendment defines a method of IP(v4) address assignment which works as a transport of DHCP.”
Moved:
Seconded:
Yes: No: Abstain:

## Slide 21: Motion 2a
Move to add the following text to the Section 2 of SFD:
“DHCP: Dynamic Host Configuration Protocol, which is defined by RFC2131 and the other supplemental RFCs.”
Moved:
Seconded:
Yes: No: Abstain:

## Slide 22: Motion 3
Move to add the following text to the Section 5 of SFD:
“5.3 IPv6 support
The TGai amendment does not define any detail of IPv6 address assignment and does encourage IPv6 to use a generalized method for upper layer transport encapsulation defined by the TGai amendment.”
Moved:
Seconded:
Yes: No: Abstain:

## Slide 23: Backup

## Slide 24: A possible counterproposal
New software for new protocol
Non-AP STA
AP
DHCP server
Processing for security
TGai new protocol
DHCP Discover w/ RCO
TGai new protocol
DHCP Ack
Translation?
Translation?

## Slide 25: Comparison
 | DHCP with RCO | New protocol w/ DHCP-like frame format | New protocol
Frame exchange | 1 round trip | 1 round trip | 1 round trip
Non-AP STA is | DHCP client | TGai client | TGai client
AP is | a forwarder | often a DHCP client | often a DHCP client
TGai is | a transport | a protocol for IP address assignment | a protocol for IP address assignment
What information is distributed? | DHCP defines | DHCP defines (including future extensions?) | TGai defines
Behavior of non-AP STA | DHCP defines | TGai defines | TGai defines
Behavior of AP | a forwarder | TGai defines | TGai defines
AP has | no state | some state(?) | some state(?)
When an address assignment expires | DHCP uses normal transport to extend | TGai defines extending procedure | TGai defines extending procedure