## Slide 1: Higher Layer Configuration Function for TGai SFD
Date: 2012-03-14
Authors:
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA Hiroshi Mano | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Gabor Bajko | Nokia | 200 S Mathilda Ave, Sunnyvale | 8585253693 | gabor.bajko@nokia.com
Mark RISON Tom Siep | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Katsuo Yunoki | KDDI R&D Laboratories | 3-10-10 Iidabashi, Chiyoda-ku, Tokyo, 102-8460 JAPAN |  | yunoki@kddilabs.jp
George Cherian Santosh Abraham Jouni Malinen | Qualcomm | 5775 Morehouse Dr., San Diego, CA | 8586516645 | gcherian@qualcomm.com

## Slide 2: Abstract
This document describes proposed text for TGai SFD Clause 4 (IP address assignment).
Example implementation: 12/0032r3, 12/0033r1

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Optimized Sequence for Internet Access with 1 Round-trip Association (e.g. 11/1160r3)
STA
AP
DHCP Server
Gateway
Correspondent Node
Communication
AS
Virtually Simultaneous
(RADIUS for AAA)
Assoc. Req.
w/HLCF Request
Element
(could be
encrypted)
Assoc. Resp.
w/HLCF Response
Element
(could be
encrypted)
e.g. DHCP w/Rapid Commit Option
ARP/ND

## Slide 5: Concept
The proposed protocol is terminated at the AP.
This protocol is NOT DHCP/RA. But it may use the message format for future flexibility.
AP
STA
.11ai HLCF
DHCP
RA
Static
Out of Scope

## Slide 6: Proposal for TGai SFD Clause 4
The TGai amendments shall support higher layer configuration function (HLCF).
The HLCF shall support IPv4 and IPv6.
The HLCF shall be able to carry the following parameters.
  IP address and netmask/prefix length for the STA.
  Default gateway’s IP address.
  Default gateway’s MAC address.
  DNS servers’ addresses.
The HLCF shall be completed by 1-roundtrip frame exchange initiated by non-AP STA.
The HLCF capability of the AP shall be indicated in Beacon and Probe Response.
The HLCF parameters shall be carried as IEs in Association Request/Response Frames.

## Slide 7: Performance Evaluation
Evaluation in IPv4 environment.
Currently DHCPv4 is used for IPv4 layer configuration in most environment.
Compare with DHCPv4.

## Slide 8: DHCPv4 Latency (measured)
STA
AP
DHCP Server
IP address assignment
EAPOL-key 4
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST
DHCPACK
Gratuitous ARP
34ms
1ms
193ms
3ms
1035ms
1ms
3ms
1ms
5ms
1619ms
Approximatery 3,000ms from the STA receiving
EAPOL-key 4 to assigning IP address
Wait for other
DHCPOFFER
Duplicate
Address Check
Wait for timeout
of Gratuitous ARP

## Slide 9: Latency Estimation of the Proposal
STA
AP
DHCP Server
IP address
assignment
Association Request
w/HLCF
Association Response
w/HLCF
1ms
5ms
3ms
IP layer configuration is simultaniously done with association,
authentication, key negotiation.
So the time just for IP layer configuration becomes practically “0”.
It means that the proposal makes initial link setup time 3sec less than
current implementation.
Without Duplicate
Address Check
(Duplicate Address
Check is defined as
“SHOULD”)
DHCPDISCOVER w/RCO
DHCPACK w/RCO
5ms
14ms from starting association to IP address assignment.

## Slide 10: Air-time Occupancy
Frame | Size | DHCPv4 (DS1) [us] | DHCPv4 (OFDM6) [us] | Proposed (DS1) [us] | Proposed (OFDM6) [us]
DHCPDISCOVER | 380 | 3812 | 667 | 3040 | 507
DHCPOFFER | 380 | 3812 | 667 | 3040 | 507
DHCPREQUEST | 380 | 3812 | 667 | 3040 | 507
DHCPACK | 380 | 3812 | 667 | 3040 | 507
ARP Req | 80 | 1412 | 267 | - | -
Total |  | 16660 | 2935 | 12160 | 2028
IP layer configuration information is included in Association Request/Response.
So it doesn’t need extra air-time overhead such as IFS, preamble and headers.
And ARP request for duplicate address detection can be omitted.
3,500us (21%) less than existing.
907us (31%) less than existing.

## Slide 11: Motion (1/6)
Move to add the following text to the clause 4 of the specification framework document:
” The TGai amendments shall support higher layer configuration function (HLCF).”
Moved:
Seconded:
Y/N/A:

## Slide 12: Motion (2/6)
Move to add the following text to the clause 4 of the specification framework document:
” The HLCF shall support IPv4 and IPv6.”
Moved:
Seconded:
Y/N/A:

## Slide 13: Motion (3/6)
Move to add the following text to the clause 4 of the specification framework document:
The HLCF shall be able to carry the following parameters.
  IP address and netmask/prefix length for the STA.
  Default gateway’s IP address.
  Default gateway’s MAC address.
  DNS servers’ addresses.
Moved:
Seconded:
Y/N/A:

## Slide 14: Motion (4/6)
Move to add the following text to the clause 4 of the specification framework document:
” The HLCF shall be completed by 1-roundtrip frame exchange initiated by non-AP STA.”
Moved:
Seconded:
Y/N/A:

## Slide 15: Motion (5/6)
Move to add the following text to the clause 4 of the specification framework document:
” The HLCF capability of the AP shall be indicated in Beacon and Probe Response.”
Moved:
Seconded:
Y/N/A:

## Slide 16: Motion (6/6)
Move to add the following text to the clause 4 of the specification framework document:
” The HLCF parameters shall be carried as IEs in Association Request/Response Frames. ”
Moved:
Seconded:
Y/N/A: