## Slide 1: FILS presentation on High Level Security Requirements
Name | Affiliations | Address | Phone | email
Rob Sun | Huawei Technologies Co., Ltd. | Suite 400, 303 Terry Fox Drive, Kanata, Ontario K2K 3J1 | +1 613 2871948 | Rob.sun@huawei.com
Ping Fang | Huawei Technologies Co., Ltd. | Bldg 7, Vision Software Park, Road Gaoxin Sourth 9, Nanshan District, Shenzhen, Guangdong, China, 518057 | +86 755 36835101 | ping.fang@huawei.com
Zhiming Ding | Huawei Technologies Co., Ltd. | Bldg 7, Vision Software Park, Road Gaoxin Sourth 9, Nanshan District, Shenzhen, Guangdong, China, 518057 | +86 755 36835837 | dingzhiming@huawei.com
Date: 2012-03-14
Authors:

## Slide 2: Abstract
This document proposes text to be inserted in TGai Specification Framework Document (SFD) regarding FILS state machine.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4
Re-caps of related contributions
  12/39r2 FILS Authentication Protocol
    Modified 802.11 Authentication and Association State Machine for FILS

## Slide 5: Modification to 802.11 Authentication and Association State Machine
Slide 5
State 1
Unauthenticated,
Unassociated
Class 1 Frames
State 2
Authenticated,
Unassociated
Class 1 & 2 Frames
State 3
Authenticated,
Associated
(Pending RSN Authentication)
Class 1 ,2 & 3 Frames
IEEE 802.1X Controlled Port Blocked
State 4
Authenticated,
Associated
Class 1 ,2 & 3 Frames
IEEE 802.1X Controlled Port
UnBlocked
Successful
802.11 Authentication
Successful
(Re)Association –RSNA Required
4- way Handshake Successful
Deauthentication
Deauthentication
Deassociation
Deauthentication
Unsuccessful
(Re)Association
(Non-AP STA)
Successful
802.11
Authentication
Unsuccessful
(Re)Association
(Non-AP STA)
Disassociation
Successful
802.11 Authentication
Successful
(Re) Association
No RSNA required or
Fast BSS Transitions
State 5
FILS Authenticated/Unassociated
Class 1 & 2 Frames
With Selected Management &
Data Frames
Successful
FILS Authentication
FILS
Deauthentication
Successful
FILS Association

## Slide 6: Temporary State 5 (FILS Authenticated/Unassociated)
Upon successful FILS authentication, both the STA and AP shall transition to FILS Authenticated/unassociated state
STA at FILS Authenticated/Unassociated state , it allows Class 1,2 and selected Data frames piggybacked over Class 1 &2 frames to be transmitted
Upon receipt of a De-authentication frame from either STA or AP STA with reasons, the STA at the FILS Authenticated/Unassociated state will be transitioned to State 1. STA transitioned back to State 1 may retry with FILS authentication or use the RSNA authentication
Upon successful FILS Association, the STA shall transition to state 4 which allows full class 1, 2 and 3 frames to pass through.
Selected Management Frames and Data Frames | Reasons
EAPOL message with EAP Packet | To carry out the EAP full authentication
IP assignment | To enable the parallel IP assignment to take place

## Slide 7
Motion for proposed text for SFD
Motion: Add the following text (proposed in 248r0 ) to Clause 3 “Security Framework” of TGai SFD, 12/0151
R.3.A: The draft specification shall include support for the optimized 802.11 FILS state machine to enable the FILS authentication and other data frame parallel processing.
Moved:
  Seconded:
  Results: Yes No Abstain