## Slide 1: Recommendations for association
Date: 2012-03-05
Authors:

## Slide 2: Abstract
The presentation provides means to recommend an AP for association.
The recommendations speed-up the discovery of the AP with capacity to serve the already associated STAs and the new associations.

## Slide 3: Discovery of the APs
The least congested APs should be the easy to discover:
  These APs should transmit frequently Measurement Pilots and Probe Responses
    Beacon transmissions should be transmitted between constant intervals
  The operating parameters of these APs should be more often present in Beacons, Measurement Pilots and Probe Responses of other APs
Recommendations of suitable BSSs operating on other channels should be provided
  This select the next channel for scanning and to balance the network load

## Slide 4: Scanning STA operation
The scanning STA selects the AP and initiates the association
  No changes to principles of association or authentication
  The recommendations help the scanning STA:
    to select a less congested AP/channel
      Load balancing effect
    to select the next channel for scanning
      Faster discovery time
The scanning STA may ignore the recommendations
  The discovery of suitable AP may take longer time

## Slide 5: Use of recommendations in passive scanning
The recommendations of Beacon and Measurement Pilot recommend generally APs that are capable to handle new associated STAs
  The frames are transmitted to broadcast address, so only general recommendations are provided
The best benefits from the recommendations is obtained when only few STAs scan simultaneously
  More randomness (to avoid collisions) is needed when large amount of STAs scan simultaneously.
  Just a list of alternatives may speed-up the scanning and allow enough randomness (mitigate collisions)

## Slide 6: Recommendations in active scanning
The recommendations of individually addressed Probe Response may be tailored according to information in Probe Request
  The capabilities of the requesting STA are considered
  Other scanning STAs get the information of available BSSs
The broadcast addressed Probe Responses should contains general recommendations for all STAs

## Slide 7: Performance related information elements
The Neighbor List element contains the capabilities of the reported APs
  Basic indications that do not change frequently
The Neighbor List element do not include performance related parameters (listed on the right)
  The element ID and length are not included to table (2 octets per element)
  Adding 33+6*2 =45 octets per one included BSS parameter set increases the size of the scanning frames
Element | Payload in Octets
BSS Load element | 5
Extended BSS Load element | 5
BSS Average Access Delay element | 1
BSS AC Access Delay element | 4
EDCA Parameter Set | 18
BSS Available Admission Capacity | Variable
Total: | 33 octets

## Slide 8: Recommending AP for association
Response to Multiple Requests | Response Type | Beacon Replacing Probe Response | Recommended Order | Recommending BSS at Other Channel | No More Responses from ESS | Reserved
Bits: 1 | 2 | 1 | 1 | 1 | 1 | 1
The Recommended Order field is set to 1 to indicate that the BSSs are listed in the Neighbor List element in the recommended association order.
The Recommending BSS at Other Channel is set to 1 to recommend association to BSS with different primary channel.
Keep the frames short!
FILS Response parameters element:

## Slide 9: Recommended Order field
The Recommended Order field enables to use implementation specific logic and many parameters
The signaling of the parameter values easily increase the frame size (see slide 7)
Some parameters may be difficult to standardize:
  The AP may be battery powered and avoid power consumption to maximize the battery lifetime
  The AP may be connected to Internet with limited capacity
    For instance many BSS share the same ADSL line and the capacity needs to be shared
  The network may adjust the amount of available APs according to offered load
    The recommendations help to take a new AP into use or to empty an AP from associated STAs in order to shut down the AP

## Slide 10: Recommending BSS on other channel
The Recommending BSS on other channel field directs the scanning STAs away from the congested channel
The listed BSS in the Neighbor List of the Beacon, Probe Response or Measurement Pilot list candidates for the next scanned channel

## Slide 11: Motions for specification framework document
Motion 1.
The ESS should enable fast discovery of BSS that are available to accomodate more STAs.
Yes:
No:
Abstain:

## Slide 12: Motions for specification framework document
Motion 2.
The Beacons, Probe Responses and Measurement Pilot frames may recommend a particular BSS for association.
Yes:
No:
Abstain:

## Slide 13: Motions for specification framework document
Motion 3.
The APs shall have possibility to direct scanning STAs to scan other channels.
Yes:
No:
Abstain: