## Slide 1: Last Response from ESS to Probe Request
Date: 2012-03-05
Authors:

## Slide 2: Abstract
The presentation enables to indicate the last response from the ESS to the Probe Request frame.
When the scanning STA knows that ESS has transmitted the last response:
- The STA knows when to stop waiting for more responses
- The STA knows when it should transmit a new probe request

## Slide 3: Recap, Probe Request and Probe Response exchange
The Probe Request may be transmitted to a broadcast address and it may be responded by many APs
An AP responds to a Probe Request by transmitting a Probe Response or Beacon frame
  The AP may respond to multiple requests with a single frame
  Information of other BSSs may be included to the response
    If AP receives its own operating parameters from other STA response the AP may not transmit Probe Response

## Slide 4: No More Responses from ESS field
Response to Multiple Requests | Response Type | Beacon Replacing Probe Response | Recommended Order | Recommending BSS at Other Channel | No More Responses from ESS | Reserved
Bits: 1 | 2 | 1 | 1 | 1 | 1 | 1
The No More Responses from ESS field is set to 1 to indicate that the Beacon or Probe Response frame is the last transmitted response to the Probe Request frame from the ESS and otherwise set to 0.
FILS Response parameters:

## Slide 5: Benefits
When scanning STA knows the ESSs will not transmit more responses:
  The scanning STA knows to transmit new Probe Request to solicit more detailed responses from the BSS in the ESS
  The scanning STA knows to stop receiving at the channel
    Especially if responses from precise number of ESS were requested, the scanning may be terminated precisely

## Slide 6: Motions for specification framework document
Motion 1.
Do you agree to add No More Responses from the ESS field to the FILS Response Paramters? (As described in slide 4 in this presentation.)
Yes:
No:
Abstain: