## Slide 1: FILS Association
Date: 2012-03-09
Authors:

## Slide 2: Overview
Simplified association
802.1X Authentication
Discovery
Passive scanning
Active scanning
Device & service discovery
Authentication
Association
Key distribution
- 4-way handshake
Higher layer setup
DHCP
ARP
802.1X Authentication
Discovery
Passive scanning
Active scanning
Device & service discovery
Key distribution
- 3-way handshake
Higher layer setup
DHCP
ARP
Current
FILS

## Slide 3: Proposal
Associate using 3-way handshake
  Plus full 802.1X authentication when needed
Association includes pairwise and group key distribution when needed
Association includes block ack parameter handshake
This presentation does not address the piggybacking of higher layer setup on association messaging

## Slide 4: FILS: Open authentication
Association handshake:
  Capability exchange
  Block ack parameter exchange
Reduces legacy exchange from 8 to 3 messages (assuming bidirectional block ack setup)

## Slide 5: FILS: PSK/PMKSA caching
Association Request:
  STA sends fresh SNonce
Association Response:
  AP selects cipher suite
  AP sends fresh ANonce
  Carries encrypted GTK
Association Confirm:
  Client confirms association
Reduces exchange from 16 to 3 (assuming bidirectional block ack setup)

## Slide 6: FILS: Full 802.1X authentication
Association Request:
  Carries implicit EAP start; triggers authentication exchange
  STA sends SNonce
802.1X exchange
Association Response:
  EAP success
  AP sends ANonce + encrypted GTK
Association Confirm
Small speedup due to reduced messaging (removes 9 messages); latency dominated by 802.1X exchange

## Slide 7: FILS and Fast BSS transition
Reduce FT protocol to a 3-way handshake (instead of 4-way handshake)
GTK, IGTK are transferred in Association Response
RIC-Request/Response in FT protocol deprecated (block ack exchange included in association exchange)
Reduces exchange from 6 to 3 messages (assuming bidirection block ack setup)

## Slide 8: Why have an Association Confirm?
Removes race condition with key plumbing
  Authenticator plumbs key prior to sending Association Response
  Supplicant plumbs key on receiving Association Response and prior to sending Association Confirm
  Without the confirm, the AP does not know when the STA has plumbed the keys
Provides a response to AP’s block ack setup request

## Slide 9: Piggy backing higher layer frames
It is possible to piggyback DHCP Discover or DHCP Request on Association Confirm
Encapsulation is tricky (data frame with management frame)
If encrypted, implementation difficulties with decryption at AP
  Not part of the normal data path flow
  Likely involves software decryption (vs hardware for data frame)

## Slide 10: Spec framework text
The draft specification shall support association using a 3-way handshake
The association exchange shall support the following:
  Capability exchange
  Cipher negotiation
  Pairwise and group key distribution
  Bidirectional block ack setup