## Slide 1: The Pitfalls of Hacking and Grafting
Date: 2012-03-08
Authors:

## Slide 2: Abstract
This submission describes the drawbacks to a seemingly attractive behavior

## Slide 3: Protocol Grafting
Desire to use what exists today
  Someone else spent time and money developing it
  It may have been vetted
  Take advantage of wide deployment (if it exists)
Sometimes the fit is not exact
  A re-used protocol ends too abruptly to use directly
  The “wrong side” begins the exchange
So we graft protocols
  Add messages to an existing protocol to “sync” it up; or,
  The combined protocol stops being request/response where the server ends one protocol by sending a message to the client and immediately begins a second by sending another message to the client

## Slide 4: Protocol Grafting in 802.11 Today
802.11 networks are client initiated
  The AP responds to queries but no client state exists until a client asks to establish some
802.1X/EAP is initiated by the infrastructure
  At “link-up” the Authenticator begins its state machine to authenticate the client
RSN defines “link-up” to be entering Authenticated and Associated state
  After 802.11 authentication request/response and 802.11 association request/response, 802.1X Authenticator begins its state machine to authenticate the client (using 802.11 data frames)
  802.11 defines its own Authenticator (in addition to 802.1X) to provide proof-of-possession assurance and derive link-specific keys

## Slide 5: One Premise Promulgated in 11ai
There are “frameworks” we need to reuse
  A framework is (according to wikipedia) “a reusable set of libraries or classes for a software system”. In this case it should be a reusable set of protocols.
The EAP framework
  It’s been deployed
  It kind of works
  People are comfortable with it
The dot1x framework
  Necessary for doing EAP on an 802.11 network
  See above
We need to do some more protocol grafting to use these “frameworks” in a Fast manner for Initial Link Set-up

## Slide 6: Using These Frameworks in 802.11ai
Fewer messages are needed– have to consolidate messages and modify their semantics, but:
  802.11 is still client initiated – protocol starts with a client message
  Network authentication is server initiated– AP sends Requests, client sends Responses
Optimized EAP proposes the following grafting:
  Do away with first message from Authenticator
  Encapsulate EAP in 802.11 authentication frames
  Switch from 802.11 authentication frames to 802.11 association frames with last EAP-Response
  Put 802.11 Authenticator information in frames containing EAP

## Slide 7: Problems with Optimized EAP
EAP is a lock-step Request/Response protocol
  Each Request gets one and only one Response
  A Response with no Request is forbidden by EAP (RFC 3748)!
EAP client must know about its transport now
802.1X defines a protocol state machine to authenticate clients using an EAP server
  AP no longer implements 802.1X Authenticator state machine
  Authenticator can no longer be purely pass-thru since it must parse some EAP frames and pass-thru others
Additional weird error conditions
  What does the Authenticator do if the EAP server responds to the EAP Response in the Assoc-Req with another EAP Request?
Fundamentally, Optimized EAP is a hack

## Slide 8: Problems with Optimized EAP
“We must re-use the ‘EAP framework’ in FILS”
  Yet it requires changes to the EAP protocol and the EAP state machine such that it is no longer EAP
“We must re-use the ‘802.1X framework’ in FILS”
  Yet it does not use 802.1X frames
  Yet it requires changes to the 802.1X protocol and 802.1X state machines such that it is no longer 802.1X
It voids the premise that supposedly required it in the first place!
  It requires changes to implementations of EAP and 802.1X that wish to be “optimized” such that those protocols are no longer being used
  It’s not re-using any sets of protocols– i.e. not re-using “frameworks”
If you have to change both sides it’s a new protocol

## Slide 9: Grafting a Hack
It’s inelegant
  Existing semantics and syntax have lost their meaning
It’s complicated
  Complicated in a security protocol is a recipe for disaster
Its attraction is deceptive
  We get to re-use all this existing code!…except we really don’t
Its benefit is illusory
  We still have to touch every single client and every single AP

## Slide 10: A Modest Proposal (that’s not a motion)
Abandon the idea of Optimized EAP
Let’s just drop the pretense and create a new protocol.