IEEE P802.11
Wireless LANs

| Resolutions for EDCA protection settings |
| --- |
| Date: 2012-03-06 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Erik Lindskog | CSR | 217 Devcon Drive, San Jose, CA 95014 | +1-408-392-8384 | Erik.Lindskog@csr.com |

## Revision History

r0: Initial revision.

## Comments

| 4572 | Erik Lindskog | 8.2.5.2@ 33.43 | It is not possible to know the duration of a VHT Compressed Beamforming frame as the beamformee may choose any Nc in the range 1 to Nr. | Change "VHT Compressed Beamforming frame response" to "biggest possible VHT Compressed Beamforming frame response" (twice) and "VHT Compressed Beamforming response frames" to "biggest possible VHT Compressed Beamforming response frames". |
| --- | --- | --- | --- | --- |
| 4787 | Mark Rison | 8.2.5.2@ 33.30 | In general, it is not possible to accurately estimate the duration of a VHT Compressed Beamforming frame as the beamformee may choose any Nc in the range 1 to Nr | Change "VHT Compressed Beamforming frame response" to "biggest possible VHT Compressed Beamforming frame response" (twice) and "VHT Compressed Beamforming response frames" to "biggest possible VHT Compressed Beamforming response frames"; add a "NOTE---The biggest possible VHT Compressed Beamforming frame is a function of the Feedback Type and Nc Index specified in the NDPA, given that the beamformee has freedom to choose grouping, codebook information, Nc and in some situations Nr." |

## Discussion

As mentioned in the comments, as the duration VHT Compressed Beamforming frame is finally determined by the beamformee, we need to account for the largest possible duration here.

## Proposed changes

The changes are relative to the baseline.  Editorial instructions are shown using bold italics.  Any Word comments should be ignored.

8.2.5.2 Setting for single and multiple protection under enhanced distributed channel

access (EDCA)

In sub-bullet a.7), replace :

"VHT Compressed Beamforming frame response" with "biggest possible VHT Compressed Beamforming frame response"

In sub-bullet a.8), replace:

"VHT Compressed Beamforming frame response" with "biggest possible VHT Compressed Beamforming frame response"

In sub-bullet b), replace:

"VHT Compressed Beamforming response frames" with "biggest possible VHT Compressed Beamforming response frames"

Proposed resolution

ACCEPT.  See proposed changes in IEEE 802.11-12/321r0.

# Text boxes

Abstract

This document proposes resolutions for CIDs 4572 and 4787 on P802.11ac/D2.0, regarding EDCA protection settings.