## Slide 1: TIM Enhancement With Group Bits
Date: 2012-03-12
Authors:

## Slide 2: Abstract
For 11ah, the traffic indication bitmap may need to be segmented and transmitted using multiple beacons [1]
  To support large networks with up to 6000 STAs
Issue with segmented TIM
  A STA may need to wait for multiple beacon intervals before receiving its TIM bit
    Increased energy consumption for STAs
Propose to enhance segmented TIM with group bits

## Slide 3: Operations of segmented TIM
For large 11ah networks, TIM needs to be segmented and transmitted using multiple beacon frames [1]
  TIM element size may be as big as 6000/8 = 750bytes
  Cannot serve a large number of STAs in one beacon interval
Beacon
Beacon
Beacon
Beacon
TIM
Segment 1
Segment 2
Segment N-1
Segment N
Notes: What do we try to say here? The TIM segment size should be smaller because only a limited amount of STA can be served during the beacon interval?

## Slide 4: Issue with segmented TIM
Increased energy consumption for STAs
  A STA may need to wait for multiple beacon intervals before receiving its TIM bit
Notes: I guess it should be enough to show that a STA wakes up for every beacon to receive the TIM segment.
We can leave the PS-POLL out of the picture. Of course we could also state that almost all STA will use PS-Poll to avoid wake up times and this will lead to overload situations where PS-Polls can take a large amount of the resources.

## Slide 5: Enhance TIM with group bits
Enable STAs to sleep after receiving 1 beacon frame
  Reserve some bits in traffic indication bitmap for groups
    1 bit for each group of STAs
    A group bit is set if AP has buffered data for any of the STAs in the group
  Include group bits in every beacon frame
    STAs belong to groups without group bits set do not need to wait for the remaining TIM segments in subsequent beacon frames
  Grouping can be done implicitly/explicitly
    Based on the last N bits of AID
Notes: How many groups should we allow? Should we propose a variable size of 0-7 octets (5 bits indicating the size of the group octets). We could then link the segments to the group, e.g. indicating the starting group number and the number of groups covered by the TIM segment. The group size could then be determined by the length of the TIM.
Instead of implicit grouping, I would prefer a group assignment at association and signaling to change the group assignment.

## Slide 6: Use TIM group bits under light downlink traffic
Allow STAs to save energy by sleeping immediately after receiving 1 beacon frame
  Probability that a group of STAs have 0 downlink data within 1 beacon interval (100ms) is high under light downlink traffic
  More efficient if STA with similar active times are grouped together
# Downlink Packets /Min/STA | Probably of 0 downlink for 50 STAs | Probably of 0 downlink for 100 STAs
0.05 | 0.996 | 0.991
0.5 | 0.96 | 0.92
3 | 0.85 | 0.78
6 | 0.61 | 0.37
Notes: I think this should be slide 3. Can we add e.g. also a group size of 25 and 200 STA?
More efficient if STA with similar active times are grouped together

## Slide 7: Use TIM group bits under heavy downlink traffic
AP cannot serve the downlink traffic for all STAs in one or more beacon intervals
AP enables STAs to save energy by selectively clearing the group bits for certain groups that have buffered downlink data
  STAs in such group will:
    Go to sleep immediately after receiving 1 beacon frame
    Check TIM again at scheduled wakeup time

## Slide 8: Conclusion
Group bits can be used as an effective mean to reduce the energy consuption of STAs when segmented TIM is used in 802.11ah

## Slide 9: Straw Poll
Do you agree to add group bits to the TIM when segmented TIM is used?

## Slide 10: References
[1] 11-12-0117-00-00ah: TIM operation