## Slide 1
Date: 2012-03-12
Authors:
Group Synchronized DCF

## Slide 2: Abstract
STAs with a group may be allowed to contend for the medium – idea of synchronized DCF (S-DCF)
- Qn [1, 2] is not necessary for access control
Medium access window allowed to certain groups and prohibited to other groups
- AP decides on defining these access start and end times
Numerical analysis of S-DCF and comparison with DCF

## Slide 3: Motivation: Combination with Group
STAs can be classified into several groups. Different group can also has different priority. Each group has its own {Qn,Tn} [1, 2].
By setting different {Qn,Tn} values for different groups, AP can control the mainly transmission groups at a period of time.

## Slide 4: Grouping in Beacon Frame
AP informed of Supported Rates, QoS Capability, QoS Traffic Capability, and Power Capability in Association Request frame from STAs
AP clusters STAs into groups and informs the group IDs in Association Response frame

## Slide 5: Proposed Information Element
Propose to add an Information Element termed as Grouping Parameter Set (GrPS) element in the Beacon frame
GrPS element for group ‘n’ shall comprise of:
(i) GID: Group Identification
(ii) Group Access Start Time: Value of T_n
(iii) Group Interval End Time: End time of medium access
Beacon Interval
Time
Stamp
Capability Information
SSID
Supported Rates
FH
Parameter
Set
DS
Parameter
Set
CF
Parameter
Set
TIM
GrPS
Parameter
Set
Proposed IE
Beacon Frame

## Slide 6: Medium Access of STA Groups
Group i’s medium access Start Time is decided by the AP
Start Time based on number of associated STAs per group and priority setting per group
Group Interval End Time for i-th group is identical to prohibition time for (i+1)-th group
Medium access delay for Group 3

## Slide 7: Overlapping Prohibition Time among STA Groups
Overlapping prohibition times for efficient medium contention, e.g., Groups 4 and 3 medium access
Overlapping medium access reduced idle medium time

## Slide 8: Synchronized Medium Access
If otherwise not DCF, beacon frame consists of information on synchronized medium access
Beacon informs the GrPS info to grouped STAs
Short beacon consists of GrPS for remaining groups yet to access medium
Beacon
Short Beacon
GrPS

## Slide 9: Grouping for S-DCF
N1
N2 > N1
N3 > N2
For DCF, number of stations is denoted by N
For S-DCF:
Three groups chosen, (N1+N2+N3) = N
Variable durations of an empty slot (σ) for N1, N2, and
N3
Transmission probability, τ, a function of N1, N2, and N3
DCF G1
DCF G2
DCF G3

## Slide 10: Summary
S-DCF outperforms DCF with increasing number of STAs contending for the channel
GrPS element proposed to be included in the Beacon frame
Only limited number of groups are allowed to contend during specified medium access window defined in the GrPS element

## Slide 11: References
“Power Saving Possibilities for Networks Supporting a Large number of STAs,” doc.: IEEE 802.11-12/0028r1, January 2012, Renesas Mobile Corporation
“DCF Enhancements for Large Number of STAs,” doc.: IEEE 802.11-11/1255r0, September 2011, CATR

## Slide 12: Straw Poll
Do you agree to include a parameter set in the Beacon frame?

## Slide 13: Straw Poll
Do you agree to include the GrPS information element in the Beacon frame?

## Slide 14: Straw Poll
Do you agree that certain number of groups are allowed to contend for access within a specific medium access window?