## Slide 1: Considerations on down-clocking ratio
Date: 2012-03-09
Authors:

## Slide 2: Abstract
This document includes considerations for selecting down-clocking ratio.

## Slide 3: Introduction
There are two major use cases for IEEE 802.11af system
  In-home media distribution
  Cellular offloading
One of the consideration point when we decide down-clocking ratio is channel statistics of possible use cases (especially delay spread)
To see delay spread statistics, we examine well-kwon channel model used for IMT-Adv. Evaluation
  Guidelines for evaluation of radio interface technologies for IMT-Advanced, REPORT ITU-R M.2135 [1] (especially annex A 1.3.1 to 1.3.2.1)
  IST-4-027756 WINNER II D1.1.1 V1.1 [2] (especially section 4.2)
Since channel model depends on user location (LoS/NLoS/OtoI), we examine multiple location for each channel model

## Slide 4: Channel model (Summary)
Scenario | InH |  | UMi |  |  | UMa | 
 | LoS | NLoS | LoS | NLoS | O-to-I | LoS | NLoS
Delay Spread (log10(s)) | (-7.7, 0.18)* | (-7.41, 0.14) * | (-7.19,0.4)* | (-6.89,0.54)* | (-6.62,0.32)* | (-7.03,0.66)* | (-6.44,0.39)*
K-factor (K) (dB) | (7,4)* | N/A | (9,5)* | N/A | N/A | (9,3.5)* | N/A
Delay distribution | Exp | Exp | Exp | Exp | Exp | Exp | Exp
Delay scaling parameter | 3.6 | 3 | 3.2 | 3 | 2.2 | 2.5 | 2.3
Number of cluster | 20 | 20 | 20 | 20 | 20 | 20 | 20
Per cluster shadowing std ζ (dB) | 6 | 3 | 3 | 3 | 4 | 3 | 3
LoS probability as a function of distance, d(m) |  |  |  |  |  |  | 
* (μ,σ)
For SNR evaluation, we assume noise figure 5dB, cable loss 2dB, 700MHz center frequency, signal power -1.8dBm per 100kHz (PSD).

## Slide 5: Indoor Hotspot (InH)
User Location | Average SNR (dB) | Mean rms delay (ns)
10m | 66.62 | 8.2
50m | 54.73 | 22.6
100m | 49.69 | 22.6

## Slide 6: Urban Micro (UMi)
User Location | Average SNR (dB) | Mean rms delay (ns)
30m | 54.90 | 180
100m | 31.42 | 238
500m | -1.67 | 238

## Slide 7: Urban Macro (UMa)
User Location | Average SNR (dB) | Mean rms delay (ns)
30m | 53.07 | 163
100m | 37.42 | 364
500m | 1.4742 | 364

## Slide 8: Observation
In most cases, CP size with 4us provides enough protection (90% probability of 5 times rms delay spread are within CP length)
So, 5x down-clock from IEEE 802.11ac PHY will be good candidates for IEEE 802.11af PHY
And we may need to think about 4x down-clock if 5MHz BW can be fit into 6MHz TV channel

## Slide 9: References
[1] Report M.2135, “Guidelines for evaluation of radio interface technologies for IMT-Advanced, ” available at http://www.itu.int/pub/R-REP-M.2135
[2] IST-4-027756 WINNER II D1.1.1 V1.1, “WINNER II interim channel models,” available at http://www.ist-winner.org/deliverables.html