## Slide 1: Downclocking Options for TGaf PHY
Date: 2012-03-14
Authors:
Slide 1

## Slide 2: Outline
Short presentation providing status of downclocking options for 6MHz and 8MHz channels
Slide 2

## Slide 3: 6MHz channels in the US
Main issue for the US is the spectral mask (-55dBr)
We have been looking at 4MHz, 5MHz and 6MHz channels in terms of the required digital filtering and PA backoff.
In regards to PA backoff , there is less than 0.8dB increase in the required backoff going from 4MHz to 5MHz and both BW require about 10dB backoff. Going from 5MHz to 6MHz may not require much increased backoff.
In regards to digital filtering, we observed that both 4MHz and 5MHz are reasonably doable whereas 6MHz is harder to do but may be possible.
Unlike 6MHz channels, both 4 and 5MHz have coexistence problems between one channel, two channels and four channels (channels partially overlap and SIG field can’t be decoded)
Slide 3

## Slide 4: Cont.
Conclusions:
  5MHz preferable to 4MHz and reasonably doable.
  6MHz appealing because it solves the coexistence issues and provides better solution for 6MHz channelization in countries where mask not as tight as the US (e.g. Canada) and in countries that use 7MHz channelization
Propose to consider 5 or 6MHz channelization but if 5MHz is chosen a good coexistence mechanism between 5/10/20MHz channel BW is needed
Slide 4

## Slide 5: Downclocking Factors
As discussed in [1], delay spread immunity and efficiency play an important role.
Given LTE’s 4.7uS GI and its successful deployment in 700MHz in the US and Korea there may be no need for a larger CP.
In addition, deployment of 11af may be limited to hotspots and hotzones (similar to current 11n deployments for outdoor WiFi) which will reduce the actual delay spread
5MHz channels can be achieved with downclocking of 4 or 8. Downclocking of 8 suffers from reduced efficiency especially with short packet or MU-MIMO
  note that a 1500byte packet at MCS8 over 5MHz channel (about 20Mbps) is only 0.6mS
6MHz channels may be achieved by downclocking of 3.3 or 6.6
A summary table is shown in the next slide
Slide 5

## Slide 6: Cont. – Summary Table
5MHz channel bandwidth can be achieved by
  Option A: Downclocking VHT20 by a factor of 4
  Option B: Downclocking VHT40 by a factor of 8
Option A | Option B
3.2us GI (Might cause PER floor at high MCS if maximum excess delay is larger) | 6.4us GI
Maximum rate of 19.5Mbps (5MHz BW, MCS8, NSS=1) MCS 9 is invalid | Maximum rate of 22.5Mbps (5MHz BW, MCS 9, NSS=1)
 | Lower efficiency due to larger preamble length (Fixed overhead is in terms of OFDM symbols, not microseconds).
Relative efficiency of 86% compared to 11ac for 2ms PPDU (Assumes MCS9 which is not valid!) (based on results in slide 7) | Relative efficiency of 70% compared to 11ac for 2ms PPDU (based on results in slide 7)
Can do 32/40MHz | Can do 2.5MHz

## Slide 7: MAC Efficiency as a Function of DC Ratio
The tables provide a list of the major contributors to overhead in the system
For assumptions see Appendix
SU | 11af Data/Preamble/Backoff/Difs/Sifs | 11af relative to 11ac
DownClk=4, PPDU=1mS | 62.2/18.1/11.2/5.2/2.3% | 75%
DownClk=8, PPDU=1mS | 42.3/28.9/15.7/7.8/3.6% | 51%
DownClk=4, PPDU=2mS | 77.8/10.6/6.5/3.1/1.3% | 86%
DownClk=8, PPDU=2mS | 63.3/18.4/10/5/2.3% | 70%
MU | 11af Data/BAR/Preamble/Backoff/Difs/Sifs/FBP | 11af relative to 11ac | MU Gain vs. SU
DownClk=4, PPDU=2mS | 45/7.1/25.6/5.2/2.4/5.3/1.4% | 65% | +73%
DownClk=4, PPDU=5mS | 65.1/3.9/17.1/3.2/1.5/3.2/1.2% | 78% | +127%
DownClk=8, PPDU=2mS | 26.7/4.1/40.7/6.7/3.3/7.7/2.8% | 42% | +26%
DownClk=8, PPDU=5mS | 42/2.3/31.1/5/2.5/5.8/3.1% | 54% | +53%
Slide 7

## Slide 8: 8MHz Channels
As discussed in [1] consider downclocking of 5 to have 8MHz or 6 to have slightly less than 8MHz channel BW.
Need more info from OFCOM on ACLR before a decision can be made
As with the 6MHz channels if downclocking value of 6 is chosen coexistence needs to be solved
Downclocking values much higher (such as 10) will limit channelization to 16MHz which is much too low for the UK
Slide 8

## Slide 9: Summary
We consider the following two options for 6MHz channels
  5Mhz with DC=4 or 8
  6MHz with DC=3.33 or 6.67
We consider DC=5 or 6 for 8MHz channels
Decision expected in the next meeting
Slide 9

## Slide 10: Straw Poll 1
Do you support 5MHz or 6MHz channelization for 6MHz channels?
Y
N
A
Slide 10

## Slide 11: Straw Poll 2
Do you support DC ratio of 5 or 6 for 8MHz channels?
Y
N
A
Slide 11

## Slide 12: Straw Poll 3
Do you support defining non-contiguous operation 5+5 or 6+6?
Y
N
A
Slide 12

## Slide 13: References
        [1] 11-11-1544-01-00af-initial-proposal-for-tgaf-phy.pptx
Slide 13

## Slide 14: Appendix - Effect of Down clocking on MAC Tput
In packet based systems such as 802.11, for a given transmission BW, having higher FFT size with a fixed PPDU length in [uS] can reduce the MAC Tput since there is a fixed overhead arising from the preamble and other control/feedback packets
  Fixed overhead is in terms of OFDM symbols, not uS, (e.g., one symbol for LTF), so the fraction of time used for overhead increases as down clocking/OFDM symbol length increases
We compare 11ac 20MHz with down clocking by 4 to 40MHz with down clocking by 8 – both result in a theoretical 11af 5MHz BW system
  Antenna configuration 4x1 with 3 users co-paired for MU-MIMO
    Tone grouping for feedback - Ng=2
  Data assumed to run using MCS9 and control using MCS0
  SU Preamble consists of 8 symbols
  MU-MIMO packet preamble adds 3 symbols
  Slot time = 5+CLOCK_RATIO*4[uS]
  SIFS time = CLOCK_RATIO*8[uS]
  Feedback at 10msec intervals, uses MCS9
  CWMIN=15
Based on the results we must carefully choose the DC ratio to avoid high MAC Tput loss
Slide 14