## Slide 1: Switching between DCF and PP-MAC
Date: 2012-3-14
Authors:

## Slide 2: Abstract
This contribution proposes a solution for 802.11ah MAC to operate efficiently under the various situations.

## Slide 3: Motivation
Various use cases are defined in 802.11ah [1].
  Smart grid, environmental/agricultural monitoring, industrial process automation, healthcare system, …
In some use cases, the traffic characteristics may vary depending on the situation.
  In normal operation, STAs transmit uplink data sparsely with different transmission starting time.
  When an event is detected or an emergency occurs, the STAs attempt to transmit data simultaneously for a while.
  For example, when disaster (forest fire, flood) is detected (use case 1c), system is out of work (use case 1d), a patient’s condition (blood pressure, heart rate) changed (use case 1f).
MAC proper to the situation should be considered.

## Slide 4: Problems
In normal operation, DCF is enough to handle uplink transmissions.
  If the STAs’ uplink transmissions are sparse, there may be little degradation from collisions.
  For example, STAs transmit few 100 bytes every few ~ 10s minutes in use case 1f [1].
  If Probe and Pull MAC [2] is used, probe/pull messages may be wasteful.
  The STAs wait for the probe message to respond it and pull message to transmit data, which causes STAs’ power consumption and delay.
SIFS
Probe
AP
STA1
P-ACK
STA2
STA3
STA4
Pull
SIFS
Data
SIFS
SIFS
ACK
Probe
Probe
Have nothing to send
Have nothing to send
Have data to send
wasteful
wasteful
Should wait for the next probe message
In DCF, STA2 can attempt to transmit data immediately
Now, STA2 can transmit data

## Slide 5: Problems
When an event is detected or an emergency occurs, PP-MAC is better.
  PP-MAC provides better throughput & fairness, and low latency for the simultaneous uplink transmissions [3].
Changing MAC according to the situation is required.

## Slide 6: Solution
Switching DCF to PP-MAC when an emergency occurs
  PP-MAC handles simultaneous uplink transmission attempts.
Switching PP-MAC to DCF in the normal operation
An emergency occurs
DCF
PP-MAC
AP
AP

## Slide 7: Solution
Criteria for switching MAC
  Information from the application (cognition of emergency traffic in AP or STAs)
  Collisions in MAC (in DCF)
  The number of STAs that respond to the probe message (in PP-MAC)
Methods
  AP starts to send a probe message (with a reserved bit set to 1) to switch DCF to PP-MAC.
  AP sends a PP-END message or a probe message (with a reserved bit set to 0) to switch PP-MAC to DCF.
  STAs request to AP for switching to PP-MAC by using a reserved bit in the MAC header of uplink data or by sending a PP-REQ message

## Slide 8: Conclusions
Issue the problem under the various situations
Propose criteria and methods for switching between DCF and PP-MAC
Further quantify the performance of the proposed solution according to the environments

## Slide 9: References
[1] 11-11/0457r0, Potential Compromise for 802.11ah Use Case Document
[2] 11-11/1512r4, MAC considerations for 802.11ah (Probe and Pull MAC)
[3] 11-12/0326r1, Uplink Performance Comparison of PP-MAC and DCF