## Slide 1: Proposed introductory text for 11ai Draft
Date: 2012-04-04
Authors:

## Slide 2: Abstract: Proposed introductory text for 11ai Draft
The template for Amendments has an introductory clause and two sub-clauses. New rules in IEEE allow the text in this introductory section to vary in wording from the PAR. This allows text which is more explanatory in nature.
The text for the Introductory paragraph and the Purpose clauses have been expanded for better reader context. The Scope clause is taken from the PAR verbatim.

## Slide 3: Introduction: paragraph 1
IEEE 802.11 devices are increasingly becoming more mobile with a need for connectivity in varied environments. The primary need which Project 802.11ai satisfies comes from an environment where a large number of mobile users are constantly entering and leaving the coverage area of an extended service set (ESS). Prior to the functionality defined by this project, every time the mobile device enters an ESS the mobile device must do an full set-up with an access point (AP) to establish wireless local area network (LAN) connectivity.

## Slide 4: Introduction: paragraph 2
Full link establishment works well when the number of new stations (STAs) in a given time period is small. It also works well when the number of choices for the STA for connection is small. In highly congested situations, where there are a very high number of STAs and APs, current over-the-air association mechanisms inefficiencies limit access to network resources.

## Slide 5: Scope
The Project Authorization for P802.11ai States:
  This amendment defines mechanisms that provide IEEE 802.11 networks with fast initial link set-up methods which do not degrade the security offered by Robust Security Network Association (RSNA) already defined in IEEE 802.1.1.

## Slide 6: Purpose (1 of 2)
Efficient mechanisms that scale well when a high number of users simultaneously enter a complex AP environment are needed. This requires the ESS to minimize the time the STAs spend in initial link setup, while maintaining secure authentication. The purpose of Fast Initial Link Setup (FILS) is to enable efficient high-volume initial access to network services.

## Slide 7: Purpose (2 of 2)
This requires efficient mechanisms that:
  scale with a high number of users simultaneously entering an ESS
  minimize the time spent within the initial link set-up phase
  securely provide initial authentication
The current IEEE 802.11 specification does not meet these requirements in some usage scenarios. Optimization of the link set-up is desirable, including improvements to
  AP / network discovery
  secure authentication
  mechanisms to support concurrency in the exchange of higher layer protocol messages during the authentication phase, such as assignment of IP addresses