## Slide 1: Proposed SFD Text for 802.11ai FILS Procedure with Pre-Acquired Knowledge
Date: 2012-05-14
Authors:

## Slide 2: Abstract
This document proposes text to be inserted in TGai Specification Framework Document (SFD) regarding a procedure that allows pre-acquired knowledge to be used to accelerate 802.11ai link setup process.
This is a follow-up contribution with “high-level” specification aspects that are currently not covered by the SFD but were presented to TGai at previous meetings in the contributions, 12/0010r1 and 12/0160r3.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2,3, 4

## Slide 4
Background
12/0191r3: Call for Contributions to the TGai Specification Framework Document (SFD);
12/0151r7: Approved TGai SFD document up-to 2012 March meeting;
12/0010r1: a contribution presented in January Jacksonville regarding 11ai link setup procedures, and Received Positive feedback on the straw polls;
12/0160r3: a contribution presented in March Hawaii meeting, as a follow-up to the contribution 12/0010r1;

## Slide 5: Discussions
Proposal Technical Key Points
  Use Pre-acquired knowledge to accelerate the 802.11ai link setup process.
  Accommodate assorted link setup optimization variants.
Motivations:
  There are 802.11ai use cases where the AP and the STA could pre-acquire knowledge of the link to be setup, e.g.,
    The STA has been previously connected to another network, e.g., 3G to WLAN Handover, and Hot-Spot Pass-Through Internet Access to offload traffic from other network;
    An AP at a transit station can access the information such as the train arrival schedule, and active internet users that are arriving in the train.
  The pre-acquired knowledge can be used to accelerate the link setup, a useful mechanism used/proven in other wireless technologies;
  It is feasible and practical to use pre-acquired knowledge in initial link setup in the 802.11 context, with proper procedural and signaling supports.

## Slide 6: Discussions – con’t
Proposed procedural actions and Signaling supports:
  FILS capability indication:
    Essentially an one-bit flag, should be provided in the earlier messages of the link to be setup.  this has been already included in the current TGai SFD at page 6, section 6.1.2.
  Pre-acquired knowledge indication and confirmation:
    Can be provided in Information Elements (IEs) carried in the existing management frames, e.g., Probe Request / Response, and/or Association Request / Response.
  Negotiation of a customized FIST solution:
    More than one FILS solutions may be defined and supported by TGai to accelerate the link setup procedure;
    The selection of a customized FILS solution should be conducted in a flexible and interoperable way, e.g., through a negotiation by piggybacking the existing management message rounds, i.e., no additional message rounds required.

## Slide 7: Straw Polls for Proposed Text for SFD
Straw-Poll-1: Do you support adding the following text to Subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7
  A TGai solution should allow AP and STA to use pre-acquired knowledge to accelerate the link setup.
  A TGai solution should provide procedural and signaling supports for pre-acquired knowledge indication and confirmation between the two STAs of the 802.11 link to be setup.
Mover:
Seconder:
Result Yes NO Need more info____________

## Slide 8: Straw Polls for Proposed Text for SFD – con’t
Straw-Poll-2: Do you support adding the following text to Subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7 :
  The pre-acquired knowledge indication and confirmation should be provided in the unicast messages between the two STAs of the link to be setup.
  The pre-acquired knowledge indication and confirmation can be provided in the Information Elements (IEs) carried by the existing management frames, e.g., Probe Request / Response, and/or Association Request / Response.
Mover:
Seconder:
Result Yes NO Need more Info_____________

## Slide 9: Straw Polls for Proposed Text for SFD – con’t
Straw-Poll-3: Do you support adding the following text under subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7:
  More than one FILS solutions can be defined and supported by TGai in a flexible and interoperable way.
  In order to accommodate more than one FILS solutions in TGai, a negotiation procedure should be supported to customize the link setup procedure for each specific cases.
  The negotiation procedure for selecting a specific link setup procdure can be conducted by piggybacking the existing management message rounds, such that no additional message rounds are required.
Mover:
Seconder:
Result Yes NO Need more info_______________

## Slide 10: Motions for Proposed Text for SFD
Motion-1: add the following text to Subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7
  A TGai solution should allow AP and STA to use pre-acquired knowledge to accelerate the link setup.
  A TGai solution should provide procedural and signaling supports for pre-acquired knowledge indication and confirmation between the two STAs of the 802.11 link to be setup.
Mover:
Seconder:
Result Yes NO Abstain_______________

## Slide 11: Motions for Proposed Text for SFD – con’t
(notes: This motion proposes additional text for the TGai SFD, in an incremental manner to the motion-1 of this contribution. It will be made only if Motion-1 passes. )
Motion-2: add the following text to Subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7 :
  The pre-acquired knowledge indication and confirmation should be provided in the unicast messages between the two STAs of the link to be setup.
  The pre-acquired knowledge indication and confirmation can be provided in the Information Elements (IEs) carried by the existing management frames, e.g., Probe Request / Response, and/or Association Request / Response.
Mover:
Seconder:
Result Yes NO Abstain_______________

## Slide 12: Motions for Proposed Text for SFD – con’t
Motion-3: add the following text under subsection “3.1 Optimizations”, on page 4, in the TGai SFD, 12/0151r7:
  More than one FILS solutions can be defined and supported by TGai in a flexible and interoperable way.
  In order to accommodate more than one FILS solutions in TGai, a negotiation procedure should be supported to customize the link setup procedure for each specific cases.
  The negotiation procedure for selecting a specific link setup procdure can be conducted by piggybacking the existing management message rounds, such that no additional message rounds are required.
Mover:
Seconder:
Result Yes NO Abstain_______________