## Slide 1: Extend 802.1X for higher layer configuration in FILS
Date: 2012-04-21
Authors:
Name | Affiliations | Address | Phone | email
Dapeng Liu | China Mobile | 32 Xuanwumen West Street Beijng, Xicheng District, 100053 China | +86-13911788933 | liudapeng@chinamobile.com

## Slide 2: Abstract
This document proposes extend 802.1X to carry the higher layer configuration information in FILS scenario.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3,4

## Slide 4: Background
802.1X is used for 802.11 authentication. The authentication and IP address configuration procedure is separated in current specification. It normally requires a DHCP or RA procedure after the authentication to configure the IP address and other higher layer information after the authentication. This will increase the link set up time.

## Slide 5: Current authentication and higher layer configuration procedure
Authentication procedure
IP address and other
Higher layer configuration
Additional procedure for IP address and other
higher layer configuration will increase the link
set up time

## Slide 6: Proposal: Combine IP address configuration and higher layer configuration with authentication
STA
AP
Auth
AS
Assoc
EAP-TTLS
/MS-CHAPv2
EAPOL
Key
802.1X extension
to carry IP
and higher layer configuration
IP address and higher layer configuration
Combine authentication and
higher layer configuration
After authentication, the IP address and other IP layer configuration is done

## Slide 7: 802.1X extension
Define new 802.1X message to carry higher layer configuration information
  Packet type: EAPOL-configuration
  Payload:
    IP address
    Subnet mask
    Default gateway

## Slide 8
Questions?