## Slide 1: Proposed SFD Text for 802.11ai Prioritized Active Scanning
Name | Affiliations | Address | Phone | email
Giwon Park | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1879 | giwon.park@lge.com
Jinsam Kwak | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-7902 | Jinsam.kwak@lge.com
Kiseon Ryu | LG Electronics | 10225 Willow Creek Rd, San Diego, CA, 92131, USA | +1 (858)-635-5209 | kiseon.ryu@lge.com
Jing-Rong Hsieh | HTC Corp. | 1F, 6-3 Baoqiang Road, Xindian district, New Taipei City, Taiwan |  | jing_hsieh@htc.com
ChaoChun Wang | MediaTek USA | 2860 Junction Ave, San Jose, CA USA |  | chaochun.wang@mediatek.com
James Yee | MediaTek, Inc. | No. 1, Dusing 1st Rd, Hsinchu, Taiwan |  | james.yee@mediatek.com
Date: 2012-05-04
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses the following phase
  AP Discovery
Prioritizing the responses from desired APs helps reduce the time for the scanning STA to discover suitable APs

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Background, related contributions
12/0191r0: Call for Contributions to the TGai Specification Framework Document (SFD);
12/0151r2: Approved TGai SFD initial document; (12/0151r3 with page numbers)
Following contributions have been submitted to 802.11ai TG regarding prioritized active scanning
  11-12-0246-00-00ai-differentiate-transmissions-of-probe-responses
  11-12-0257-00-00ai-active-scanning-enhancement

## Slide 5: Background
Three kinds of active scanning are defined in the current IEEE 802.11 standard
  Probe Request including
    Specific SSID(s) only
    Wildcard SSID only
    Specific SSID(s) + wildcard SSID
Each method has the following Cons.
  Wildcard SSID only OR Specific SSID(s) + wildcard SSID
    Contention among APs is highly expected
    It may be hard for an STA to find a preferred AP on early stage
  Specific SSID(s) only
    If there is no APs with specific SSID(s) around STA, delay of active scanning can be increased
During AP discovery, it is highly recommended that STA can discover and select AP, which STA prefers, with high priority

## Slide 6: Prioritize preferred APs to respond
To help FILS, AP should prioritize the timing of sending probe responses based on the ID addressing scheme in probe request
  The probe requests with
    Only specific ID
    Only broadcast/wildcard ID addresses
    Both broadcast/wildcard ID addresses and specific ID
  If AP’s ID matches the specific ID in the Probe Request, the AP has a high priority to respond. Otherwise, AP has a low priority to respond.
Possible solution
  Option 1
    Adopt EDCA parameters for giving higher priority to respond to probe request carrying specific ID address over wildcard SSID address.
      Specific ID case uses parameters for AC_VO or AC_VI
        AC_VI has larger contention window size
      The wildcard case remains the same or uses those for AC_BE
    Replace DIFS with shorter inter-frame space, such as PIFS
  Option 2
    Allowing high priority AP to send Probe Response first and delaying the Probe Response transmission from lower priority AP

## Slide 7: Motion 1
Concept
  The 802.11ai shall have a mechanism for prioritized active scanning to reduce the latency of active scanning.
Motion
  Do you support to add the above concept into Section 6 “Fast Network Discovery” of the TGai spec framework?
    Yes
    No
    Abstain

## Slide 8: Motion 2
Concept
  Prioritized active scanning is helpful for the STA to discover and select the high priority AP(s) earlier than the low priority AP(s).
Motion
  Do you support to add the above concept into Section 6 “Fast Network Discovery” of the TGai spec framework?
    Yes
    No
    Abstain

## Slide 9: Motion 3
Concept
  An AP should respond to probe request addressed to the AP with higher priority over probe request with wildcard ID.
Motion
  Do you support to add the above concept into Section 6 “Fast Network Discovery” of the TGai spec framework?
    Yes
    No
    Abstain