## Slide 1: Wide Scanning Requests and Responses
Date: 2012-05-17
Authors:

## Slide 2: Abstract
The very high throughput (VHT) enables transmission bandwidths of 20, 40, 80 and 160 MHz
  Scanning benefits also from use of larger bandwidths
The larger scanned bandwidth per operation reduces the number of scanning operations speeds-up the scanning
  This ensures initial link setup within 100ms

## Slide 3: Background
The discovery delay may be calculated:
  Number of scanning operations * time per scanning operation
    It is important to reduce the number of scanning operations as well as shorten the time per scanning operation
The 802.11ai has provided solutions to speed-up discovery in a scanned channel
  However, one channel is scanned at a time
The scanning messages may hint the next channel to be scanned

## Slide 4: Motivation, channels at 5 GHz
5 GHz has many channels to be scanned
  Some mechanism to reduce the number of scanning operations is needed to speed-up the scanning
The turquoise colour shows the channelization of the VHT STA
  VHT STA is capable to use 20, 40, 80 and 160 MHz transmission bandwidths as shown
140
136
132
128
124
120
116
112
108
104
100
165
161
157
153
149
64
60
56
52
48
44
40
36
IEEE channel #
20 MHz
40 MHz
80 MHz
5170
MHz
5330
MHz
5490
MHz
5710
MHz
5735
MHz
5835
MHz
Weather radars
only in US

## Slide 5: Recap, VHT transmissions
Each STA obtains TXOPs in its primary channel
  The channel status (busy /idle) of other channels does not affect to backoff calculation
Larger transmission bandwidth may be used, if CCA of the indicates channel idle a PIFS before the TXOP
The channels are taken into use on specific order
  The primary channel may be freely selected
  The primary channel defines the secondary20 and secondary40 channels as shown in previous slide

## Slide 6: Recap, VHT receptions
Each transmission has a preamble
  The preamble indicates the transmission bandwidth
  The transmission is receivable only if the receiver has the same primary channel as the transmitter
The STA obtains preambles only in its primary channel, i.e. Transmissions at other channels are not receivable
Preamble
Preamble
Preamble
Preamble
Data

## Slide 7: Recap, Non-HT Duplicate PPDU
802.11n defines non-HT duplicate PPDU
  The PPDU duplicates the 20 MHz wide MPDUs to larger bandwidth
  The PPDU is receivable for the whole transmission bandwidth
    The reception of the frame is the same as 20MHz PPDU
    The receiver need not to have the same primary channel as the transmitter
  VHT RTS and CTS frames are non-HT duplicate PPDU
Data
Data
Data
Data
Primary channel of the transmitter
Preamble
Preamble
Preamble
Preamble

## Slide 8: Use of Non-HT Duplicate PPDU in scanning
The Non-HT duplicate PPDU enables all STAs which primary channel is in transmission bandwidth
  The scanning request and scanning response may be communicated to larger banbwidth
  Larger bandwidth may be scanned in a single operation
Scan request
Scan request
Scan request
Scan request
Scan response
Scan response
Scan response
Scan response
Primary channel of scanning STA
Primary channel of responding STA

## Slide 9: Backward compatibility
Currently, Beacon and Probe Response frames are transmitted at primary channel
  Non-FILS capable STAs may be confused, if these frames are transmitted to other than primary channel
New management frame may be transmitted to larger bandwidth to enable
  The frame indicates the primary channel of the AP

## Slide 10: Advantages
More channels are scanned in a single scanning operation
  The discovery is faster, for instance 80 MHz may be scanned instead of 20 MHz
  The amount of scanning operations is reduced
    This makes discovery delays acceptable to FILS Requirements, i.e. initial link setup < 100ms
The mechanism is simple
  No new PPDU type is needed
  Transmission and reception details are already specified in 802.11ac

## Slide 11: Motion
Move to add the following text to the clause 6 of TGai Specification Framework document (11-12/0151r07):
” 802.11ai shall enable scanning frames transmission as non-VHT duplicate PPDUs at 20, 40, 80 and 160 MHz”