## Slide 1: Multiple Frequency Channel Scanning
Date: 2012-05-04
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon | Huawei Technologies Co., LTD. | 10180 Telesis Ct. Ste 165, San Diego, CA 92121 |  | younghoon.kwon@huawei.com
Yunsong Yang |  |  |  | 
Zhigang Rong |  |  |  | 

## Slide 2: Abstract
This document describes a technical proposal for TGai. In this proposal means are provided to speed-up AP/network discovery that reduces network congestion by reducing chance of Probe Request/Response transmission.
Related sections of the SFD (12/0151r7)
  6. Fast network discovery
    6.2 Passive scanning

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: AP Discovery: Scanning
2 scanning schemes defined in IEEE :
  Passive scanning
    A STA waits until next beacon frame comes.
    Based on received beacon frame, a STA discovers APs and initiates association.
    Pros: No additional air channel occupancy for AP discovery.
    Cons: As beacon frame is broadcasted once in a while (normally in the order of 100msec), it takes more time to discover an AP.
  Active scanning
    A STA transmits a Probe Request message including specific SSID that the STA wants to associate.
    Corresponding APs that receives Probe Request send back Probe Response message including needed BSS information.
    Pros: Fast AP discovery available.
    Cons: additional air channel occupancy required, especially for the case wildcard SSID is included in Probe Request message. (In this case, every AP needs to send back Probe Response message.)

## Slide 5: AP Discovery: Scanning
Improvement on passive scanning schemes [1]
  Use of FILS beacon
    Define a very short beacon (FILS beacon) to advertise AP, transmit it much more frequently.
    FILS beacon only contains several necessary element for discovery.
    FILS beacon will not replace the traditional beacon frame, it will be sent much more frequently between traditional beacons.

## Slide 6: Multiple Channel Scanning
There are multiple frequency channels and there may be multiple APs in each frequency channel.
  Even though FILS/short beacon can reduce inter-beacon time, to scan the short beacon of all APs in all frequency channels takes quite amount of time.
  If there are N frequency channels, and each AP’s inter-beacon interval is T, the total FILS beacon scanning time can be up to N*T, which can be easily over 100msec.

## Slide 7: Multiple Channel Scanning
Example scenario
  3 frequency channels
  3 APs in each frequency channel
Freq. ch. 1
Freq. ch. 2
Freq. ch. 3
Inter FILS beacon duration
AP1
AP1
AP2
AP2
AP2
AP3
AP1
AP3
AP1
AP3
AP4
AP4
AP4
AP5
AP5
AP5
AP6
AP6
AP6
AP9
AP7
AP7
AP7
AP7
AP8
AP9
AP8
AP9
AP8
Total FILS beacon scanning duration

## Slide 8: Proposed Recommendation
Proposed features
  Time to earliest next FILS beacon among all APs in all frequency channels is indicated in FILS beacon, such that STAs can hop to right frequency channel after finishing scanning of current AP.
  Short beacon transmission time from multiple APs in same frequency channel is arrange to be closely located together, such that scanning of one frequency channel can be done in short time and STAs can switch to other frequency channel.

## Slide 9: Proposed Recommendation
Standard impact
  Indication of time to earliest FILS beacon transmission and corresponding frequency channel in FILS beacon
  STA’s report on FILS beacon transmission timing information of nearby APs including APs in different frequency channels
  Availability of FILS beacon transmission time shift and/or interval change with minimum confusion on associated STAs

## Slide 10: Proposed Recommendation
Example scenario using proposed recommendations
  3 frequency channels
  3 APs in each frequency channel
Freq. ch. 1
Freq. ch. 2
Freq. ch. 3
Inter FILS beacon duration
AP1
AP2
AP3
Total FILS beacon scanning duration
AP1
AP2
AP3
AP1
AP2
AP3
AP1
AP4
AP5
AP6
AP4
AP5
AP6
AP4
AP5
AP6
AP7
AP8
AP9
AP7
AP8
AP9
AP7
AP8
AP9

## Slide 11: Benefits
Reduction of passive scanning time
Reduction of Probe Request/Response packet transmission occurrence
Reduction of overall AP discovery time

## Slide 12: Straw Poll 1
Do you agree to add the sentence to section 6.2 Passive Scanning of TGai SFD, 12/0151r7.
  “FILS beacon should include information on time to earliest next FILS beacon among nearby APs and corresponding frequency channel.”?
Yes:
No:
Abstain:

## Slide 13: Straw Poll 2
Do you agree to add the sentence to section 6.2 Passive Scanning of TGai SFD, 12/0151r7.
  “A non-AP STA can report FILS beacon transmission timing information of nearby APs including APs in different frequency channels.”?
Yes:
No:
Abstain:

## Slide 14: Straw Poll 3
Do you agree to add the sentence to section 6.2 Passive Scanning of TGai SFD, 12/0151r7.
  “AP can shift FILS beacon transmission time and/or change FILS beacon transmission interval without ambiguity on associated STAs.”?
Yes:
No:
Abstain:

## Slide 15: References
[1] IEEE802.11-12/0042r4, AP discovery with FILS beacon