## Slide 1: Alternative Mesh Path Selection
Date: 2012-07-14
Authors:

## Slide 2: Abstract
The 802.11 Mesh standard provides the hooks to support a variety of path selection protocols and link cost metrics. Different network environments and applications are best supported by different path selection protocols and link metrics. TRILL, as a proactive link state based path selection protocol, would be the basis for a useful alternative path selection protocol to HWMP.

## Slide 3: Contents
Why
Background
TRILL
Process

## Slide 4: Why Should 802.11 Be Interested?
802.11 Mesh depends on a Path Selection and Link Metric protocol to determine how to forward frames. Different Path Selection protocols are best for different types of meshes.
Meshes differ along various dimensions such as:
  Percent of pairwise multi-hop paths that will actually be used.
  Density, dimensionality, and dynamism of mesh station locations.
  Can mesh path selection be entirely local to an 802.11 mesh or should it be possible to optimize path selection on a wider scale possibly including multiple meshes and intervening nets?
  Should mesh stations have a global view of the mesh topology?

## Slide 5: Why Should 802.11 Be Interested?
There is only one Path Selection protocol specified in the 802.11 Mesh standard.
But mesh is designed so that other Path Selection protocols can be deployed and agreed to by mesh stations.
There are successful 802.11 mesh products, but they tend to use propriety Path Selection protocols due to problems with the Path Selection protocol in the 802.11 standard.

## Slide 6: Why IETF TRILL?
The IETF TRILL protocol would provide a new type of 802.11 mesh Path Selection extending the utility of 802.11 mesh.
“The TRILL WG has expressed interest in collaborating with IEEE 802.11 to write a specification to use components of TRILL for path selection in IEEE 802.11s.”
  – IETF Chair Liaison to IEEE 802.1, 10 May 2012
Donald Eastlake, Co-Chair of the TRILL Working Group was formerly Chair of the 802.11 Mesh Networking Task Group.
It would provide a worked example of building on an 802 protocol using external interfaces in support of the 802 JTC1 SC’s efforts.

## Slide 7: Contents
Why
Background
TRILL
Process

## Slide 8: 802.11 Mesh Path Selection

## Slide 9: 802.11 Mesh Path Selection
802.11 Mesh is designed to support multiple Path Selection protocols and multiple Link Metrics.
  All Mesh STAs in an MBSS (Mesh BSS) must use the same Path Selection protocol and Link Metric.
  The default Path Selection protocol and the only one specified in the 802.11 Standard is HWMP (Hybrid Wireless Mesh Protocol).
    Typically mesh paths are multi-hop. After each hop the receiving Mesh STA uses path selection to determine the next hop, if further forwarding is required. Path selection uses the link metric to decide what path is best.
  The default Link Metric and the only one now specified in the 802.11 Standard is the Airtime link metric which estimates the amount of airtime to transmit an 8192 data bit frame.

## Slide 10: HWMP Path Selection Protocol
Hybrid Wireless Mesh Protocol: “Hybrid” because it uses two techniques:
  Proactively building spanning trees rooted at portals or other configured roots.
  Reactively finding paths to a specific destination when initiated by a source Mesh STA by processing flooded request frames and the reply from the destination. This part of HWMP is based on AODV (Ad-hoc On Demand Distance Vector).
Both of the above are Distance Vector techniques (see later slides).

## Slide 11: Types of Path Selection
Pros and Cons:
      These are very general characterizations!
Distance Vector
  Path selection is based on local view.
  Lower storage and computation cost at each node.
  Local cost calculation must be done before propagating changes.
Link State
  Path selection is based on a global view of the network permitting more intelligent decision making.
  Requires more storage and process at each node.
  Topology information update can be propagated after trivial check that is has not been previously received.

## Slide 12: Types of Path Selection
Pros and Cons:
      These are very general characterizations!
Reactive: Paths determined when needed.
  Typically a start up delay for a pair of nodes to communicate.
  Less overhead if only a few pairs of nodes communicate.
Proactive: All paths determined and maintained.
  No delay for a pair of nodes to communicate
  Less overhead if many pairs of nodes communicate.
Different mesh environments and/or applications are best served by different Path Selection protocols.

## Slide 13: 802.11 Mesh Use Cases
The use cases motivating the development of 802.11s were as follows:
  Residential
  Office
  Campus/ Community/ Public Access Network
  Public Safety / Military
  IEEE 802.11 TGs Usage Models 11-04-0662-16-000s-usage-models-tgs.doc

## Slide 14: Contents
Why
Background
TRILL
Process

## Slide 15: IETF TRILL WG
TRILL is a Proactive Link State Protocol
TRansparent Interconnection of Lots of Links
  Current TRILL WG Charter
    http://www.ietf.org/dyn/wg/charter/trill-charter.html
  Co-chaired by
    Erik Nordmark, Cisco Systems
    Donald E. Eastlake 3rd, Huawei Technologies
  See also
    http://www.postel.org/rbridge/

## Slide 16: TRILL
The IETF TRILL Protocol is built on the IS-IS link state protocol. Devices that implement TRILL are called TRILL Switches or RBridges (Routing Bridges).
  TRILL provides transparent routing. It delivers the same frame as sent.
Basically a simple idea similar in structure to 802.11 mesh:
  Encapsulate native frames in a transport header providing a hop count.
  Route the encapsulated frames using link state routing.
  Decapsulate native frames before delivery.

## Slide 17: History
The use of TRILL for 802.11s path selection was discussed early. For example, during the following presentation made in 2004: 11-04/1462r0 “Routing and RBridges”
Early versions of the 802.11s draft included a link state routing protocol: RA-OLSR (Radio Aware – Optimized Link State Routing).
  For a brief period, HWMP was mandatory and RA-OLSR was optional in the draft but the forces to simplify the draft won and RA-OLSR was removed from the 802.11s draft.

## Slide 18: Some TRILL Features
Supports multi-access links – and most wireless links are inherently multi-access.
Pro-actively provides least-cost paths with zero configuration. Supports multi-pathing.
Unicast forwarding tables at transit RBridges scale with the number of RBridges, not the number of end stations. Only edge RBridges need to learn end station (MAC) addresses.
Supports frame priorities and VLANs.
Has a poem (see backup slides)

## Slide 19: Peering Between/Thru Meshes
If 802.11 meshes using TRILL are connected by bridged LANs, those TRILL instances can peer with each other and form a unified campus, picking least cost paths, for example from A to B and from C to D below.
C
D
MBSS
MBSS
MBSS
A
B
802.3 LAN
802.3 LAN
802.3 LAN
B1
B2

## Slide 20: TRILL for Mesh Cases
Cases involving communication between many different pairs of mesh stations in a mesh, such as between between people in an independent group or between top-of-rack switches.
Cases where a global least cost path is needed involving more than one mesh or optimization over both mesh path choices and wired TRILL campus path choices.
Cases where a global knowledge of the mesh topology is useful to mesh stations.

## Slide 21: TRILL Standardization Status
Some standards track RFCs that have issued:
  6325, “RBridges: TRILL Base Protocol Specification”
  6326, “TRILL Use of IS-IS”
  6327, “RBridges: Adjacency”
  6361, “TRILL over PPP”
Base Protocol Code Points Allocated
  Ethertypes: TRILL = 0x22F3, L2-IS-IS = 0x22F4
  Multicast MACs: 01-80-C2-00-00-40 to 01-80-C2-00-00-4F
  NLPID: 0xC0; IS-IS code points (see RFC 6326)
TRILL has an open source software implementation for Solaris and one in progress for Linux.

## Slide 22: Contents
Why
Background
TRILL
Process

## Slide 23: Suggested Process
0. Straw polls at May 2012 802.11 Interim Meeting:
  Interest in the concept of the TRILL WG doing this: 53 to 2
802.11 transmits a liaison to the IETF TRILL WG.
TRILL gets an item added to its Charter.
Suggested methods of collaboration:
  Participation by 802.11 mesh knowledgeable individuals in the TRILL WG mailing list and TRILL WG meeting.
  Co-location of one or more TRILL WG meetings at 802.11 meetings. (first at January 2013?)
Estimated completion: January 2014?

## Slide 24: TRILL Work to Support 802.11 Mesh
It is likely that the following work on TRILL would be needed:
  Optimization of link state flooding.
    Useful for any richly connected TRILL campus.
  Encoding of TRILL frames in 802.11 mesh.
    TRILL currently standardized over 802.3 and PPP. Drafts exist for TRILL over IPv4/IPv6 and MPLS.
  Optimization of multi-destination data distribution.
  Mapping of Airtime Link Metric values to TRILL link metric.
    This is a simple numeric mapping. Perhaps ( ca * 25 * 104 ).

## Slide 25: Draft Liaison Envelope
To: Donald E. Eastlake 3rd and Erik Nordmark, IETF TRILL WG Co-Chairs
CC: Dorothy Stanley, IEEE 802.11 Liaison to the IETF
Ralph Droms and Brian Haberman, IETF Internet Area Co-Directors
Dan Romascanu, IETF Liaison to IEEE SA
<Body of Liaison from next slide>
Signed: Bruce Kramer, Chair 802.11 WG

## Slide 26: Liaison Text
We understand that there is interest in the IETF TRILL Working Group developing, with collaboration as mutually convenient from 802.11, a variation of the TRILL protocol for use as an 802.11 mesh path selection protocol.
802.11 would encourage the TRILL WG to proceed with this work.
The IEEE 802.11 standard is designed to support a variety of path selection protocols and link cost metrics, although only one of each can be in use at one time in an 802.11 mesh. Thus such an alternative path selection protocol would not be exclusive. If 802.11 code point allocation is required to support such a TRILL based mesh path selection for mesh, 802.11 does have a mechanism by which such code points could be allocated to the TRILL WG, but approval of such allocations is not guaranteed.
Looking forward to collaborating,

## Slide 27: Liaison Motion
Motion:
Request the IEEE 802.11 WG chair transmit the liaison on slide 26 of “11-12-0621-03-0000-alternative-path-selection-protocol.pptx” to the IETF TRILL WG and any additional persons he deems appropriate.
Moved: <name>, Seconded: <name>
Result: y-n-a]

## Slide 28: References
IEEE 802.11 TGs Usage Models, 11-04-0662-16-000s-usage-models-tgs.doc
IEEE Std 802.11-2012, “… Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 6 February 2012
IETF RFC 3561, “Ad hoc On-Demand Distance Vector (AODV) Routing”, July 2003, http://www.ietf.org/rfc/rfc3561.txt
IETF RFC 6325 (TRILL), “RBridges: Base Protocol Specification”, July 2011, http://www.ietf.org/rfc/rfc6325.txt
IETF Liaison to IEEE 802.1, 10 May 2012, https://datatracker.ietf.org/liaison/1155/

## Slide 29: Back Up Slides

## Slide 30: Airtime Link Metric
The Airtime Link Metric is based on the estimated amount of channel resources used to transmit a 8192 bit frame over the specific link.
  O = frame overhead, depend on PHY
  Bt = 8192 bits
  r = data rate in Mb/s
  ef = frame error rate for a 8192 bit frame

## Slide 31: Types of Path Selection
Distance Vector versus Link State:
      These are very general, basic descriptions!
Distance Vector
  Each node locally announces that it is a zero cost route to itself.
  Each node trusts what its neighbors say about their cost to various destinations, picks the best for each destination, adds the cost to that neighbor, and believes the sum is its cost to that destination through that neighbor.
Link State
  Each node finds its neighbors and the one hop cost to each neighbor. This data is reliably flooded to all nodes in the network.
  From this network wide neighbor data, each node can calculate the global topology and things like the optimum next hop.

## Slide 32: Peering and Layers
TRILL operates at layer 2 ½. TRILL switches will peer with each other, both becoming part of a unified TRILL campus, through bridges but not through routers.
Layer 3:
TRILL Layer:
Layer 2:
Routers (plus servers and other end stations)
TRILL Switches
Bridges

## Slide 33: Peering and Layers
Router /End Station
Router /End Station
Bridge
Peers
Non-Peers
Bridge
Bridge
Peers

## Slide 34: Peering and Layers
Peers
Peers
Peers
Router /End Station
Router /End Station
TRILL Switch
TRILL Switch
Bridge(s)
TRILL Switch
Bridge(s)
Non-Peers

## Slide 35: TRILL Open Source Status
Oracle: TRILL for Solaris
  http://hub.opensolaris.org/bin/view/Project+rbridges/WebHome
TRILL Port to Linux (in process): National University of Sciences and Technology (NUST),
Dr. Ali Khayam
Islamabad, Pakistan
  http://www.wisnet.seecs.nust.edu.pk/people/~khayam/index.php

## Slide 36: Algorhyme V2
I hope that we shall one day see
A graph more lovely than a tree.
A graph to boost efficiency
While still configuration-free.
A network where RBridges can
Route packets to their target LAN.
The paths they find, to our elation,
Are least cost paths to destination!
With packet hop counts we now see,
The network need not be loop-free!
RBridges work transparently,
Without a common spanning tree.
- By Ray Perlner