## Slide 1: Preamble Format For 1 MHz Beamforming
Date: 2012-05-14
Authors:

## Slide 2: Abstract
This document proposes a preamble for the 1 MHz mode which supports Single-User Beamforming (SU-BF).

## Slide 3: Background
Document 12/371r0 proposed adoption of the following transmit beamforming sections from IEEE P802.11ac™/D2.0:
  8.4.1.46 VHT MIMO Control field
  8.4.1.47 VHT Compressed Beamforming Report field - contents of feedback frame
  8.4.1.48 MU Exclusive Beamforming Report field - contents of MU frame
  9.31.5 VHT sounding protocol
  22.3.11 and its subsections: SU-MIMO and MU-MIMO Beamforming
However, the 1 MHz mode has a different preamble and it is not clear how transmit beamforming will be supported.

## Slide 4: Beamforming for 1 MHz
The 1 MHz mode will likely be used for low-cost sensor applications, where the STAs may have only one or two antennae.
Beamforming to low-cost sensor STAs is good method for increasing the rate/range as most of the complexity is at the AP.
The 1 MHz mode should include a minimal overhead preamble format which supports SU-BF.

## Slide 5: Proposed Single User Preamble Format
Similar to the 802.11n GF preamble.
Supports beamforming for 1 MHZ Single-User case without added overhead of a SIG-B symbol.
Supports Beamforming without creating hidden nodes.

## Slide 6: Conclusion/Recommendations
The current specification framework does not have a preamble mode for 1 MHz that supports SU-BF.
Adopting a preamble format that supports SU-BF would be very beneficial for 1 MHz systems.

## Slide 7: Straw Poll
Do you think that a 1 MHz preamble mode that supports SU-BF should be specified?
  Yes
  No
  Abstain