## Slide 1: Block ACK Transmission
Date: 2012-09-12
Authors:

## Slide 4: Introduction
Block ACK transmission issue in IEEE 802.11ah, where asymmetric transmissions will likely to prevail [1]
  AP to STN (Downlink) vs STN to AP (Uplink)
  Asymmetric data rates in uplink and downlink [2]
STN has more constraints as opposed to AP
  Transmission power (power amplifier etc)
  Capability
    Transmission capability (1 MHz vs AP with 2 MHz and beyond)
    Functionalities (AP may serve different types STN)
Short Block ACK limitations
  Basic Block ACK only, limited to at most 8 bits or 16 bits [baseline: 128octets]
  No fragments
Use Cases: Extended range Wi-Fi, Sensors and meters
Slide 4

## Slide 5: Problems for Normal ACK
ACK transmission [1]
  STN can receive data but AP may not receive ACK
  Simple Fix: allow STN to use lower MCS for ACK
Short ACK
  Short ACK works with lowest MCS in SIG
Slide 5

## Slide 6: Problem for Block ACK
Block ACK
  Improves channel efficiency by aggregating several ACKs
Problem in asymmetric cases: Data & Block ACK phase
  Multiple downlink data MPDUs use lower MCS
  Not efficient use of channel
  BlockAck payload can be large
    ~ 214 bytes
  Short Block ACK is limited
Use Cases
  Use Case 3 : Extended range Wi-Fi
  Use Case 1: Sensors and meters
Slide 6

## Slide 7: Example: AMPDU Transmissions and Block Ack
Slide 7
A-MPDU at MCS7
AP
STN
BA at MCS7
X
A-MPDU at MCS3
(inefficient DL)
BA at MCS3

## Slide 8: Example: AMPDU Transmissions and Block Ack
AP
STN
A-MPDU at MCS7
(efficient DL)
BA at MCS3
Slide 8

## Slide 9: References
[1] 802.11-12/0400r0 I2R, ACK transmission
[2] Novarum Inc. Report, 2010 “Guidelines for Successful Large Scale Outdoor Wi-Fi Networks”
[3] 802.11-12/0645r1 Open-Loop Link Adaptation
Slide 9

## Slide 10: Straw Poll
Do you agree that a STA may transmit an immediate Block ACK with lower (or more robust) modulation and coding rate than that of the eliciting AMPDU?
Slide 10