## Slide 1: Block ACK Transmission Follow up
Date: 2012-11-8
Authors:

## Slide 4: Introduction
In 11ah, Block ACK from STN may not reach AP
  AP may transmit at higher power and better off in capability
  STN can receive Data but its Block ACK may not reach AP
Motion Approved in IEEE Sept 2012
  STN may use same or lower MCS (more robust) for BA frames than eliciting A-MPDUs
Remaining Issue
  Duration field cannot be computed readily
Proposal
  Negotiate degree of asymmetry
Slide 4

## Slide 5: Proposal: negotiate degree of asymmetry
Basic idea
  Assumption: degree of asymmetry between uplink and downlink is constant
  Figure out the degree (and hence uplink and downlink MCS difference) prior to BlockAckReq and BlockAcks, e.g., through Association & Authentication frames, or other frames.
  Indicate the MCS uplink and downlink configuration difference at BA setup phase
BA setup phase (ADDBA)
ADDBA request
  STN records successful downlink MCS from AP
ADDBA response
  STN informs AP the preferred MCS for downlink
  AP notes uplink MCS used by STN

## Slide 6: Implementation Example 1
STN already figured out the difference between downlink and uplink with previous frames such as association and authentication phase
Indicate difference to each other at ADDBA phase
ADDBA Request
ShortACK
Config “A”: MCS2
AP
STN
STN notes “config A”
ADDBA Response
ShortACK
Config “B” =
Config “A” – difference:
MCS1
AP notes “config B”
for uplink, and record the difference
STN notes “config B” for uplink, and confirms AP has recorded the difference
AP notes “config A” for downlink
(indicate Config “A”)

## Slide 7: Implementation Example 2
No such prior knowledge
ADDBA Request: STN records successful Downlink MCS
ADDBA Request
ADDBA Request
X
ADDBA Request
ShortACK
Try
Config “A”:
Lower MCS
Try lower MCS
(config “B”)
ShortACK
X
X
ADDBA Response
STN may send ADDBA Response
AP
STN
STN notes “config A”

## Slide 8: Implementation Example (cont’d)
ADDBA Response: STN indicates to AP the preferred MCS for downlink (config “A”)
  (*) Could be a new field, part of status code, or dialog token
ADDBA Response (*)
ADDBA Response (*)
X
X
ADDBA Response (*)
ShortACK
AP
STN
Try same MCS as config “B”
Try lower MCS
(config “C”)
Config “D”:
lower MCS
AP notes difference between “config A” and “config D”
STN notes difference between “config A” and “config D”
May skip using open-loop link adaptation [3]

## Slide 9: Summary
Proposal | Summary | Pros
Negotiate Degree of Asymmetry | STA indicates MCS difference to AP at ADDBA (mgmt) AP uses MCS difference to calculate DUR | No new frames defined AP only needs to get MCS difference from STA

## Slide 10: Straw Poll
Do you support to include in SFD that the STA informs AP the preferred MCS for downlink (indication format TBD) in the ADDBA response and AP notes uplink MCS used by STA and records the MCS difference for computing the duration of an immediate BA
Slide 10