## Slide 1: Low-rate compatible BCC for IEEE 802.11ah lowest MCS
Date: 2012-05-06
Authors:

## Slide 2: Abstract
We propose an efficient ¼-rate compatible binary convolutional code (BCC) for IEEE 802.11ah lowest MCS on the 1 MHz mode.
It is compatible with the original half-rate BCC, and just introduces small complexity overhead.
It is much better than the new MCS0- 2x Repetition mode, and then SNR gain is up to 0.85 dB at PER=0.1 .
.

## Slide 3: Overview
According to the document 1294r0[1], the group adopted the following:
    An 802.11ah STA shall support reception of 1 MHz and 2 MHz PHY transmissions.
Subsequently, the document 1482r0[2] proposed that an MCS0-Rep2 mode in 1MHz is needed for good indoor coverage.
The document 1484r0[3] proposed the 11ah data transmission flow, both for regular MCS and for a new MCS0- 2x Repetition mode .
An improved ¼-rate BCC of the data transmission flow for 1 MHz mode is proposed, and obtains much better performance than the MCS0-2x Repetition mode with only small complexity overhead.

## Slide 4: MCS0 ¼-rate BCC Mode in 1MHz
We propose a ¼-rate BCC mode that just imposes minimal Tx and Rx design change from regular MCSs.
  The first two generator polynomials of the compatible ¼-rate BCC shall use the original generator polynomials g0=1338 , g1=1718,
  The other two new generator polynomials are g2=1178 , g3=1658.
¼ -rate compatible Convolutional encoder

## Slide 5: MCS0 ¼-rate BCC Tx Flow
Scrambler
Interleaver
BPSK
mapper
Spatial Mapping
New ¼ rate BCC
FEC
IFFT
:
:
IFFT
GI &
Window
Analog
& RF
GI &
Window
Analog
& RF
Interleaver parameters are the same as regular MCS0
Ncol = 8

## Slide 6: Performance in AWGN
¼-rate BCC obtains 0.7 dB SNR gain at PER=0.1 compared with Rep2x.
New ¼-rate BCC Parameters | Value
Information bits | 516
Code Rate | 1/4
Modulation Type | BPSK
Bandwidth | 1.0 MHz
Number of OFDM | 86
FFT | 32
number of data subcarriers | 24
Subcarrier Bandwidth | 31.25 kHz

## Slide 7: Performance in SCM-UMa
New ¼-rate BCC obtains 0.85 dB and 1.2 dB SNR gain at PER=0.1 compared with MRC and EGC Rep2x schemes, respectively.
New ¼-rate BCC Parameters | Value
Information bits | 516
Code Rate | 1/4
Modulation Type | BPSK
Bandwidth | 1.0 MHz
Number of OFDM | 86
FFT | 32
number of data subcarriers | 24
Subcarrier Bandwidth | 31.25 kHz

## Slide 8: Complexity Discussions
BCC Viterbi decoder complexity depends mainly on the state number.
  ¼ -rate BCC has the same state number 64 and Trellis diagram as the ½-rate BCC, and the only difference lies in the branch probability computation.
  Number of additions and multiplications in different schemes.(assumptions: l information bits+Viterbi decoding)
    For EGC Rep2x, 134*l additions
    For MRC Rep2x,134*l additions and 4*l multiplications
    For ¼-rate BCC, 176*l additions
    Conclusion: The new complexity is almost as the MRC Rep2x

## Slide 9: Conclusions
  An improved ¼-rate BCC data transmission flow for 1 MHz mode is proposed.
  It obtains much better performance than the MCS0-2x Repetition mode, which is up to 0.85 dB SNR gain at PER=0.1
  It is compatible with the original half-rate BCC, and just introduces small complexity overhead.
  It is suitable for the case where the transmit power is strictly restricted.

## Slide 10: References
[1] 11-11-1294-00-00ah-spec-framework-text-of-11ah- bw-modes
[2] 11-11-1482-00-00ah-preamble-format-for-1-MHz
[3] 11-11-1484-00-00ah-11ah-phy-transmission-flow