## Slide 1: Prioritized PS-Polls
Date: 2012-5-15
Authors:

## Slide 2: Abstract
This contribution suggests allowing PS STAs to transmit PS-Polls at different priority levels. This is achieved by having a TIM encoding that conveys different STA groups, and assigning channel-access priority to each group
The objective is to reduce PS-Poll collisions when a large number of PS STAs are associated with an AP

## Slide 3: Background
In 11ah, there can be a large number of STAs associated with each AP; many of them operate in PS mode
Upon waking up from doze and seeing its bit in the TIM being set, an STA will send a PS-Poll to AP
PS-Poll collisions will happen when several STAs transmit PS-Polls shortly after a TIM
PS-Poll collisions increase latency/drop-rate for buffered BUs at AP

## Slide 4: Observation 1
Not all STAs with set TIM bits are ready to transmit PS-Polls:
  Different STAs have different Listen Interval values that determine how often they listen to the Beacon frames
  For each STA, the longer the TIM bit has been set without PS-Poll being received at AP, the more likely that the STA will attempt to transmit a PS-Poll following the next TIM
=> AP may compare the likelihood of different STAs being ready to transmit PS-Polls and use that to coordinate their transmissions

## Slide 5: Observation 2
Not all buffered BUs at AP need to be delivered to STAs with the same latency/drop-rate requirements:
  Different applications, e.g., real-time vs. best effort, have different QoS constraints
  Within one application, there are certain messages with more stringent requirements than others
=> Based on QoS requirements of the buffered BUs, AP can coordinate PS-Poll transmissions from the corresponding STAs

## Slide 6: Main Idea – Prioritized PS-Polls
Define a mechanism that allows AP to prioritize PS-Polls transmissions by:
  Indicating different STAs groups within each TIM
  Associating with each STA-group within the TIM a channel-access priority
  An awake STA with buffered BUs transmits PS-Poll according to the given channel-access priority of its indicated group

## Slide 7: Indicating STA Groups within TIM
Approach 1: using a fixed k-bit field after each set TIM bit:
Approach 2: mixed use of explicit AID listing and TIM bitmap:

## Slide 8: Assigning Priority to PS-Polls
Each STA-group within a TIM can be given an access priority to transmit PS-Polls; the priority can be a combination of:
  Interframe Space, e.g., AIFS
  Contention Windows, e.g., CW, Cwmin, CWmax
  Time Allowance, i.e., different groups of STAs are allowed to transmit PS-Polls in different slots/periods
  Retry Limit, i.e., set the maximum number of PS-Poll retries within a beacon interval for different STA groups
=> Can be further studied

## Slide 9: Summary
In 11ah, with a large number of power-save STAs, PS-Poll collisions increase latency and drop-rate for buffered BUs
AP has knowledge of how ready/urgent each STA can/should transmit PS-Poll
=> We propose that AP indicates through TIM the different groups of STAs (that have buffered BUs) and gives different channel-access priorities to different groups
The implementation details are TBD

## Slide 10: Straw Poll 1
Do you agree that, to reduce collisions, PS-Polls from different STAs can be transmitted using different channel-access priorities?
  Y:
  N:
  A:

## Slide 11: Straw Poll 2
Do you agree that PS-Poll priority can be indicated in the TIM through STA grouping, as explained in Slide 6?
  Y:
  N:
  A: