## Slide 1: Operating Channels Information
Date: 2012-07-19
Authors:

## Slide 2: Abstract
This submission proposes inclusion of concept to SFD. It’s relating to AP discovery.
It’s not a new idea. Some contributors proposes similar concepts in the past meetings.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Motivation
APs/STAs operating multi-bands (2.4GHz/5GHz) are getting common in these days.
It takes longer time for these multi-bands operating STAs to complete searching all the channels to find a desired AP.
It’s not allowed for STAs to execute Active scanning in some 5GHz channels because of radio regulations. But Passive scanning is time consuming.
Uses of 5GHz channel are highly demanded because of congested situation in 2.4GHz band.
Informing operating channels may be solution for Fast AP discovery in 5GHz bands.

## Slide 5: Recap of the past proposal 11/1510r0 (FOKUS)
5GHz part operates “as known”  Master device w/ channel sensing
2.4GHz part asks 5GHz part which channel are in use (or is told)  „real time synchronization of that shared knowledge“
Non-AP STA conducts active scanning in 2.4GHz band  receives valid 5GHz channel list
Option a) verify this information via passive scanning on specific 5GHz channel
Option b) directly start link set-up on 5GHz channel
Continue w/ regular 5GHz operation
Single Device / Box
2.4 GHz AP
5 GHz AP
Internal Mgmt. Not accessible by user
Non-AP STA 2.4 & 5 GHz operation
Active scan  receive 5GHz channel list
Optional passive scan on channel for verification
Link-Set Up
Non-AP STA is under the control of the master (single device)
Open issues:
  Enabling signal is not received in 5GHz channel
  Different propagation characteristics of different frequency bands  larger tranmission range of 2.4GHz as compared to 5GHz

## Slide 6
Motion
Move to add the following clause to the TGai SFD under the "General" Section:
Mover: Second:
Yes: No: Abstain:
A FILS STA should be capable of announcing all of its operational channels that the STA is the Master of. One possible approach to consider, is to include information in the neighbor report element that the STA sending this information is the Master of the channel referenced in the neighbor report. A STA receiving this information is immediately enabled for accessing the channels under the AP issuing the neighborhood report is the Master of.
(Note: Maybe a "time window" in which this enablement is "valid" has to be specified. A STA should not be able to immediately access a channel indicated under the control of a master if the neighborhood report had been received hours ago).

## Slide 7: References
10/922r2 Achievable gains in AP Discovery (FOCUS)
11/1064r0 Supported Operating Band (Vodafone/Nokia)
11/1510r0 Enablement in 5GHz for FILS (FOCUS)
12/0013r0 Proposal of Fast AP Discovery (KDDI)
12/0546r0 Fast Passive Scan for FILS (China Mobile)