## Slide 1: FILS STA Support for QoS, HT and VHT?
Date: 2012-07-04
Authors:

## Slide 2: Abstract
The mandatory capabilities of the FILS STA have not been defined or discussed properly in the group.
The presentation is asking: Are all FILS STAs:
- QoS capable
- HT capable
- VHT capable

## Slide 3: Background
802.11ai task group defines enhancements that are mandatory or optional for FILS capable devices
  The enhancements modify MAC-layer or authentication procedures of the STA
  The enhancements may be implemented with any PHY (DSSS, OFDM, HT or VHT PHY)
    Many broadcast frames should be receivable by all STAs in the coverage area

## Slide 4: QoS support ?
QoS support is assumed for 802.11ae Prioritization of management frames
Many presentations have been tuning EDCA and Access Categories (ACs); they have targetted to lower delays and to prioritize FILS related frames transmission
If all STAs are QoS STAs, the priorization schemes are simplified and reliability of the FILS is improved
Recommendation is that all FILS STAs are QoS Capable, i.e. QoS STA

## Slide 5: HT Support ?
HT Support enables STA to use A-MPDU, A-MSDU aggregations, block ack, PSMP, MIMO transmissions, 40 MHz transmission bandwidth, etc.
None of these features seem to directly impact to FILS STA operation
  Of course, having support and capability for these operations would enable better operation in some scenarios
  Also all HT STAs are QoS STAs
How does group feel, should FILS STA be HT STA?

## Slide 6: VHT Support ?
VHT support enables 80 MHz (or 160 MHz ) transmission banwidth, new MCS schemes, improvements to RTS CTS signaling, new MIMO transmission schemes, etc.
None of these features seem to directly impact to FILS STA operation
  Of course, having support and capability for these operations would enable better operation in some scenarios
  Also all VHT STAs are HT STAs
How does group feel, should FILS STA be VHT STA?

## Slide 7: Motion 1
Move to add the following text to the clause 6 of TGai Specification Framework document (11-12/0151r08):
” FILS STA is QoS STA”

## Slide 8: Motion 2
Move to add the following text to the clause 6 of TGai Specification Framework document (11-12/0151r08):
” FILS STA is HT STA”

## Slide 9: Motion 3
Move to add the following text to the clause 6 of TGai Specification Framework document (11-12/0151r08):
” FILS STA is VHT STA”