## Slide 1: Scanning from Specific Channel
Date: 2012-07-13
Authors:
Name | Affiliations | Address | Phone | email
Ping Fang Ji Chen | Huawei Technologies Co., Ltd. | Bldg 7, Vision Software Park, Road Gaoxin Sourth 9, Nanshan District, Shenzhen, Guangdong, China, 518057 | +86 755 36839346 | ping.fang@huawei.com ji.chen@huawei.com
Dapeng Liu | China Mobile | 32 Xuanwumen West Street Beijng, Xicheng District, 100053 China |  | liudapeng@chinamobile.com
Katsuo Yunoki | KDDI R&D Laboratories | 3-10-10 Iidabashi, Chiyoda-ku, Tokyo, Japan |  | yunoki@kddilabs.jp

## Slide 2: Abstract
This contribution describes a technical proposal for Tgai AP discovery. In this proposal, channel priority per SSID is proposed. STA scans for a AP starting from a specific channel calculated from the target AP’s SSID, to improve the AP discovery efficiency. And channels can be decided by AP to have different priorities as its working channel.

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Problem Statement
In above examples, the scanning time T1 and T2 in CH1 and CH2 are wasted.
If a AP randomly selects a working channel, and STA scan for a AP starting with a randomly chosen channel, time can be wasted before the STA can find the target channel.
AP in CH3
STA
T1
T2
T3
Probe Request in CH2
Probe Request in CH1
Probe Request in CH3
Probe Response in CH3
Active Scan case
AP in CH3
STA
T1
T2
T3
Listen in CH2
Listen in CH1
Listen in CH3
Beacon in CH3
Passive Scan case

## Slide 5
AP selects a specific channel as its working channel with higher priority per SSID.
  The specific channel could be a channel calculated from the AP’s SSID.
STA scan for the target AP starting from the specific channel.
  The specific channel is a channel calculated from the AP’s SSID, with the same rule as used by AP.
Proposed Solution 1

## Slide 6
STA starts to scan from a specific channel, then the target AP could be found within T1.
Proposed Solution 2
AP in CH3
STA
T1
Probe Request in CH3
Probe Response in CH3
Active Scan case
AP in CH3
STA
T1
Listen in CH3
Beacon in CH3
Passive Scan case

## Slide 7
What if the specific channel is not available when AP select its working channel?
  AP could select the second, third, fourth, … specific channel, as its working channel.
  The second, third, fourth, … specific channel could be decided from the AP’s SSID.
What if the target AP can not be found in the specific channel by a STA?
  STA could continue the scan in the second, third, fourth, … specific channel.
  The second, third, fourth, … specific channel could be calculated from the target AP’s SSID, with same rule as used by AP
Error handling

## Slide 8: Summary
AP selects a specific channel as its working channel according to its SSID, and STA scan for the target AP start from this specific channel to speed up the AP/network discovery.

## Slide 9: Q&A-1
Q: How will this work for an AP with multiple SSIDs?
For this kind of AP with multiple SSIDs, you can decide the working channel based on one of the SSIDs, so to speed up AP discovery for that SSID, but for the rest of the SSIDs, compare to the randomly scanning, you can still get some gain (for that specific SSID).

## Slide 10: Straw Poll
Do you support adding the following text to the subsection of 6.1 in the TGai SFD, 12/0151r7:
  11ai should have mechanism to support that AP select its working channel according to its SSID, and STA scan a target AP with known SSID from the channel according to the SSID
Yes:
No:
Abstain:

## Slide 11: Motion
Do you support adding the following text to the subsection of 6.1 in the TGai SFD, 12/0151r7:
  11ai should have mechanism to support that AP select its working channel according to its SSID, and STA scan a target AP with known SSID from the channel according to the SSID
Yes:
No:
Abstain: