## Slide 1: BSS information on other channels
Name | Affiliations | Address | Phone | email
Jing-Rong Hsieh | HTC Corp. | 1F, 6-3 Baoqiang Road, Xindian district, New Taipei City, Taiwan |  | jing_hsieh@htc.com
Authors:
Date: 2012-07-06

## Slide 2: Fast Network Discovery (12/0157r8)
6.1.4 BSS Information on other Channels
  802.11ai shall have mechanism to include information of the responding AP and other APs to the Probe Response

## Slide 3: Available information in probe responses/beacons
AP Channel Report (2+)
  Operating Class(1 octets)/Channel (Variable octets)
Multiple BSSID (3)
  BSSID Index (1)/DTIM Period(opt)(1)/DTIM Count(opt)(1)
BSS Load (4)
  Station Count(2)/Channel Utilization(1)/Available Admission Capacity(1)
  Num/0~255/Time
BSS Average Access Delay (4)
  Access Category Access Delay (4) (0~255)
BSS Available Admission Capacity (2+32)
  Available Admission Capacity Bitmask (2)/Available Admission Capacity List (2*total num of nonzero bits)
  0/1 , Time
Notes: 47 octets

## Slide 4: BSS Information on other Channels
The information helps STA know the “existence” of other APs in other channels and allow them to move to the channel to scan
  However, they may not be superior to the one it just scanned
  PHY info such as signal quality is not conveyable
To reduce unnecessary scans, in addition to existence, it may help if the “suitability” and “difference” between the scanned ones and the remaining ones is known to the STA
  If the BSS has many properties in common,
  Give stronger reason for the STA to continue scan for better channel or stop here
    whether the remaining ones are likely to be better or not

## Slide 5: Proposal
In addition to AP Channel Report, AP can attach the loading information of BSSs on other channels in the probe response and beacon for STA’s reference
  A condensed and aggregated loading information
    Use a coarser unit to represent BSS load, BSS Avg access delay, BSS Available Admission Capacity
  A comparison (helpful in ESS case)
    A signed value of condensed loading information;
    A signal bit for a certain information (like a scoreboard)

## Slide 6: Proposal
By the scan result, STA can include “STA Channel Report” in association request when it decides to join certain BSS
  Report to the APs with the existence of BSSs on other channels
    BSSs of the same SSID are more viable
  Can additionally attach the loading info or differences of loading info between the scan result and the intending one
    A condensed and aggregated loading information
      Use a coarser unit to represent BSS load, BSS Avg access delay, BSS Available Admission Capacity
    A comparison (helpful in ESS case)
      A signed value of condensed loading information;
      A signal bit for a certain information (like a scoreboard)

## Slide 7: Proposal of scoreboard
BSS Load
  Station Count(2)/Channel Utilization(1)/Available Admission Capacity(1)
BSS Average Access Delay
  Access Category Access Delay (4) (0~255)
BSS Available Admission Capacity
  Available Admission Capacity Bitmask (2)/Available Admission Capacity List (2*total num of nonzero bits)
Scoreboard (Size is dependent on the adopted unit and interpretation) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BSS Load |  |  | BSS Average Access Delay |  |  |  | BSS Available Admission Capacity |  |  |  |  |  |  |  | Reserved
STA Count | Channel Utilization | Available Admission Capacity | Avg Access Delay for AC_BE | Avg Access Delay for AC_BK | Avg Access Delay for AC_VI | Avg Access Delay for AC_VO | UP 0 | … | UP 7 | AC 0 | AC 1 | … | AC 3 | Reserved | …

## Slide 8: Conclusion
In addition to existence, more information can be provided to reduce unnecessary scan
The information can be a comparison between others and the one announcing it
  For ESSs with common capabilities, most recent information such as loading and access delay
  The notion of Multiple BSSID can be reused (only coding the different part based on a reference BSSID)
For scanning STAs obtained this info can decide to continue scanning in the indicated better channels or even stop scanning
  Some of channels remaining in ChannelList of MLME-SCAN.request can be omitted based on
    Existence of BSSs
    Suitability and availability of BSSs

## Slide 9: Straw Poll
Do you support to include the condensed loading-related information for other channels in the probe response and beacon? Yes: No: Abstain: