## Slide 1: Response considerations in AP discovery
Name | Affiliations | Address | Phone | email
Jing-Rong Hsieh | HTC Corp. | 1F, 6-3 Baoqiang Road, Xindian district, New Taipei City, Taiwan |  | jing_hsieh@htc.com
Date: 2012-07-06
Authors:
Notes: 2012.05.07
2012.05.25
2012.06.07
2012.06.20

## Slide 2: Fast Network Discovery (11-12/0153r9)
6.1.6 Omission of Probe Response (11-12/0153r9)
  An FILS Capable AP may omit transmission of Probe Response frame to FILS capable STAs if the TBTT occurs within a predefined time interval.
  (11-12/0655r5) Probe request may contain new information that would enable an AP to make the decision whether to respond to a probe request. Examples of this kind of information include:
    Link Quality parameters
    AP Capabilities
    QoS Requirement
    Address/ID

## Slide 3: Background and motivations
The defined behavior of AP discovery
  The AP shall respond to any probe request with matching ID
Observations
  Weak links may occupy air resource for a BSS/ESS and harm FILS
    Low transmission rate and higher probability for problems such as hidden node
  For the purpose of WiFi offloading, it may degrade user experience for offloading them to a slower link than the original one
  In office or hotspot scenarios, there are usually many APs with the same SSID nearby but differentiated by the signal strength and operating channel
  Connection manager on user device shows only the SSID with best signal
    It is also the AP that user will associate with if it is selected
    The hidden ones may be ignored during scan for the goal of FILS

## Slide 4
STA
AP
Auth Request
Auth Response
Assoc Request
Assoc Response (with RCPI)
Probe Request
Probe Response
Received channel power indicator (RCPI): An indication of the total channel power (signal, noise, and interference) of a received frame measured on the channel and at the antenna connector used to receive the frame.
….

## Slide 5: Criterion of not responding to probe request
AP may choose not to respond with a unicast probe response
  Consider known SSIDs
  Sol: Based on the RCPI of the received probe request and info
    The probe request can attach a target RCPI info along with the SSID
    The target RCPI info can be measured by AP with same SSID previously
      RCPI were attached in the Association Response and can be recorded as reference like desired SSID
        An indication that the STA had decided to join the SSID before with the recorded RCPI value
      A Tolerance can be added along (or being deducted from target RCPI)
    The scanned AP can decide if it should respond to the request with the target RCPI and
      Reply if larger or same as before ; Otherwise, do Not reply

## Slide 6
If transmit power control is used by APs, link asymmetric may be induced
AP
AP
AP
STA
AP
STA
Low power case
High power case

## Slide 7: Criterion of not responding to probe request
AP may choose not to respond with a unicast probe response
  Consider link asymmetric and the decision to join a BSS or not is based on downlink signal quality
  Sol: Based on the estimated RSSI (of the intending probe response) for the scanning STA
    The probe request can attach an unsolicited TPC report element and a desired RSSI for the STA-side
      Path loss can be measured
      The RSSI of the intending probe response can be derived
    The AP chooses not to respond if the estimated RSSI for the STA is weaker than the desired RSSI

## Slide 8: Conclusion
Reducing airtime occupancy is critical to reduce the latency for FILS
In this contribution we propose to add signal quality information in the probe request to reduce number of probe responses and the corresponding possible retransmissions
By the notion of hybrid scanning fashion introduced in TGai, those APs disqualified can still be discovered via the passive scanning way

## Slide 9: Straw Poll
Do you support to include the parameters described in this submission in the Probe Request frame body?
Yes: No: Abstain: