## Slide 1: ProbeTimer of Active Scanning
Authors:
Name | Affiliations | Address | Phone | email
Lin Cai | Huawei | 3601 Algonquin Road, Suite 1000, Rolling Meadows, IL 60008 | 1-847-848-1778 x 379 | Lin.cai@huawei.com
07/05/2012

## Slide 2: Active Scanning[1]
PHY-CCA.indication (busy) primitive is not detected, scan the next channel when ProbeTimer reaches MinChannelTime
Otherwise, when ProbeTimer reaches MaxChannelTime, process all received probe responses
Probe
MinChannelTime
MaxChannelTime
[1] 11REVmb-D12, Cls 10.1.4.3.3

## Slide 3: Problem Statement
CCA is based on energy detection technique
  Responses from other STAs
  Non-Wifi devices operating in unlicensed channel
    Microwave, cordless phone, etc.
If CCA busy primitive is detected but no AP exists in the scanned channel, STAs have to scan for MaxChannelTime before switching to the next channel
  MinChannelTime = 0.67 ms [2,3]
  MaxChannelTime = 15 ms [2,3]
[2] M. Ryong Jeong, et.al., ”Fast Active Scan for Measurement and Handoff,” DoCoMo USA Labs, Contribution to IEEE802, May 2003.
[3] M. Emmelmann, “Achievable gains in AP Discovery,” FOCUS, doc. IEEE 802.11-10/0922r1

## Slide 4: Delay of Active Scanning
M APs uniformly distributed over N channels
  The probability that there is at least one AP in any given channel is
    P=1-(1-1/N)^M
  Given an AP exists in a given channel, the expected time a STA spends in scanning this channel is
    T1= ProbeDelay + Tx_ProbeReq + MaxChannelTime
  Given no AP exists in a given channel
    CCA busy primitive is not detected (ideal case):
    T2_{ideal}=ProbeDelay + Tx_ProbeReq + MinChannelTime
    CCA busy primitive is detected due to interference/requests (non-ideal case):
    T2_{Non-ideal}=ProbeDelay + Tx_ProbeReq + MaxChannelTime
  Expected scanning delay in one channel: D=T1*P + T2 *(1-P)

## Slide 5: Delay of Active Scanning (Cont’d)
Parameters[3]:
  ProbeDelay = 0.1 ms
  MinChannelTime = 0.67 ms
  MaxChannelTime = 15 ms
  Tx_ProbeReq = 0.4 ms
  N=14 channels
Chart: 
Ideal Case | 2.1936 | 3.144 | 4.0266 | 4.8461 | 5.6071 | 6.3138 | 6.9699 | 7.5792 | 8.145 | 8.6703 | 9.1582 | 9.6112 | 10.0318 | 10.4224 | 10.7851 | 11.1218 | 11.4346 | 11.725 | 11.9946 | 12.245
Non-ideal Case | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5
Number of APs M
Expected scanning delay over each channel (ms)
[3] M. Emmelmann, “Achievable gains in AP Discovery,” FOCUS, doc. IEEE 802.11-10/0922r1

## Slide 6: Proposed ProbeTimer
CCA busy primitive is not detected
  ProbeTimer = MinChannelTime
CCA busy primitive is detected, and STAs receive some messages with hard evidence of APs’ existence
  Example of messages: data frames (may change NAV setting to non-zero), management frames ( association, authentication, etc.), and control frames (RTS, CTS, ACK, block-ACK, ps-poll, etc.)
  ProbeTimer = MaxChannelTime
CCA busy primitive is detected, but there is no hard evidence of Aps’ presence
  ProbeTimer =MedChannelTime, where MinChannelTime<=MedchannelTime<= MaxChannelTime

## Slide 7: MedChannelTime
Probe
MinChannelTime
MaxChannelTime
MedChannelTime
MinChannelTime<=MedchannelTime<= MaxChannelTime
Scan for MedChannelTime when the channel is sensed busy, however, there is no hard evidence that any AP exists in the scanned channel

## Slide 8: Delay Comparison
Expected delay with proposed timer
  D=T1*P + T2_{proposed} *(1-P), where
  T2_{proposed} = ProbeDelay + Tx_ProbeReq + MedChannelTime
Number of APs M
Expected scanning delay over each channel (ms)
Chart: 
Ideal Case | 2.1936 | 3.144 | 4.0266 | 4.8461 | 5.6071 | 6.3138 | 6.9699 | 7.5792 | 8.145 | 8.6703 | 9.1582 | 9.6112 | 10.0318 | 10.4224 | 10.7851 | 11.1218 | 11.4346 | 11.725 | 11.9946 | 12.245
Non-ideal Case | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5 | 15.5
MedChannelTime=2ms | 2.9643 | 3.8597 | 4.6911 | 5.4632 | 6.1801 | 6.8458 | 7.464 | 8.038 | 8.571 | 9.0659 | 9.5255 | 9.9522 | 10.3485 | 10.7165 | 11.0582 | 11.3754 | 11.67 | 11.9436 | 12.1976 | 12.4335
MedChannelTime=5ms | 5.75 | 6.4464 | 7.0931 | 7.6936 | 8.2512 | 8.769 | 9.2498 | 9.6962 | 10.1108 | 10.4957 | 10.8532 | 11.1851 | 11.4933 | 11.7795 | 12.0452 | 12.292 | 12.5211 | 12.7339 | 12.9315 | 13.115

## Slide 9: Conclusion
In current standard, energy detection based CCA may cause long scanning delay when no AP exists in the scanned channel
Another timer, namely, MedChannelTime, is proposed for STAs with detected CCA busy primitive but no other evidence of AP’s presence

## Slide 10: Straw Poll 1
Do you agree that using CCA only for determining the ProbeTimer is not sufficient and may cause long delay?
Yes
No
Abstain

## Slide 11: Straw Poll 2
Do you agree that a STA should decide the ProbeTimer by checking CCA primitive and some other messages or parameters (e.g., NAV)?
Yes
No
Abstain