## Slide 1: Preamble Discussions
Date: 2012-07-16
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Short and Long preamble Mandatory/Optional Rules
For >=2MHz, two preamble formats are defined: Short and Long preambles [1].
Short preamble is the simplest to implement, may allow simple sensor devices (that only support 1MHz and 2MHz) to only do short preamble, other devices (AP, or STAs targeted for data applications) shall support both preambles.
To guarantee interoperability, any device has to be able to at least decode SIGA field of long preamble to set up CCA.

## Slide 5: Proposed Text Change (1)
Insert the following text in the spec framework:
  “
  Both short and long preambles are mandatory at the AP.
  For a STA,
    If it supports only 1MHz/2MHz, short preamble is mandatory, and long preamble is optional (exchanged by capability fields).
    Otherwise, both short and long preambles are mandatory.
  Any device shall be able to detect and decode SIGA field in the long preamble for CCA.
  ”

## Slide 6: Short Preamble Description
Current spec framework starts short preamble section as below.
  “R.3.2.1.1.A: The general structure for SU open-loop packet is similar to 11n green field preamble, as below (short preamble):”
The description “SU open-loop” seems vague, and is not normative.
  Similar to 11n green field packet and legacy 11a/g packets when transmitted with multiple antennas, there was no restriction on what spatial mapping matrix should be used (TxBF or not), as in 11n/11ac spec.
  Transmitter/AP may decide on its own whether to transmit BF/Non-BF packets using short preamble or long preamble, based on performances or other criterion, depending on implementations.

## Slide 7: Proposed Text Change (2)
Make the following text change:
“
  R.3.2.1.1.A: The general structure for SU open-loop packet is similar to 11n green field preamble, as below (short preamble): The general short preamble structure for greater than equal to 2 MHz PHY packet is defined as in the figure below:
  ”

## Slide 8: Straw Poll / Pre-Motion
Do you agree with the text change as described in slide 5 and slide 7?

## Slide 9: References
[1] 11-12-0595-00-00ah-Rename-2MHz-Preamble