## Slide 1: Smoothing Bit and Beam-Change Indication Bit for 2MHz Preamble
Date: 2012-07-10
Authors:

## Slide 4: Propose to Add Smoothing and Beam-change Indication Bit in SIG/SIGA Field
 | Short preamble | Long preamble | 
 | SU | SU | MU
Length / Duration | 9 | 9 | 9
MCS | 4 | 4 | -
BW | 2 | 2 | 2
Aggregation | 1 | 1 | -
STBC | 1 | 1 | 1
Coding | 2 | 2 | 5
SGI | 1 | 1 | 1
GID | - | - | 6
Nsts | 2 | 2 | 8
PAID | 9 | 9 | -
Ack Indication | 2 | 2 | 2
Smoothing | 1 | - | -
Beam-change Indication | - | 1 | -
Reserved | 4 | 4 | 4
CRC | 4 | 4 | 4
Tail | 6 | 6 | 6
Total | 48 | 48 | 48

## Slide 5: Smoothing Indication in Short Preamble
Channel smoothing can improve PER performance by 1~2dB
  There is a smoothing bit in HT-SIG
    A value of 1 indicates that channel smoothing is recommended.
    A value of 0 indicates that channel smoothing is not recommended.
Smoothing bit can also partially serve as the beamforming indication
  Beamformed channel generally can not be smoothed

## Slide 6: Beam-Change Indication in Long SU Preamble
Beam-Change Indication: to tell if the pre-multiplied Q matrix is changed from Omni-portion to Data Portion
  Channel Combination Gain
      Channel estimation from LTF1 and D-LTF1 can be combined if there is a beam-change indication
      4.7dB gain on channel estimation MSE (3 CE symbols V.S. 1 CE symbol)
  Smoothing Gain
    It could also serve as channel smoothing recommendation.
  Beam-change indication bit
    A value of 1 indicates that Q matrix is changed; A value of 0 indicates that Q matrix is un-changed

## Slide 7: Straw poll 1
 | Short preamble | Long preamble | 
 | SU | SU | MU
Length / Duration | 9 | 9 | 9
MCS | 4 | 4 | -
BW | 2 | 2 | 2
Aggregation | 1 | 1 | -
STBC | 1 | 1 | 1
Coding | 2 | 2 | 5
SGI | 1 | 1 | 1
GID | - | - | 6
Nsts | 2 | 2 | 8
PAID | 9 | 9 | -
Ack Indication | 2 | 2 | 2
Smoothing | 1 | - | -
Beam-change Indication | - | 1 | -
Reserved | 4 | 4 | 4
CRC | 4 | 4 | 4
Tail | 6 | 6 | 6
Total | 48 | 48 | 48
Do you agree to have a smoothing bit in short preamble SIG field and a beam-change indication bit in long SU preamble SIGA field?
Yes: No: Abstain:
  Beam-change indication bit:
    A value of 1 indicates that Q matrix is changed;
    A value of 0 indicates that Q matrix is un-changed

## Slide 8: Straw poll 2
Do you agree to add the following paragraph in the Specification Framework for Tgah in section R.3.2.1.1.E?
  Note: If the beam-change indication bit in long preamble is set to 0, the receiver may do channel smoothing. Otherwise, smoothing is not recommended.
Yes: No: Abstain: