## Slide 1: Tail Bits in 1MHz SIG Field
Date: 2012-07-16
Authors:

## Slide 4: Proposal
The current spec-frame work document has the following SIG field allocation with Tail bits left TBD as the group wanted to explore tail-biting
In this proposal we propose to use 6 tail bits in the 1MHz SIG just like the 2MHz SIG field
  Same as 11n and 11ac SIG fields
Field of SIG | Bits | Comments
Nsts | 2 | Number of space-time-streams
SGI | 1 | Short Guard Interval
Coding | 2 | 1st bit is coding type (LDPC/BCC), 2nd bit is for LDPC Nsym ambiguity
STBC | 1 | Same as in 11ac
MCS | 4 | The MCS for SU case
Aggregation bit | 1 | Signals use of AMPDU
Length | 9 | Length field (in symbols when aggregation is ON, is in bytes when aggregation is OFF, Mandate AMPDU for packet sizes > 511 bytes
ACK Indication | 2 | 00: Ack; 01: BA; 10: No Ack; 11: reserved
Reserved | 4 | Some possible uses are MAC bits or any other new features etc. Details TBD
CRC | 4 | 4 bits of CRC should be enough
Tail | 6 (TBD) | Tail-biting can be explored
Total | 36 | 

## Slide 5: Reason for having tail bits
Does not make sense to have tail-biting just for the purposes of 1MHz SIG
  2MHz data, SIG and 1MHz data do not have tail-biting
  The special processing does not seem worth it for just 1 symbol saving in the preamble

## Slide 6: Pre-motion 1
Do you agree to have 6 tail bits in the 1MHz SIG field and make the following change to the spec framework document (delete the strike-through text below)?
Field of SIG | Bits | Comments
Nsts | 2 | Number of space-time-streams
SGI | 1 | Short Guard Interval
Coding | 2 | 1st bit is coding type (LDPC/BCC), 2nd bit is for LDPC Nsym ambiguity
STBC | 1 | Same as in 11ac
MCS | 4 | The MCS for SU case
Aggregation bit | 1 | Signals use of AMPDU
Length | 9 | Length field (in symbols when aggregation is ON, is in bytes when aggregation is OFF, Mandate AMPDU for packet sizes > 511 bytes
ACK Indication | 2 | 00: Ack; 01: BA; 10: No Ack; 11: reserved
Reserved | 4 | Some possible uses are MAC bits or any other new features etc. Details TBD
CRC | 4 | 4 bits of CRC should be enough
Tail | 6 (TBD) | Tail-biting can be explored
Total | 36 |