## Slide 1: Active Scanning considering Operating Status of APs
Date: 2012-07-06

## Slide 2: Abstract
We propose a Probe Request filtering mechanism considering AP’s operating status to reduce unnecessary Probe Responses
Approach:
  Filter the Probe Request by the responding AP considering its operating status based on the requirement selected by the STA that has sent the Probe Request
    can reduce the traffic caused by unnecessary Probe Responses
    helps the selection of an appropriate AP operating under good condition to be associated with the requesting STA
Jae Seung Lee, ETRI

## Slide 3: Background
This contribution proposes text for TGai Specification Framework Document regarding scanning enhancement for fast network discovery
This contribution proposes the next level of detail of Section 6.1.6 Omission of Probe Response of the SFD
(11-12/0655r5) Probe request may contain new information that would enable an AP to make the decision whether to respond to a probe request. Examples of this kind of information include:
      Link Quality parameters
      AP Capabilities
      QoS Requirement
      Address/ID
Proposed Spec Framework text is included in the Motion section at the end of this contribution
Jae Seung Lee, ETRI
Slide 3

## Slide 4: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Jae Seung Lee, ETRI

## Slide 5: Active Scanning considering Operating Status of APs
AP responds to the Probe Request although its operating condition is not good enough to accept the STA
  If the AP is fully loaded or does not have enough resources for the new association, then it is better for the requesting STA not to be associated with the AP
  If the AP cannot fulfill the operating condition required by the STA, then sending Probe Response to such STAs is not necessary
Jae Seung Lee, ETRI

## Slide 6: Approach
STA’s requirement on the AP’s operating condition is included in the Probe Request frame
The Responding AP checks the requirement and if it cannot satisfy the requirement on its operating condition, it does not transmit Probe Response
  STA may specify its requirement on AP’s operating condition such as Available Admission Capacity, AP Average Access Delay, and BSS AC Access Delay in the Probe Request
Jae Seung Lee, ETRI

## Slide 7: AP Operating Condition Preference (1/2)
Example of AP Operating Condition Preference IE:
STA indicates its requirements on AP’s operating condition, such as AP Average Access Delay, BSS AC Access Delay, and Available Admission Capacity in the Probe Request
If the responding AP’s operating condition is not good and cannot satisfy the indicated requirement, AP does not transmit Probe Response
Element ID | Length | AP Average Access Delay | BSS AC Access Delay | Available Admission Capacity | Other TBD optional elements
Octets: 1 1 1 4 2
Jae Seung Lee, ETRI
Slide 7
Notes: 삭제

## Slide 8: AP Operating Condition Preference (2/2)
AP Average Access Delay
  indication of the relative level of loading at an AP
  A low value indicates more available capacity than a higher value
  For example, if the STA indicates value 250 in the Probe Request but the AP’s current Average Access Delay is 253, AP does not transmit Probe Response
BSS AC Access Delay
  indication of the average access delay at a QoS AP for services for each of the indicated Access Categories
Available Admission Capacity
  specifies the remaining amount of medium time available via explicit admission control
Jae Seung Lee, ETRI
Slide 8

## Slide 9: Benefits of the Filtering
Reduces the unnecessary Probe Responses
  Filter the Probe Request because the AP cannot satisfy the operating condition demanded by the requesting STA
Prevent the association with APs that cannot satisfy the operating requirement of the requesting STAs
Helps the association process by enabling the STA to choose the appropriate APs that can be associated with the requesting STA
Jae Seung Lee, ETRI

## Slide 10: Conclusion
We proposed Probe Request filtering considering AP’s operating status to reduce Probe Responses
In this proposal:
  Filter the Probe Request by the responding AP regarding its operating status based on the requirement selected by the STA that has sent the Probe Request
    can reduce the traffic caused by unnecessary Probe Responses
    helps the selection of appropriate AP operating under good condition to be associated with the requesting STA
Jae Seung Lee, ETRI

## Slide 11
Motion
Move to update the spec framework document with the following text under subsection “6.1.6 Omission of Probe Response”:
  Non-AP STA may include its requirements on responding STA’s operating condition including AP Average Access Delay, BSS AC Access Delay, and Available Admission Capacity in the Probe Request frame for omission of Probe Response.
Moved:
Seconded:
Yes
No
Abstain
Jae Seung Lee, ETRI

## Slide 12
References
11-12/0063r1 Selective transmission of the Probe Response
11-12/0064r0 Text for Selective transmission of the Probe Response
  11-12/265r7 Spec Framework Proposal – Selective transmission of the Probe Response
  11-12/0572r0 Selective transmission of the Probe Response for 11ai Spec Framework
  11-12/0151r8 Specification Framework for TGai
Jae Seung Lee, ETRI