## Slide 1: Fast Initial Service Discovery: An enabler for Self-Growing
Date: 2012-07-16
Authors:

## Slide 2: Abstract
This presentation highlights three use cases showing how fast initial service discovery supports cognitive network (re-) configuration and service composition via the ‘self-growing’ concept.
This document derives two main requirements towards the ISD functionality

## Slide 3: Self Growing
A self-growing network coexists, collaborates or integrates—potentially in symbiosis—with collocated networks utilizing their service or geographical extend to augment network capacity, or operational constrains such as energy consumption.
The self-growing process including network operation and management is realized by focused cognitive decision making controlling network and node reconfiguration.
The self-growing process includes discovering if other networks or devices comprise cognitive, self-growing features or specific services.
To reduce the time spend in this discovery, a fast service discovery—optimally not requiring a full-state link set-up—is required.

## Slide 4: Self-growing for energy-aware end-to-end delay optimization
Sensor nodes are deployed in a given environment partially covered by a second type of network, e.g. IEEE 802.11 WLAN
The sensor nodes are equipped with a reconfigurable radio unit; they share the communication band (e.g. 2.4 GHz band) with the WLAN but use a sensor network specific MAC protocol optimized for low energy consumption in order to achieve a long lifetime of the sensor network. They use multi-hop communication, causing long delays, to forward sensor readings.
During their lifetime of the sensor network, a change in its purpose occurs: in addition to existing functionality, sensor nodes have to report on delay sensitive data to a data sink.
Instead of reconfiguring the sensor network, nodes discover WLAN APs in their vicinity and discover if they either offer “self-growing services” or at least “data offloading capabilities”

## Slide 5: Purpose-driven network reconfiguration during an emergency situation
Sensor nodes forming an ad-hoc network are deployed in a given environment partially covered by a second type of network providing centralized, single-hop backbone access, e.g. IEEE 802.11 WLAN
Under normal operation, the sensor network provides sensing information (e.g. temperature in various locations of a building) at low duty cycles; the network is optimized for long network lifetime accepting higher delays in the acquisition of sensing information#
An incident situation and the existing sensor node infrastructure is partially disrupted
Additionally, the cognitive decision engine controlling the network reconfiguration and self-growing process of the sensor and WLAN network might detect that sensor nodes are located in an are where WLAN coverage is (no longer) given
As a result, sensor nodes are reconfigured to permanently use the 802.11 MAC in order to act as a meshed network re-establishing 802.11-based coverage. Mobile devices of users within the incident area have to quickly discover those newly available “mesh APs” and their services to establish a link with them.

## Slide 6: Cognitive Coexistence and self-growing for white space operation
This use cases focuses on a locally deployed access point operating in white spaces in order to form a WLAN providing access to a small (company) network
Over the lifetime of the deployments, the purpose of the deployed network elements grows from only supporting nomadic mobility to additionally supporting seamless mobility for mobile users.
Achieved in various ways
  cognitive decision engine achieves separation in (used) spectrum
  the engine learns about the requirements of each device and intelligently considers a dynamic adaptation of assigned spectrum per node/network
  each network adapts its purpose according to users’ needs (e.g. adding low latency low bandwidth communication for surveillance purposes to existing high bandwidth but long delay services).
For the integration of 802.11-based networks in this self-growing process, devices have quickly to query for cognitive, self-growing capabilities via application layer services

## Slide 7: Summary
Fast Initial Service Discovery is one key enabler for sufficient self-growing incorporating WLAN devices
Limited requirements towards the scope of ISD SG:
  Transparent “tunneling” of service discovery protocols before actual 802.11 link set-up
  Announcement of “available services” via beacon, or probe response, or other means (provisioning of unsolicited announcements)

## Slide 8: Straw Poll
Are you in favor of adding the self-growing use cases and the two derived requirements to the ISD SG Use Case Document?
Yes
No
Abstain

## Slide 9: References