## Slide 1: Ad Hoc Discussions of 802.11ai Passive Scanning during 2012-July San Diego Meeting
Date: 2012-07-20
Authors:

## Slide 2: Abstract
This document is intended to keep tracking of the ad hoc discussions about 802.11ai passive scanning during 2012-July San Diego meeting.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4
Background
11ai Passive Scanning Work Status before 2012-July San Diego Meeting:
  Accepted 11ai SFD text about passive scanning: Subsection 6.2.1 and 6.2.2 in 12/0151r8;
  Previous discussions about passive scanning: 12/0406r5 and 12/0669r1.
Passive Scanning related Submissions to TGai for 2012-July San Diego meeting
  11-12-0741-01-00ai-discussions-about-fils-discovery-frame-content-design
  11-12-0742-00-00ai-discussions-of-fils-discovery-frame-format-design
  11-12-0790-00-00ai-multiple-frequency-channel-scanning
  11-12-0784-00-00ai-bss-information-on-other-channels
Passive Scanning Discussions during 2012-July San Diego meeting
  Monday PM-1: Presentations / Discussions of contributions, 12/0741r1, 12/0742r0, and 12/0790.
  Monday PM-2: Ad Hoc discussions
  Wednesday AM-1: Ad Hoc discussions
  Wednesday PM-2: Ad Hoc discussion

## Slide 5
Ad Hoc Discussion Agenda Items
Re-cap the design purpose of FILS Discovery frame?
  Is FILS Discovery frame a periodical message?
  Is it a replacement of regular beacon?
  Does it enable STA to initiate association?
Does the FILS discovery frame apply to other bands than 20MHz?
PPDU type for FILS discovery frame?
Target size of FILS discovery frame or other design constraints?
Detailed contents for FILS discovery frame?
  Including mandatory vs. optional?
FILS Discovery frame format decision?
  Should we consider MAC header optimization?

## Slide 6
Is FILS Discovery frame a periodical message?
    Based on 11ai SFD, “The FILS Discovery Frame may be transmitted periodically and/or non-periodically. “
    Another related issue: should FILS discovery frame indicate its periodicity (if periodical)?
      Yes: 4
      No: 8
      Abstain: 16
    Configurable system parameter?
    Function of FILS discovery frame:
      Just for AP/Net discovery, not for STA synchronization?
Re-cap: Design Purposes of FILS Discovery Frame

## Slide 7
Re-cap: design purposes of FILS Discovery frame
Is it a replacement of regular beacon?
    No
Does it enable STA to initiate association?
    Delay the discussions to the “contents” item, will be the leading question for that agenda item.

## Slide 8
Bands/Bandwidth, PPDU Type, Target Size
Does the FILS discovery frame apply to other bands than 20MHz?
  Yes, 11ai will be bands/bandwidth independent!
PPDU type for FILS discovery frame?
  Any PPDU types (non-HT PPDU, legacy STAs can understand)??
  Table it to the discussion of contribution 12/0772.
Target size of FILS discovery frame or other design constraints?
  Wireless media occupancy vs. Size of FD frame?
  a previous contribution related to this issue: 12/0042r4.
  Should we agree on a “max size” before the discussion of the FD contents?
    Be as small as possible

## Slide 9
Discussion about FILS Discovery Frame Contents
contents for FILS discovery frame? (Including mandatory vs. optional?)
Purpose of FILS discovery frame?
  Does it enable 11ai-capable STA to initiate association?
    Case-1: STA has the info of AP’s SSID and AP’s configuration change count;
    Case-1 STA does not have any info about the AP.
  Does it only enable AP discovery?
  Is AP’s SSID sufficient for AP discovery? If not, what else info is needed?

## Slide 10
Purposes of FILS Discovery Frame
enable AP discovery, i.e., advertise the presence of the AP on the channel
yes
Enable STA to synchronize with the AP
No
provide information for AP/Network initial de-selection
Nice-to-have, optional
Enable all non-AP STA to initiate association
no
Enable some STAs to initiate association
Yes, (need further investigation about which STAs)
Enable STA to efficiently scan multiple APs/Channels
Nice-to-have, optional

## Slide 11
FILS Discovery Frame: Purpose and Required Info Items
Purposes | Info Items | Needed in FD frame | Notes
Enable AP Discovery | SSID BSSID (in MAC header) | Yes | Advertise the presence of AP on the channel
Enable STA Synchronization | TimeStamp | No | ** in units of TUs (i.e., 1024us)
provide information for AP/Network de-selection | SSID, BSSID -- yes Capability – a compressed indication , Yes Access network options , yes Security (simple indications) , yes BSS load , no (could be implied by other parameters) ??? | optional | 
Enable any STA to initiate association | SSID, BSSID TimeStamp capability Access network options Security BSS load Channel descriptors PHY parameters ??? | NO | 

## Slide 12
FILS Discovery Frame: Purpose and Required Info Items –con’t
Purposes | Info Items | Needed in FD frame | Notes
Enable some STAs to initiate association | SSID, Yes Configuration count, yes, optional | Yes | The selected STAs are those ones that have the AP’s SSID and its configuration count
Enable optimizations for multiple APs/Channels scanning | AP’s next TBTT, yes info about Neighbor AP/Channel Next TBTT if available, (need to be really compressed), yes Next FD frame Tx Time if available, Cannot be decided now, need to further discussion about FD frame periodical issue. | optional | 

## Slide 13: Straw-Polls
Straw-Poll-1: Do you support that the following information items shall be included in the FILS Discovery Frame body?
  SSID
Result Yes 26 No 0 Abstain______7_________

## Slide 14: Straw-Polls
Straw-Poll-2: Do you support that the following information items may be included in the FILS Discovery Frame body?
  Capability
  Access network options
  Security
  AP Configuration change count
  AP’s next TBTT
  Neighbor AP’s next TBTT
Result Yes 23 No 0 Abstain______14_________

## Slide 15: Motions
Motion-1: add the following text to Subsection “6.2.1 General Approach”, on page 8, in the TGai SFD, 12/0151r10
The FILS Discovery frame shall include the following information item:
  SSID
Result Yes 30 No 0 Abstain________1_____

## Slide 16: Motions
Motion-2: add the following text to Subsection “6.2.1 General Approach”, on page 8, in the TGai SFD, 12/0151r10
The FILS Discovery frame may include the following information items:
  Capability
  Access network options
  Security
  AP Configuration change count
  AP’s next TBTT
  Neighbor AP’s next TBTT
Result Yes 21 No 0 Abstain_____11__________

## Slide 17
FILS Discovery Frame Contents
SSID
references
  802.11-2012: SSID IE with 0 to 32 bytes
  11ah short beacon: compressed SSID 4 bytes
Discussion questions
  Compressed SSID is not enough to initiate association based on current 802.11 spec!
  Can FILS Discovery frame use compressed SSID?
  Does compressed SSID provide enough info to advertise AP’s presence in the channel?
  Should the FILS discovery frame information items be designed to keep backward
  Truncated SSID
  11ah compressed SSID only provides one-way mapping
  Compressed SSID could be useful to STAs that have associated with the AP previously
  Use full SSID
  Use condensed SSID with 8 bytes, as the current commonly used SSIDs are from 6 to 8 bytes

## Slide 18
FILS Discovery Frame Contents – con’s
Access Network Options
references
  802.11-2012: 1-byte info as defined in Figure 8-352, in 802.11-2012 spec, also adopted in 802.11ah short beacon.
Discussion questions
  Re-use the 1-byte as defined in Figure 8-352 in 802.11-2012 spec
  Possibility to improve its encoding efficiency

## Slide 19
FILS Discovery Frame Contents – con’s
Capability
references
  Beacon/Probe Response in 802.11-2012 spec
    Capability info field: p438, section 8.4.1.4
    Supported Rates element, p478, 8.4.2.3
    Extended Capabilities element, p562, section 8.4.2.29
    Neighbor Report element, 8.4.2.39
  Measurement Pilot frame
  11ah short beacon
Discussion questions
  Support data rates
  Attempt to eliminate the supported rates element, by using the reserved bits in capability info field to indicate the identified minimum rates.

## Slide 20: Straw-Polls
  Straw-Poll-3: Do you support that the FILS Discovery frame may include the information item of Access Network Options , encoded as 1-byte information as defined in Figure 8-352 in 802.11-2012 spec?
Result Yes 24 No 0 Abstain_____1_________

## Slide 21: Motions
Motion-3: add the following text to Subsection “6.2.1 General Approach”, on page 8, in the TGai SFD, 12/0151r10
The FILS Discovery frame may include the information item of Access Network Options , encoded as 1-byte information as defined in Figure 8-352 in 802.11-2012 specification
Result Yes 24 No 0 Abstain______7_____

## Slide 22
References:
IEEE Std 802.11™-2012
11-12-0151-08-00ai-proposed-specification-framework-for-tgai
11-12-0406-05-00ai-passive-scanning-improvements-draft
11-12-0669-01-00ai-passive-scanning-improvements-ad-hoc-report
11-12-0741-00-00ai-FILS-Discovery-Frame-Content-Discussions
11-12-0742-00-00ai-discussions-of-fils-discovery-frame-format-design
11-12-0790-00-00ai-multiple-frequency-channel-scanning