IEEE P802.11
Wireless LANs

| Clause 9.19.2.8 Proposal |
| --- |
| Date: 2012-07-17 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Zhou Lan | NICT | 3-4, Hikarino-oka, Yokosuka, Japan | +81-46-847-5097 | lan@nict.go.jp |
| Kenichi Mizutani | NICT |  |  | mizk@nict.go.jp |
| Gabriel Villardi | NICT |  |  | gpvillardi@nict.go.jp |
| Hiroshi Harada | NICT |  |  | harada@nict.go.jp |

The editing instructions are shown in bold italic. Four editing instructions are used: change, delete, insert, and replace. Change is used to make corrections in existing text or tables. The editing instruction specifies the location of the change and describes what is being changed by using strikethrough (to remove old material) and underscore (to add new material). Delete removes existing material. Insert adds new material without disturbing the existing material. Insertions may require renumbering. If so, renumbering instructions are given in the editing instruction. Replace is used to make changes in figures or equations by removing the existing figure or equation and replacing it with a new one. Editorial notes will not be carried over into future editions because the changes will be incorporated into the base standard.

This amendment’s baseline is IEEE Std 802.11™–2012, as amended by

- Amendment 1 802.11ae-2012

- Amendment 2 802.11aa-2012

- Amendment 3 P802.11ad Draft 8.0

- Amendment 4 P802.11ac Draft 3.0

TGaf Editor: change the title of clause 9.19.2.8. as follows:

9.19.2.8 EDCA channel access in a VHT and TVHT BSS

TGaf Editor: Insert the following rows at the end of Table 9-20:

| Table 9-20-Channels indicated idle by the channel-list parameter |
| --- |
| PHY-CCA.indication channel-list element | Idle channels |
| primaryTVHT_W | None of the TVHT_W channel |
| secondaryTVHT_W | Primary TVHT_W channel |
| secondaryTVHT_2W | Primary TVHT_W channel and secondary TVHT_W channel(#4151) |

TGaf Editor: change the following paragraphs in section 9.19.2.8.

If a STA is permitted to begin a TXOP (as defined in 9.19.2.3 (Obtaining an EDCA TXOP)) and the STA has at least one MSDU pending for transmission for the AC of the permitted TXOP, the STA shall perform exactly one of the following steps:

- transmit a 160 MHz or 80+80 MHz mask PPDU if the secondary channel, the secondary 40 MHz channel and the secondary 80 MHz channel were idle during an interval of PIFS immediately preceding the start of the TXOP

- transmit an 80 MHz mask PPDU on the primary 80 MHz channel if both the secondary channel and the secondary 40 MHz channel were idle during an interval of PIFS immediately preceding the start of the TXOP.

- transmit a 40 MHz mask PPDU on the primary 40 MHz channel if the secondary channel was idle during an interval of PIFS immediately preceding the start of the TXOP.

- transmit a 20 MHz mask PPDU on the primary 20 MHz channel.

- transmit a TVHT_4W or TVHT_2W+2W mask PPDU if the the secondary TVHT_W channel and the secondary TVHT_2W channel were idle during an interval of PIFS immediately preceding the start of the TXOP

- transmit an TVHT_2W mask PPDU on the primary TVHT_2W channel if the secondary TVHT_W channel  were idle during an interval of PIFS immediately preceding the start of the TXOP.

- transmit a TVHT_W mask PPDU on the primary TVHT_W channel.

# Text boxes

Abstract

Submission for candidate P802.11af draft section 9.19.2.8 text for next draft.