## Slide 1: Aggregated Probe Response
Date: 2012-09-13
Authors:

## Slide 2: Abstract
The presentation describes an improvement to the Active Scanning mechanism to reduce the delay on unused channels during the AP discovery phase.
This presentation will focus on comparing the enhancement of Rapid Scan to Active Scan compared to the current status of only using Active Scan.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | Yes
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: Recap, Active Scanning Procedure
Active scanning procedure is defined in 10.1.4.3.3 and is very effective in certain environments:
  Where coverage is known to be present.
  Where the procedure is user triggered.
  Where the number of scanned channels is not great or the latency is not critical.
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time
MAC Action message
Time uncertainty <
Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS

## Slide 5: Recap, Active Scanning Procedure
Active scanning procedure is defined in 10.1.4.3.3 and has the following properties:
  Minimum duration of procedure 5msec (STA perspective) per channel.
  Normal length of Probe Req transmission duration approx. 0.35msec.
  Example to cover the 2.4Ghz and 5Ghz bands if No Coverage scenario would take: Scan Total time = Number channels * Min duration per channel
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time

## Slide 6: Recap, Active Scanning Procedure
Active scanning procedure is defined in 10.1.4.3.3 and has the following properties:
  Minimum duration of procedure 5msec (STA perspective) per channel.
  Normal length of Probe Req transmission duration approx. 0.35msec.
  Example to cover the 2.4Ghz and 5Ghz bands if No Coverage scenario would take: Scan Total time = Number channels * Min duration per channel
Probe
Req
T
STA on ch. # 1
G3
T
T
Min_Probe_Response_Time
STA on ch. # 2
Probe
Req
G3
Min_Probe_Response_Time
Probe
Req
G3
STA on ch. # N
Min_Probe_Response_Time

## Slide 7: Recap, Active Scanning Procedure
How much does it adds up to? :
  Scan Total time = Number channels * Min duration per channel =
  = number channels * (Probe Req + Min_Probe_Response_Time)
  To cover the complete 2.4Ghz and 5Ghz non DFS/TPC bands in Korea would take a minimum of:
  = (11+25) * (0.05 + 0.35+5) = 194.4msec
  To cover the complete 2.4Ghz and 5Ghz bands in Japan would take a minimum of:
  = (11+12) * (0.05+0.35+5) = 124.2msec
Probe
Req
T
STA on ch. # 1
G3
T
T
Min_Probe_Response_Time
STA on ch. # 2
Probe
Req
G3
Min_Probe_Response_Time
Probe
Req
G3
STA on ch. # N
Min_Probe_Response_Time

## Slide 8: Recap, Active Scanning Procedure
How much does it adds up to? :
  Scan Total time = Number channels * Min duration per channel =
  = number channels * (Probe Req + Min_Probe_Response_Time)
  To cover the complete 2.4Ghz and 5Ghz bands in Korea would take a minimum of:
  = (11+25) * (0.05 + 0.35+5) = 194.4msec
  To cover the complete 2.4Ghz and 5Ghz bands in Japan would take a minimum of:
  = (11+12) * (0.05+0.35+5) = 124.2msec
Probe
Req
T
STA on ch. # 1
G3
T
T
Min_Probe_Response_Time
STA on ch. # 2
Probe
Req
G3
Min_Probe_Response_Time
Probe
Req
G3
STA on ch. # N
Min_Probe_Response_Time
Conclusion: Active Scan as is defined today is
not fast enough for the 11ai use case scenario.

## Slide 9: Problem Identified
The scan duration to identify AP coverage where most channels are unused adds up to a substantial delay:
  Use case reference document IEEE 802.11-11/0238 gives multiple scenarios where the complete link setup of <100msec is required with no prior knowledge:
    Scanning and performing Active Scan alone is simply not feasible.
    Neighbor messages transmitted during long interval either beacon or FILS beacon is not good enough on their own – delay too large.
  Use cases requiring complete setup time of 100msec or below:
    3.1.3 Hot-Spot Pass-Through Internet Access
    3.2.2 Traveller Information
    3.2.2 Multi-modal Real-Time Traveller Information
    3.2.2 Dynamic Speed Harmonization

## Slide 10: Problem Identified (con.)
Example of possible 24hr usage:
Night time
Early morning
Day time
Rush hour
Evening
Static
Low/No coverage
High/Low/No coverage
Rural and urban
Urban
High and low mobility
Static/low mobility
Urban
High coverage
High/low mobility
High/Low/No coverage
Low/No coverage
Urban
Static/Low mobility
24hr
Probability for long duration of cyclic Scan without response
Probability for long duration of cyclic Scan without response
Probability for long duration of cyclic Scan without response
Good Probability for long duration of cyclic Scan without Probe Rsp.

## Slide 11: Problem Identified (con.)
Conclusion:
  11ai use cases needs an inherent support for long durations of no/low coverage as well as provide support for efficient and fast discovery of AP coverage over a multiple channels and bands.

## Slide 12: Suggested Improvement
Divide the AP coverage discovery and AP identity discovery to two phases:
  STA attempts AP coverage discovery using a very fast AP discovery phase.
  STA attempts AP identity discovery if AP coverage found.
Enable a shorter listening duration by non AP STA for each channel by:
  Transmitting an APs discovery broadcast message in search for AP coverage.
  AP responds using an ACK after a period of an SIFS.
  STA detects the ACK or if more than one STA responds, detects channel usage using its CCA function. Process completes within 170usec.
  STA than able to perform Active or Passive scanning over the channel to discover the identity of the AP.

## Slide 13: Suggested Improvement
Probe
Response
Multiple APs respond after SIFS and identified by STA’s CCA
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
G1
G3
STA sends a Rapid Scan Request
MAC message
Rapid Scan Ack
Probe Response ACK
Time uncertainty < Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
AP coverage discovery
Existing Active Scan procedure – AP identity discovery
~230usec
~5-10msec

## Slide 14: Suggested Improvement – in case of no AP
No response identified STA goes to next channel within ~80usec
Rapid Scan
Request
T
STA performing
Rapid Scan
G1
MAC message
Time uncertainty <
Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
~230usec
Probe Req
STA performing
Rapid Scan
G3
Min_Probe_Response_Time
~5.350msec
STA waits 5msec for AP to response than switch to next channel

## Slide 15: Suggested Improvement – in case of only non 11ai capable APs
No response identified STA goes to next channel within ~80usec with minimal impact on medium
RSR
T
STA performing
Rapid Scan
G1
10usec
~230usec
G1
ACK
Probe
Req
T
STA performing
Rapid Scan
G3
T
T
Probe
Response
Probe
Response
G3
G1
ACK
Min_Probe_Response_Time
Max_Probe_Response_Time = ~10msec
STA takes up substantial medium resource.
Procedure takes 10msec to identify no 11ai support.

## Slide 16: Suggested Improvement – mix of 11ai and non 11ai APs
Probe
Response
Multiple APs respond after SIFS and identified by STA’s CCA
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
G1
G3
STA sends a Rapid Scan Request
MAC message
Rapid Scan Ack
Probe Response ACK
Time uncertainty < Min_Probe_Response_Time
G1 == SIFS
G3 == DIFS
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
Post AP coverage STA continues to perform active scanning
AP coverage discovery
Existing Active Scan procedure – AP identity discovery
~230usec
~10msec
~
~
~
~
~
~

## Slide 17: Performance comparisons
The Rapid Scan Request message:
  A new control message using existing headers.
Assumptions:
  Probe Request transmission duration: 350usec
  Rapid Scan Req transmission duration: 100usec.
  Min_Probe_Response_Time: 5msec.
  No AP coverage scenario.
  Number of non DFS/TPC channels to scan: 35 (Korea), 23 Japan
  Rapid Scan Total time = Number channels * Min duration per channel = (2.4Ghz ch. + 5Ghz ch.) * (Rapid Scan Req + SIFS + ACK duration)
  Korea = (11+25) * (50+50+70usec+10usec+ 70usec) = 9 msec
  Japan = (11+12) * (50+50+70usec+10usec+70usec) = 5.75 msec

## Slide 18: Key Performance Indicators
Comparing the proposed and existing methods in two aspects:
  Time to discover AP coverage within n non DFS/TPC channels.
  PWR invested in discovering AP coverage within n channels to directly derive polling rate.
Compared scenarios:
  IDLE channels – no AP coverage on STA geographical vicinity.
  Heavily dense deployment – AP coverage on every 1:4 channels for all bands.
These parameters sets the following limits to actual products:
  The discovery delay when user triggered action is performed.
  The discovery delay when automatic polling method is performed.
  Rate of the discovery attempts due to PWR limitations.

## Slide 19: KPI comparison – Scan Time Idle Channel
  Active Scan Total time w/o Rapid Scan = Number channels * (Probe Req + Min_Probe_Response_Time)
  Active Scan Total time w/ Rapid Scan = Number channels * (Rapid Scan Req + SIFS + ACK)
Chart: 
Active scan delay w/o Rapid [msec] | 5.4 | 10.8 | 16.2 | 21.6 | 27 | 32.4 | 37.8 | 43.2 | 48.6 | 54 | 59.4 | 64.8 | 70.2 | 75.6 | 81 | 86.4 | 91.8 | 97.2 | 102.6 | 108 | 113.4 | 118.8 | 124.2 | 129.6 | 135 | 140.4 | 145.8 | 151.2 | 156.6 | 162 | 167.4 | 172.8 | 178.2 | 183.6 | 189
Active scan delay w/ Rapid [msec] | 0.23067 | 0.46133 | 0.692 | 0.92267 | 1.1533 | 1.384 | 1.6147 | 1.8453 | 2.076 | 2.3067 | 2.5373 | 2.768 | 2.9987 | 3.2293 | 3.46 | 3.6907 | 3.9213 | 4.152 | 4.3827 | 4.6133 | 4.844 | 5.0747 | 5.3053 | 5.536 | 5.7667 | 5.9973 | 6.228 | 6.4587 | 6.6893 | 6.92 | 7.1507 | 7.3813 | 7.612 | 7.8427 | 8.0733
Note:
In this comparison, STA goes through a set of channels without AP coverage attempting to perform Active Scan or Rapid Scan.
Active Scan takes 5msec per channel while Rapid Scan completes within 250usec.

## Slide 20: KPI comparison – Scan Time Idle Channel
  Full scan Korea = 9msec full scan w/ Rapid Scan vs. 194.4msec w/o Rapid Scan.
  Full scan Japan = 5.75msec full scan w/ Rapid Scan vs. 124.2msec w/o Rapid Scan.
Chart: 
Active scan delay w/o Rapid [msec] | 5.4 | 10.8 | 16.2 | 21.6 | 27 | 32.4 | 37.8 | 43.2 | 48.6 | 54 | 59.4 | 64.8 | 70.2 | 75.6 | 81 | 86.4 | 91.8 | 97.2 | 102.6 | 108 | 113.4 | 118.8 | 124.2 | 129.6 | 135 | 140.4 | 145.8 | 151.2 | 156.6 | 162 | 167.4 | 172.8 | 178.2 | 183.6 | 189
Active scan delay w/ Rapid [msec] | 0.23067 | 0.46133 | 0.692 | 0.92267 | 1.1533 | 1.384 | 1.6147 | 1.8453 | 2.076 | 2.3067 | 2.5373 | 2.768 | 2.9987 | 3.2293 | 3.46 | 3.6907 | 3.9213 | 4.152 | 4.3827 | 4.6133 | 4.844 | 5.0747 | 5.3053 | 5.536 | 5.7667 | 5.9973 | 6.228 | 6.4587 | 6.6893 | 6.92 | 7.1507 | 7.3813 | 7.612 | 7.8427 | 8.0733
Note:
In this comparison, STA goes through a set of channels without AP coverage attempting to perform Active Scan or Rapid Scan.
Active Scan takes 5msec per channel while Rapid Scan completes within 250usec.

## Slide 21: KPI comparison – Scan PWR Idle Channel
  Active Scan PWR w/o Rapid Scan = Number channels * (Probe Req + Min_Probe_Response_Time)
  Active Scan PWR w/ Rapid Scan = Number channels * (Rapid Scan Req + SIFS + ACK)
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.3375 | 0.675 | 1.0125 | 1.35 | 1.6875 | 2.025 | 2.3625 | 2.7 | 3.0375 | 3.375 | 3.7125 | 4.05 | 4.3875 | 4.725 | 5.0625 | 5.4 | 5.7375 | 6.075 | 6.4125 | 6.75 | 7.0875 | 7.425 | 7.7625 | 8.1 | 8.4375 | 8.775 | 9.1125 | 9.45 | 9.7875 | 10.125 | 10.4625 | 10.8 | 11.1375 | 11.475 | 11.8125
Active Scan PWR w/ Rapid [mJ/scan] | 0.028534 | 0.057068 | 0.085601 | 0.11414 | 0.14267 | 0.1712 | 0.19974 | 0.22827 | 0.2568 | 0.28534 | 0.31387 | 0.34241 | 0.37094 | 0.39947 | 0.42801 | 0.45654 | 0.48508 | 0.51361 | 0.54214 | 0.57068 | 0.59921 | 0.62774 | 0.65628 | 0.68481 | 0.71335 | 0.74188 | 0.77041 | 0.79895 | 0.82748 | 0.85602 | 0.88455 | 0.91308 | 0.94162 | 0.97015 | 0.99868
Note:
Rapid Scan assumed 70usec
Probe Req 350usec (conservative)
Tx/Rx PWR ratio 1:5
Min_Probe_Response_Time, Max_Probe_Response_Time, DIFS, SFIS, probDelay, PLMP header and preamble, other…

## Slide 22: KPI comparison – Scan PWR Idle Channel
  Single full scan Korea = 1.14mJ/scan with Rapid Scan vs. 12.24mJ/full w/o Rapid Scan
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.34 | 0.68 | 1.02 | 1.36 | 1.7 | 2.04 | 2.38 | 2.72 | 3.06 | 3.4 | 3.74 | 4.08 | 4.42 | 4.76 | 5.1 | 5.44 | 5.78 | 6.12 | 6.46 | 6.8 | 7.14 | 7.48 | 7.82 | 8.16 | 8.5 | 8.84 | 9.18 | 9.52 | 9.86 | 10.2 | 10.54 | 10.88 | 11.22 | 11.56 | 11.9
Active Scan PWR w/ Rapid [mJ/scan] | 0.031533 | 0.063067 | 0.0946 | 0.12613 | 0.15767 | 0.1892 | 0.22073 | 0.25227 | 0.2838 | 0.31533 | 0.34687 | 0.3784 | 0.40993 | 0.44147 | 0.473 | 0.50453 | 0.53607 | 0.5676 | 0.59913 | 0.63067 | 0.6622 | 0.69373 | 0.72527 | 0.7568 | 0.78833 | 0.81987 | 0.8514 | 0.88293 | 0.91447 | 0.946 | 0.97753 | 1.0091 | 1.0406 | 1.0721 | 1.1037
Note:
Rapid Scan assumed 100usec
Probe Req 350usec (conservative)
Tx/Rx PWR ratio 1:5
Min_Probe_Response_Time, Max_Probe_Response_Time, DIFS, SFIS, probDelay, PLMP header and preamble, other…

## Slide 23: KPI comparison – dense deployment delay
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.34 | 0.68 | 1.02 | 1.61 | 1.95 | 2.29 | 2.63 | 3.22 | 3.56 | 3.9 | 4.24 | 4.83 | 5.17 | 5.51 | 5.85 | 6.44 | 6.78 | 7.12 | 7.46 | 8.05 | 8.39 | 8.73 | 9.07 | 9.66 | 10 | 10.34 | 10.68 | 11.27 | 11.61 | 11.95 | 12.29 | 12.88 | 13.22 | 13.56 | 13.9
Active Scan PWR w/ Rapid [mJ/scan] | 0.031533 | 0.063067 | 0.0946 | 0.68463 | 0.71616 | 0.7477 | 0.77923 | 1.3693 | 1.4008 | 1.4323 | 1.4639 | 2.0539 | 2.0854 | 2.117 | 2.1485 | 2.7385 | 2.7701 | 2.8016 | 2.8331 | 3.4232 | 3.4547 | 3.4862 | 3.5178 | 4.1078 | 4.1393 | 4.1709 | 4.2024 | 4.7924 | 4.824 | 4.8555 | 4.887 | 5.4771 | 5.5086 | 5.5401 | 5.5717
Notes: Apples to Apples
In this comparison, if an 11ai capable AP was discovered by Rapid Req, a 2nd stage of identifying AP identity using Active Scan is accounted for

## Slide 24: KPI comparison – dense deployment PWR
  Full scan Korea = 6.16mJ/Scan full Scan w/ Rapid vs. 14.49mJ/Scan w/o Rapid APs deployed at every 1 out of 4 channels
Chart: 
Active Scan PWR w/o Rapid [mJ/scan] | 0.34 | 0.68 | 1.02 | 1.61 | 1.95 | 2.29 | 2.63 | 3.22 | 3.56 | 3.9 | 4.24 | 4.83 | 5.17 | 5.51 | 5.85 | 6.44 | 6.78 | 7.12 | 7.46 | 8.05 | 8.39 | 8.73 | 9.07 | 9.66 | 10 | 10.34 | 10.68 | 11.27 | 11.61 | 11.95 | 12.29 | 12.88 | 13.22 | 13.56 | 13.9
Active Scan PWR w/ Rapid [mJ/scan] | 0.031533 | 0.063067 | 0.0946 | 0.68463 | 0.71616 | 0.7477 | 0.77923 | 1.3693 | 1.4008 | 1.4323 | 1.4639 | 2.0539 | 2.0854 | 2.117 | 2.1485 | 2.7385 | 2.7701 | 2.8016 | 2.8331 | 3.4232 | 3.4547 | 3.4862 | 3.5178 | 4.1078 | 4.1393 | 4.1709 | 4.2024 | 4.7924 | 4.824 | 4.8555 | 4.887 | 5.4771 | 5.5086 | 5.5401 | 5.5717
Note:
In this comparison, if an AP was discovered by Rapid Req, a 2nd stage of identifying AP identity using Active Scan is accounted for

## Slide 25: Comparison
Advantages:
  Shorter procedure yields substantial shorter delay.
  Separates the 11ai and non 11ai APs enables to focus on the important channels.
  Purpose built AP coverage message is shorter duration and enables higher polling rate without hindering the mobile device power consumption.
  Fully backwards compatible - a combination of legacy and 11ai APs, both APs gain shorter discovery.
  Reduces WM usage on a non 11ai deployments by transmitting shorter message with shorter still reply.
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
Probe
Response
G1
G3
AP coverage discovery
Existing Active Scan procedure – AP identity discovery

## Slide 26: Comparison
Disadvantages:
  Additional procedure adds ~180usec if channel is already pre-known (procedure can be skipped).
Rapid Scan
Request
Probe
Request
T
STA performing
Rapid Scan
Responder
# 1
Responder
# 2
G1
T
T
Probe
Response
G1
G3
AP coverage discovery
Existing Active Scan procedure – AP identity discovery

## Slide 27: Backup

## Slide 28: Motion
Insert the following text on clause 6 of the SFD (11-12/0151r12):
The amendment will define a mechanism to reduces the FILS capable AP coverage discovery duration using a newly or existing message. The procedure will enable the STA to identify FILS capable AP coverage within SIFS plus ACK message delay post request by STA by using decoding an ACK message or using CCA in case of a collision.
Yes:
No:
Abstain: