## Slide 1: Enhanced scanning procedure for FILS
Date: 2012-09-17
Authors:

## Slide 2: Abstract
This proposes to reduce the frame length of probe response frame during active scanning procedure to preferred AP

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4: Background
Active scanning procedure
  Probe request/response exchanges for finding the AP/network[1]
  Legacy probe response frame includes all system information elements supported by AP
    Size of probe response frame is similar to beacon frame except TIM IE (e.g., more than 230 bytes [2])
  A STA may send the unicast probe request for scanning the preferred AP (BSSID of the AP is included in MAC header )
  In case of actively scanning the preferred/target AP, if the STA stores the system information of the AP which the STA was previously associated with, the AP does not need to send the probe response including full system information elements
AP configuration change count[3] [4]
  May be included in the FILS Discovery frame
  Indicates the change of system parameters of AP/BSS

## Slide 5: Proposal (1/2)
For fast initial link setup, the 802.11ai STA will store the system information elements of some preferred APs which the STA was associated with
  To reduce the information to store, the STA may restrict the number of preferred APs which system parameters are stored by the STA
Whenever the AP changes the system parameters, the AP will store the old configuration change count and the changed system information element ID (1byte) for the change count
  E.g.,) In case of the current configuration change count = ‘3’, the stored information by AP. [change count = 0, ID = ‘x’], [change count = 1, ID = ‘y’], [change count = 2, ID = ‘Z’]
  If one parameter is changed in one change count and the change count size is 8 bits, the maximum size of the stored information is 512 bytes

## Slide 6: Proposal (2/2)
During the active scanning procedure to a preferred AP, if the STA has system parameters of the AP, a STA may include the configuration change count of target AP in the probe request frame
When an AP receives the probe request frame including the configuration change count, the AP may send to the STA the optimized probe response frame including only the system information elements which need to be received by the STA based on the received configuration change count

## Slide 7: Analysis (1/2)
Size of Probe response frame is similar to size of beacon frame except for TIM IE
  The size of beacon frame/probe response[2]
    > 100 byte(typical 802.11 BSS), > 230 bytes (enterprise environment)
    Mandatory fields: Timestamp (8bytes(B)), Beacon Interval (2B), Capability (2B)
The following system information elements can be changed in legacy system [1]
  Channel Switch Announcement (5B)
  Extended Channel Switch Announcement (6B)
  EDCA parameters (20B)
  Quiet element (8B)
  DSSS Parameter Set (3B)
  CF Parameter Set (8B)
  FH Parameter Set (7B)
  HT Operation element (24B)

## Slide 8: Analysis (2/2)
Comparison between legacy probe response size and optimized probe response
  Size of mandatory fields: 12 bytes
  Best case: > 83% (typical BSS), > 92% (enterprise environment)
  Worst case: > 64% (typical BSS), > 84% (enterprise environment)
Most of optimized probe response frames will contain only mandatory fields because the BSS system elements hardly change.
Updated IE | Legacy probe response (>100B) |  | Legacy probe response (>230B) | 
 | Optimized Probe Response | Gain (%) | Optimized Probe Response | Gain (%)
No change | 12 B | > 88% | 12B | > 94.79
Channel Switch Announcement (5B) | 17 B | > 83% | 17 B | > 92 %
Quiet element (8B) | 20 B | > 80% | 20 B | > 91%
EDCA parameters (20B) | 32 B | > 68% | 32 B | > 86%
HT Operation element (24B) | 36 B | > 64% | 36 B | > 84%

## Slide 9: Conclusion
During active scanning procedure to a preferred AP, sending the probe response frame including full system parameters can be unnecessary resource overhead and the delay of initial link setup may be increased
In this case if a STA sends preferred AP the probe request including AP Configuration Change Count, the AP can send the optimized probe response frame based on the change count

## Slide 10: References
[1] IEEE Std 802.11™-2012
[2] IEEE 802.11-11/1503r2, Short beacon
[3] IEEE 802.11-12/0741r1, Discussions about 802.11ai FILS Discovery Frame (DF) Content Design
[4] IEEE 802.11-12/0151r12, Specification Framework for TGai

## Slide 11: Straw Poll 1
Do you support that STA may send the probe request frame including the configuration change count of a preferred AP if the STA has the system information elements of the preferred AP during the active scanning procedure to preferred AP?
  Y:
  N:
  Abstain:

## Slide 12: Straw Poll 2
Do you support that AP may send the optimized probe response frame including only the system parameters which need to be received by the STA when the AP receives the probe request frame including the configuration change count?
  Y:
  N:
  Abstain:

## Slide 13: Motion 1
Move to add the following text to “Section 6.2 Active scanning” in the TGai SFD, 12/0151r12:
“6.2.12 Active scanning to preferred AP
STA may send the probe request frame including the configuration change count of a preferred AP if the STA has the system information elements of the preferred AP during the active scanning procedure to preferred AP.”
Mover:
Seconder:
Result Yes No Abstain___________

## Slide 14: Motion 2
Move to add the following text to “Section 6.2 Active scanning” in the TGai SFD, 12/0151r12:
“6.2.12 Active scanning to preferred AP
AP may send the optimized probe response frame including only the system parameters which need to be received by the STA when the AP receives the probe request frame including the configuration change count.”
Mover:
Seconder:
Result Yes No Abstain___________

## Slide 15: Appendix (Issues)
How many Element IDs & AP configuration change count should the AP store?
  May store the information for all AP configuration change counts. If the size of the change count is 8 bits and one parameter is only changed each count, need 512 bytes to store all information
  To reduce amount of stored information, AP may restrict the cached information according to number of change count (e.g., only 32 or 64 change counts) or a specific duration (e.g., days, months, years, etc.)
How does the AP do if the AP receives the unclear change count from STA?
  AP may send the legacy probe response including full system information
AP configuration change count is different from GAS change count
  GAS change count indicates the change of GAS parameter set