## Slide 1: Multi-Access Link Model
Date: 2012-09-17
Authors:
Name | Address | Affiliations | Phone | Email
Donald Eastlake | Huawei Technologies | 155 Beaver Street, Milford, MA 01757 USA | +1-508-333-2270 | d3e3e3@gmail.com

## Slide 2: Abstract
This presentation discusses the modeling of an AP with associated stations as a multi-access shared link that can be used as a transit link inside networks.

## Slide 3: Multi-Access Link Model for GLK
This presentation just talks about the case people are most interested in: An AP with associated STAs.
Radio “links” are inherently multi-access. You broadcast and, in general, multiple stations can receive.
Network connectivity in such cases is currently provided by pretty much just saying that the AP can have one portal.
  Clearly there are mechanisms required to get this to work well – particularly in the case of an ESS – which are mostly left out of scope

## Slide 4: Usual Diagram of an AP with two STAs
STA1
STA2
Portal
AP

## Slide 5: But Radio Links are Inherently Multi-Access
AP
STA1
STA2
Portal

## Slide 6: Multi-Access Link Model for GLK
So – why not just say that STAs can have a portal?
AP
STA1
STA2
Portal
Portal
Portal

## Slide 7: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Loop prevention
    Not always a problem, for example when the STA portal leads to an IP router.
    When it is a potential problem, just put a loop preventing device such as an 802.1 bridge at the end of the portal.
    (If bridges added to all portals, previous example look like this:
STA1
Bridge1
Bridge2
STA2
Bridge3
AP

## Slide 8: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Actual link costs are poorly reflected to the outside so routing may be pretty far from least cost.
    At least for IS-IS and some other protocols that understand multi-access links, a pseudo-node is created to model the link which permits much better reflection of costs:
STA1
Bridge1
Bridge2
STA2
Bridge3
AP
Pseudo Node

## Slide 9: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  Some protocols are inefficient on multi-access links or don’t support them at all.
    Fix them

## Slide 10: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  How does the STA decide whether to send frames over the air or over the portal or both?
    For the single AP with single portal case, it is easy. STAs just send to the AP. The AP knows the MAC addresses of the associated STAs, so unicast is send to the right station or sent out the portal. And multi-destination frames are sent to both.
    Add a portal to the STA makes all this much more complex.
      The AP may have to send a frame to a STA so the STA can send it out the STA’s portal.
      A STA does not always just send to the AP. It may need to send out its STA.
      No simple rule is possible at the STA. Some form of address table appears necessary

## Slide 11: Multi-Access Link Model for GLK
Potential Problems with “just add a portal to STAs”
  How does the STA decide whether to send frames over the air or over the portal or both? (continued)
    No simple rule is possible at the STA. Some form of address table appears necessary