## Slide 1: Ad Hoc Discussions of 802.11ai Passive Scanning during 2012-September Meeting
Date: 2012-09
Authors:

## Slide 2: Abstract
This document is intended to keep tracking of the ad hoc discussions about 802.11ai passive scanning during 2012-September Indian Wells meeting.

## Slide 3
Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | ??
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,2

## Slide 4
Background
11ai Passive Scanning Work Status :
  High-level descriptions have been accepted in TGai SFD,12/0151r12, during/before 2012-July meeting;
  Initial text has been accepted in TGai draft specification document in Monday AM-2 meeting in 2012-September meeting;
  There are still some open issues, e.g., FD frame format, detailed contents, etc.
Passive Scanning related Submissions to TGai for 2012-September meeting
  11-12-1028-03-00ai-spec-text-for-passive-scanning
  11-12-1029-01-00ai-further-discussion-about-fils-discovery-frame-format
  11-12-1030-00-00ai-detailed-design-for-fils-discovery-frame-contents
  11-12-1054-00-00ai-fils-reduced-neighbor-report
  11-12-1098-00-00ai-fils-reduced-neigbhor-report-normative-text

## Slide 5
Overview of Passive Scanning Ad Hoc Discussion
Ad Hoc Discussion Items and Order:
    Monday-Evening
  FD frame format (12/1029)
  Reduced Neighbor Report (12/1054 and 12/1098)
    Wednesday-PM1
  FD frame processing (what was taken out from the motion in 12/1028r3 during Monday AM-2)
  FD frame detailed contents (12/1030)

## Slide 6
Ad Hoc Discussions – Monday Evening
Presentation and discussions on 12/1029r1
  Three Straw-Polls were made, see details in Slide 7, 8, and 9;
  Updated version: 12/1029r2;
Presentation and discussions on 12/1054r1 and 12/1098r1
  One Straw-Poll was made, details in Slide 10,

## Slide 7
Ad Hoc Discussions – Monday Evening (con’t)
Straw-Poll-1 in 12/1029r2:
Which of the following options do you prefer to being the starting point of the FILS Discovery frame format design?
a) 11ah short beacon
b) a new Extension frame with Type =0b11
c) neither, need more info
Result a) 3 b) 6 c)________10_______

## Slide 8
Ad Hoc Discussions – Monday Evening (con’t)
Straw-Poll-2 in 12/1029r2:
Do you agree that the FILS Discovery frame format design should not consider the option of modifying the Measurement Pilot frame, due to the big differences in the content items?
Result Yes 11 No 0 Abstain_______3___

## Slide 9
Ad Hoc Discussions – Monday Evening (con’t)
Straw-Poll-3 in 12/1029r2:
Do you think that the MAC header overhead reduction should be considered in the FILS Discovery frame format design?
Result Yes 8 No 0 Abstain____9______

## Slide 10
Ad Hoc Discussions – Monday Evening (con’t)
Straw-Poll in 12/1054r1:
Do you support to authorize the Editor to incorporate the text changes proposed in contribution 11-12-1098-01-00ai-fils-reduced-neigbhor-report-normative-text to draft Tgai Draft Specification document (D0.0)?
Regulatory
1.5 Tus
Physically collocated
Result Yes 3 No 0 Abstain:___Majority__

## Slide 11
Scanning Ad Hoc
Wednesday PM-1

## Slide 12
Discussion Items
A quick update about FD frame format design
Discussion of FD frame detailed content design, based on
  12/1030
  12/1054 and 12/1098
Discussion of FD processing, based on
  the text that was taken out from the motion in 12/1028r3 during Monday AM-2

## Slide 13
Update about FD Frame Format Design
Further discussion in TGai Tuesday PM-1
  12/1148
Conducted Straw-poll-1 on slide 7 in TGai:
  Result: a (5); b(16); c(14)
Indication from the straw-polls:
  Design FD frame as a new Extension frame
   Further discussions are needed about FD frame format design!!

## Slide 14
Discussion of FD Frame Detailed Content Design
  Presented contribution 12/1030
  discussed the detailed design of FD frame content items
    Use the FD control field:
      Presence indicators of the optional content items;
      Control info, e.g., length, etc., for variable-size content items
    SSID:
      full SSID, variable-size;
      Anticipate further contributions about “condensed” SSID.
    AP Configuration Change Count:
      1-byte, integer number
      Associated with an AP (BSSID)
    Access Network Options:
      1-byte, as defined in Figure 8-352 in 802.11-2012.
    AP’s next TBTT: 1-byte,
      offset value from the FD frame Tx time to next TBTT.

## Slide 15
Discussion of FD Frame Detailed Content Design – con’t
  discussed the detailed design of FD frame content items
    Neighbor AP’s next TBTT info:
      Not to limit the number of neighbor channels to be included;
      Allow multiple “next TBTT” items for one neighbor channel;
      Need further work based on the options below:
        Modified the proposal in 12/1030 to reflect the above two points;
        Reduced Neighbor Report IE (12/1054 and 12/1098)
        Mixed of the above two options.
    Capability: need further discussions;
    Security: need further discussion with TGai Security people, i.e., they are not in another parallel Security Ad hoc session.

## Slide 16
Discussion of FD Frame Processing
  Discussed the text in 12/1028r2, Section 3.1.2, starting from “During scanning ….”
  Revised the text, as shown in contribution 12/1168, with a motion to be presented in TGai meeting.

## Slide 17
Discussion of Next-Step Work
  Prepare the proposal of text for TGai draft specification document about FD frame contents based on the discussions in this meeting;
    discuss it in TGai CC(s) between September and November meetings, and/or in emails;
    Submit it to TGai November meeting.
  Continue the work/discussions about the two remaining content items: Capability and Security.

## Slide 18
References:
IEEE Std 802.11™-2012
11-12-0151-12-00ai-proposed-specification-framework-for-tgai
11-12-1028-02-00ai-spec-text-for-passive-scanning
11-12-1028-03-00ai-spec-text-for-passive-scanning
11-12-1029-01-00ai-further-discussion-about-fils-discovery-frame-format
11-12-1030-00-00ai-detailed-design-for-fils-discovery-frame-contents
11-12-1054-00-00ai-fils-reduced-neighbor-report
11-12-1098-00-00ai-fils-reduced-neigbhor-report-normative-text